Pre SA2#143E e-meeting Email Discussion

Source: 	<Jinguo Zhu/ZTE>

Title: 	<Email discussion on FS_eNS_Ph2>

# 1.	Issues for FS_eNS_Ph2

## 1.1	Key Issue #3: limitation of data rate per network slice in UL and DL per UE

### 1.1.1	Issue Description

For key issue 3 we have categorized the solutions into 3 categories

-	Category A1: Those enforcing the Slice-MBR in the UPF, in CN i.e. solution #13.

-	Category A2: Enforcing SMBR in the RAN and also admitting GFBR aggregate for the slice only up to the SMBR at the admission control time in the RAN, i.e. solution #22,

-	Category B: Those ensuring that the Slice-MBR limits the aggregated MBR and GBR for QoS flows of established PDU sessions and related QoS flows, i.e. solution #20, #21 and #37. Enforcement is done using the existing QoS parameter

### 1.1.2	Companies View

Question 1) Whether UPF based solution (Category A1) should be supported for KI#3。

| Company Name | Company View (Yes/No) | Notes(Justifications) |
| --- | --- | --- |

Question 2) Whether RAN based solution (Category A2) should be supported for KI#3:

| Company Name | Company View (Yes/No) | Notes(Justifications) |
| --- | --- | --- |

Question 3) Whether PCF based solution (Category B) should be supported for KI#3:

| Company Name | Company View (Yes/No) / (Option A/Option B) | Notes(Justifications) |
| --- | --- | --- |

### 1.1.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.1.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.2	Key Issue #5: Dynamic adjustment to meet the limitation of data rate per network slice in UL and DL

### 1.2.1	Issue Description

For key issue 5 we have categorized the solutions into 3 categories

-	Category A with enforcement of Slice max bit rate for each UE in RAN (#14,#25).

-	Category B with enforcement of Slice max bit rate in control plan function to control that the accumulate bit rate for all PDU sessions within the Slice do not exceed the Slice max bit rate.(#12,#18, #19, #20, #24).

-	Category C with enforcement of slice max bit rate in the user plane by distributing a quota to UPF for enforcement.(#16).

### 1.2.2	Companies View

Question 1) Whether RAN based solution (Category A) should be supported for KI#5:

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |

Question 2) Whether PCF based solution (Category B) should be supported for KI#5:

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |

Question 3) Whether UPF based solution (Category C) should be supported for KI#5:

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |

### 1.2.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.2.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.3	Key Issue #6: Constraints on simultaneous use of the network slice

### 1.3.1	Issue Description

For this key issue several solutions(#26,#28,#39) propose that UE is provided with a new rejection cause value of the S-NSSAI, to indicate that it is mutually exclusive to one or more of the S-NSSAIs in the Allowed NSSAI.

Serveral solutions(#27,#28, #41,#42) proposes that the UE is provided with network slice incompatible information per slice so the UE can efficiently use them to determine the Requested NSSAI. The network slice incompatible information per slice is provided together with Configured NSSAI or together with the Allowed NSSAI

Solution#40 proposes that the UE is provided with network slice incomptible information per SUPI/GPSI.

Some solutions proposes that the slice incompatible information is determined based on SLA, or on UE subscription. There is need to decide  how this slice incompatible information is determined.

### 1.3.2	Companies View

Question 1) In addition to the current Rel-15/16 support in the network,whether the UE should additionally be provided with a rejection cause value of the S-NSSAI, to indicate that it is mutually exclusive to the Allowed NSSAI?

| Company Name | Company View (Yes/No) | Notes(Justifications) |
| --- | --- | --- |
| Convida Wireless | Yes | This is needed so that the UE can decide which of the mutually exclusive slices to access and so that the UE knows that the slice is not rejected for some other reason (e.g. the slice is not supported). |

Question 2) In addition to the current Rel-15/16 support in the network, whether the UE should be additionally provided with network slice incompatible information so the UE can efficiently use them to determine the Requested NSSAI. If the answer is YES, please indicate how it is done

| Company Name | Company View (Yes/No) | Notes(Justifications) If the answer is YES, please provide whether the network slice incompatible information is provided together with the Configured NSSAI, or together with the Allowed NSSAI, or per SUPI/GPSI |
| --- | --- | --- |
| Convida Wireless | Yes | With the configured NSSAI |

Question 3): How do the home and serving networks determine the network slice incomptible information, Option A) based on SLA; Option B) based on UE subscription; C) based on both SLA and UE subscription

| Company Name | Company View (Option A/Option B/Option C) | Notes(Justifications) |
| --- | --- | --- |
| Convida Wireless | Option B |  |

### 1.3.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.3.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.4	Key Issue #7: Support of 5GC assisted cell selection to access network slice

### 1.4.1	Issue Description

For this key issue several UE based solutions(#29,#30) propose that UE is provided with frequency band information per network slice in the Configured NSSAI so the UE can efficiently select proper cell before access the network.

For network based solutions, sol#44 has been supported in Rel-16 and has no impact on the system. But whether it is sufficient for KI#7 depends on RAN WG feedback.

For other network based solution, Sol#17 and Sol#46 propose to steer the UE to prefered frequency band during the Registration procedure, and Sol#31 proposes to steer the UE to prefered frequency band UE during the PDU Session procedure. Sol#45 propose to generate Allowed NSSAI by considering the UE radio capability.

### 1.4.2	Companies View

Question 1) Whether the UE based solutions should be supported for KI#7:

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |
| Convida Wireless | Yes | If the UE is not aware of what bands can be used with its configured slices, then situations will arise where the UE requests slices that cannot operate in the same band and the Network will need to pick what service the UE gets. We do not think that the network is always able to know what service is most important to the user. Solution 29 is preferred because solution 30 requires DC and allows the UE to register to slices that are not simultaneously accessible. |

Question 2) Whether the network based solution(#17, #31,#45,#46) should be supported for KI#7

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |
| Convida Wireless | Yes, but network based solutions do not completely address KI#7. | The network-based solutions are useful for legacy UEs and to allow the network to steer the UE. |

### 1.4.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.4.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.