## Slide 1: SA2#143E CC1 disabling and Enabling N1 mode AI 6.9
Laurent.Thiebaut@nokia.com
2021.02.24

## Slide 2: Introduction / background
R16 maintenance topic/ LS on interworking to 5GS with N26 due to UE’s N1 mode capability disabling/enabling: C1-207531/S2-2100037
The UE operating in single-registration mode has disabled its N1 mode capability when registered in 5G and then moves to 4G of the current PLMN with N26 interface supported.
The UE initiates an EPS attach or TAU procedure in 4G during which the UE will indicate N1 mode is not supported.
Hereafter, the UE requests to establish a new PDN connection in 4G during which the UE will not generate the PDU session ID included in the (e)PCO IE to the network and the network will not include the mapped PDU session parameters (e.g. QoS flow descriptions, Session-AMBR, QoS rules) included in the (e)PCO IE to the UE.
The UE re-enables its N1 mode capability in 4G and then moves back to 5G.
As in step (3), there is no mapped PDU session parameters included in the PDN connection, this PDN connection cannot be transferred to 5G in step (4).
If in above step (3), a combo PGW-C+SMF was selected for the PDN connection, whether and how to maintain the session continuity for this PDN connection when moving back to 5G?
If in above step (3), a standalone PGW was selected for the PDN connection, whether and how to maintain the session continuity for this PDN connection when moving back to 5G?

## Slide 3: 5 different Proposals !!
SA2 is not sure what is the background and would like to ask for clarification on the use case that triggers the UE to disable the N1 mode capability when UE is registered in 5GS, and later triggers the UE to re-enable N1 mode capability when the UE is attached to EPS. S2-2100325
At EPS to 5GS mobility (S2-2100100 , S2-2100101)
    the UE considers as released the PDN connections that were established over EPS while N1 mode capability was disabled,
    The MME does not transfer to 5GS a PDN connection that was established over EPC while N1 mode capability was disabled on the UE.
During PDN connection establishment in the EPC, the UE allocates the PDU Session ID and sends it to the SMF+PGW-C via PCO, regardless of whether N1 mode is enabled or disabled in the UE EPS S2-2100905, S2-2100902,
  session continuity cannot be supported in case a stand-alone GW was selected for the PDN connection
The session continuity for the PDN connection needs to be maintained, when a combo PGW-C+SMF was selected : The UE generates a PDU Session ID for the PDN connection and includes it in the PCO, in order to request the mapped 5G QoS parameters for the respective EPS bearer(s) of this PDN connection. (S2-2100130, S2-2100131)
For the case that a UE in EPS changes UE Core Network Capability to (re)enable 5G NAS support, a UE or the network may release and re-establish PDN connection(s) to update 5G session parameters for interworking, after completion of TAU due to UE capability change (S2-2100920)

## Slide 4: And so what?
At this CC1 decide whether we liaise back (ask for clarification) or whether we try to define a technical solution
Unlikely that we can technically decide at CC1 (first time we discuss the topic)
Have a short discussion (not more than 5 min) as we hardly can decide at CC1; but useful to exchange arguments instead of sending 10s of mails
Proposal take following Tdoc for support of the technical discussion (this is NOT an endorsement of their technical content and possibly it may be discussed some are not needed)
S2-2100130 for the LS out
S2-2100920 for the 23.501 CR
S2-2100101 for the 23.502 CR

## Slide 5: THANK YOU