## Slide 1
SA2#144E CC1:
SRVCC Issue
Source: Ericsson

## Slide 2
Background
Two issues raised in RAN3 LS (E-RABs that cannot be handed over to 2G/3G or 5G):
  Issue#1 Specific to (4G)SRVCC
    Delay or even failure of SRVCC with PS+CS HO if Transaction Identifier (TI) is not available (e.g., due to UE being in 5GS previously)
  Issue#2 General PS HO issues
    EUTRAN to GERAN/UTRAN PS HO failure due to UE in 5G previously,
    EUTRAN to NG-RAN HO failure due to UE previously in GERAN/UTRAN
    ===Text from RAN3 LS S2-2102093 ===
    “RAN3 has discussed the below issue: when perform SRVCC from 4G to 3G, if the UE was earlier handed over from 5G and having the PS bearer (no voice) from 5G, eNB would perform SRVCC with two Iu connections (Iu-CS and Iu-PS) and informs the target RNC. But the Forward Relocation Request message may never be sent to the target node due to the QoS flow established in 5G does not contain Transaction Identifier (TI) and this TI is mandatory in the Forward Relocation Request message. This causes the SRVCC delay and in the worst case could even cause failure
    The issue is general, with the introduction of NR, the PS bearers set up at 5G may not be able to handover to 2G/3G or vice versa, e.g.: 5G without TI cannot be handed over to 2/3G. Similarly, some E-RABs from 2G/3G cannot be handed over to 5G. The mobility procedure may be delayed and in the worst case could fail”

## Slide 3
Input documents
 | ZTE | Nokia | Cisco | Ericsson
Discussion | S2-2102775 |  |  | S2-2102311
Tdoc Set1 to address Issue#1 | 23.216: S2-2102776 | 23.502: S2-2102763 Rel-17 mirror in S2-2102930 | 23.216: S2-2102952 | 23.216: S2-2102279
 | Proposal: Turn off 4G->2G/3G PSHO for SRVCC procedure Configuration, no impact on product. Turning off PS HO may not be accepted by some market | Proposal: MME does not provide PDP Context in Forward Relocation Request if no TI MME impact | Proposal: MME does not provide PDP Context in Forward Relocation Request if no TI MME impact | Proposal: If TI is not available, MME assign TI and provide PDP Context in Forward Relocation Request MME impact
Tdoc Set2 to address both Issue#1 & Issue#2 | 23.502: S2-2102777 Rel-17 mirror in S2-2102778 |  |  | 23.502:S2-2102280 Rel-17 mirror in S2-2102281
 | Proposal: MME provide new indication to eNB to control EUTRAN to GERAN/UTRAN HO. Requires upgrade of eNB and MME. |  |  | Proposal: In addition to ZTE proposal, MME also provides indication to control EUTRAN to NG-RAN HO Requires upgrade of eNB and MME.
LS out |  | S2-2102751 |  | S2-2102278

## Slide 4
Discussion
Question: Is Tdoc set 2 (addressing general PS HO issue) sufficient? Or both Tdoc set 1 (addressing SRVCC) and Tdoc set 2 are needed?
  If only set 2 is needed, the following is proposed:
    For general PS HO issue, take 23.502:S2-2102280 (Ericsson) as baseline
    For LS out, take S2-2102751 (Nokia) as baseline
  If both set 1 and set 2 are needed, the following is proposed:
    For SRVCC specific issue, take 23.216 S2-2102776 (ZTE) as baseline
    For general PS HO issue, take 23.502:S2-2102280 (Ericsson) as baseline
    For LS out, take S2-2102751 (Nokia) as baseline
  Ericsson recommends to go for both sets, as set 1 can avoid eNB upgrade.

## Slide 5
Thank You!