## Slide 1: SA2#145e CC#3 eNPN input
20210524

## Slide 2: UE capabilities for additional parameters using UPU
CT1 options:
  Alternative-1: in the UPU transparent container carrying the UPU acknowledgement; or
  Alternative-2: in the registration request message during the registration procedure.
S2-2104336 stating
  SA2 preference is to minimize the impacts on AMF as to easier enable the use of extended UPU also in roaming scenarios.
  SA2 will align the SA2 specifications with the CT1 and SA3 specifications, if needed.
S2-2104584 stating
  SA2 decided that Alternative-1 is the most appropriate. SA2 suggests CT1 to take the lead and standardize this option and SA2 will later align accordingly
S2-2104602 stating
  SA2 decided to include Alternative-2 allowing the UE to inform the network about which parameter(s) are supported in the UPU procedure prior to initiating the UPU procedure.
Questions
  Do you support:
    Alternative-1?
    Alternative-2?
 | S2-2103760 | LS In | Action | LS from CT WG1: Reply LS on UE capabilities indication in UPU | CT WG1 (C1-212599)
 | S2-2104336 | LS OUT | Approval | [DRAFT] Reply LS on UE capabilities indication in UPU | Ericsson
 | S2-2104584 | LS OUT | Approval | [DRAFT] Reply LS on UE capabilities indication in UPU | Qualcomm
 | S2-2104602 | LS OUT | Approval | [DRAFT] Reply LS on UE capabilities indication in UPU | MediaTek Inc.
 | S2-2104603 | CR | Approval | 23.501 CR2949 (Rel-17, 'B'): The supported parameters set type indication for UPU | MediaTek Inc.

## Slide 3: KI#1: Interface between AAA-S and SNPN
Only submitted option is using NSSAAF as interworking between SBI and AAA protocols:
Discussion on way forward
  Option 1:
    NSSAAF is renamed to Network System Specific Authentication and Authorization Function which supports the following separate and independent functionality:
      NSSAA for network slice.
      AIW for SNPN.
  Option 2:
    Define a new NF for SNPNs e.g. AIWF
Questions:
  Do you support to progress option 1?
    Yes
    No
  Do you support to progress option 2?
    Yes
    No
S2-2104442 | CR | 23.501 CR2926 (Rel-17, 'C'): Interaction between AUSF and AAA Server | CATT, Ericsson, Huawei, Nokia, Nokia Shanghai Bell
S2-2104443 | CR | 23.502 CR2820 (Rel-17, 'C'): Add a new NSSAAF service to support interaction between AUSF and AAA Server | CATT, Ericsson, Huawei, Nokia, Nokia Shanghai Bell

## Slide 4: Updating CH controlled lists for SNPN selection
CT1 indicated preference for UPU over SoR, SA3 has not yet replied
CRs from Huawei, Ericsson and MediaTek propose to use UPU, but CR from Xiaomi propose to use SoR
Discussions:
  Questions:
    Do you support to use UPU for updating CH controlled lists for SNPN selection?
      Yes
      No
    Do you support to use SoR for updating CH controlled lists for SNPN selection?
      Yes
      No
S2-2103747 | LS In | Reply LS on updating the Credentials Holder controlled lists for SNPN selection | CT WG1 (C1-212419)
S2-2104176 | CR | 23.501 CR2754R1 (Rel-17, 'F'): Update of CH controlled prioritized list of preferred SNPNs and GINs | Huawei, HiSilicon
S2-2104215 | CR | 23.502 CR2789 (Rel-17, 'F'): Update of prioritized list of preferred SNPNs and Group IDs to the UE | Huawei, HiSilicon
S2-2104352 | DISCUSSION | Discussion for updating the preferred list. | Xiaomi
S2-2104353 | CR | 23.502 CR2717R1 (Rel-17, 'B'): Support for update of Credentials Holder controlled prioritized list of preferred SNPNs | Xiaomi
S2-2104356 | CR | 23.501 CR2839R1 (Rel-17, 'B'): Support for update of Credentials Holder controlled prioritized list of preferred SNPNs | Xiaomi
S2-2104338 | CR | 23.502 CR2801 (Rel-17, 'B'): Additional parameters using UE Parameters Update via UDM Control Plane Procedure | Ericsson
S2-2104606 | CR | 23.501 CR2951 (Rel-17, 'B'): Updating the Credentials Holder controlled lists for SNPN selection | MediaTek Inc.
S2-2104607 | CR | 23.502 CR2846 (Rel-17, 'B'): Updating the Credentials Holder controlled lists for SNPN selection | MediaTek Inc.

## Slide 5: Handling of SUCI/SUPI format for CH selection
S2-2104332 issue: “if the SNPN and the Credentials Holder are using the same PLMN ID and IMSI based SUPI is used, currently the HNI(MCC/MNC) of the corresponding SUCI is not able to distinguish if the UE is from the Credentials Holder or if the UE is a native subscriber.”
  Option 1.
  UE indicate NID of subscribed SNPN or indicate it is using PLMN subscription. AMF in serving SNPN will be able to distinguish if UE is from another SNPN or it is from PLMN, even when another SNPN or PLMN is using the same MCC/MNC as the current serving SNPN. AMF is able to use this information to perform AUSF/UDM selection.
  Option 2
  Except HNI in SUCI, other parts of the SUCI can be utilized for differentiating the serving SNPN and the Credentials Holder, for example the Routing Indicator. Then, if SNPN and Credentials Holder are using the same MCC/MNC, the Routing Indicator must be coordinately assigned for each network. Furthermore, there is a recent development in CT4 to add home network public key id in the SUCI as query parameter(C4-210158) which has the potential to be enhanced for the use case of access to SNPN with CH.
  Option 3
  When IMSI based SUPI is used, all the SNPNs and all the CHs must use different PLMN IDs
S2-2103978 | DISCUSSION | Discussion on the format of SUPI/SUCI used to access to a SNPN | vivo
S2-2103979 | CR | 23.501 CR2830R1 (Rel-17, 'B'): Handling of SUPI/SUCI format of a UE from credentials holder when accessing to a SNPN | vivo
S2-2104332 | CR | 23.501 CR2919 (Rel-17, 'B'): KI#1 T3: Handling of SUPI/SUCI format when accessing to a SNPN | Ericsson

## Slide 6: Handling of SUCI/SUPI format for CH selection
Questions:
  Do you support standardizing option 1?
    Yes
    No
  Do you support standardizing option 2?
    Yes
    No
  Do you support standardizing option 3?
    Yes
    No

## Slide 7: DCS architecture See S2-2104335
Questions:
  Do you support standardizing the DCS architecture options 1?
    Yes
    No
  Do you support standardizing the DCS architecture options 1?
    Yes
    No