## Slide 1
Sensing in 5G and Trial for Respiration Monitoring
2021-10-11

## Slide 2
Case3:
Bodyweight exercises 3
Requirement 3:
Count and recognize different typical bodyweight exercises.
Case1:
Respiration monitoring 1
Requirement 1:
Acquire the target respiration rate of a person.
Case2:
Indoor intrusion detection 2
Requirement 2:
Detect the intrusion of a person walking inside the monitored area and track his movements.
Reuse existing reference signals for communication (e.g., SRS, CSI-RS) to support sensing.
Sensing use cases based on existing reference signals
Source1 : Youwei Zeng et. al., “Farsense: Pushing the range limit of wifi-based respiration sensing with csi ratio of two antennas”
Source2 : O. Kaltiokallio and M. Bocca, "Real-Time Intrusion Detection and Tracking in Indoor Environment through Distributed RSSI Processing”
Source3 : S. Li, X. Li, Q. Lv, G. Tian and D. Zhang, "WiFit: Ubiquitous Bodyweight Exercise Monitoring with Commodity Wi-Fi Devices"

## Slide 3
Sensing mode
End-to end Arch. supporting sensing
Sensing function: management, control and computing, etc.
Procedure(s):
  Sensing Control procedure
  Sensing Data report procedure
Prioritize sensing based on sensing mode 1~4：
Existing UL reference signals for measurements executed by BS
Existing or new measurements between BSs
Existing or new measurements based on BS echo
Existing DL reference signals for measurements executed by UE
No. | Transmitter | Receiver
1 | UE | BS
2 | BS A | BS B
3 | BS A | BS A
4 | BS | UE
5 | UE A | UE B
6 | UE A | UE A
BS: Base Station
Network architecture supporting sensing
Notes: 注：可扩展到多UE多基站

## Slide 4
Sensing procedure:
Acquire channel frequency response data based on the received reference signal (CSI-RS)
Preprocess the data(e.g., denoising, outliers removing, filtering) and execute measurement
Report measurements to the core network
Calculate sensing results
Trial (sensing for respiration monitoring) setup:
System：5G NR, Central frequency 3.63GHz, bandwidth 100MHz
Scenario：indoor
gNB-UE distance： 2 meters
Person-UE distance： 0.5 meter
CSI-RS periodicity: 20 ms
Sensing trial based on NR: trial setup
Respiration monitoring based on DL existing reference signals

## Slide 5
respiration rate:~0.268Hz (16 breaths per minute)
Respiration monitoring trial results
Target person for respiration monitoring
Amplitude of channel frequency response
Phase of channel frequency response
Utilizing the channel frequency response based on CSI-RS, the receiver can monitor the respiration rate of the target people.

## Slide 6
Observations and proposals
Observation 1: It is feasible to perform sensing by utilizing existing downlink reference signals in some use cases.
Observation 2: Sensing based on uplink reference signals is also feasible similar to sensing based on downlink reference signals in principle.
Proposal : Study sensing service in R18 based on existing uplink/downlink reference signals

## Slide 7
THANK
YOU