## Slide 1
Discussion paper on Network & Computing
Power integration
China Telecom

## Slide 2
Content
Background and New Requirements
Use cases
Introduction of Computing network
Objectives and procedure
3
4
2
1

## Slide 3
  Background: requirements on computing in ITU
    Draft new Recommendation ITU-T Y.CAN-reqts: “Functional requirements of computing-aware networking”
    With the development of 5G and cloud computing, the transmission, analysis and storage of massive data pose huge challenges to traditional network and cloud computing, finally driving computing to move down from the cloud to the edge near the data source, forming distributed computing resources in the network.

## Slide 4
  Background: Computing Power Network architecture
  in ITU
    Draft Recommendation ITU-T Y.2501 (formerly Y.CPN-arch): “Computing Power Network – framework and architecture
    The objective of Recommendation ITU-T Y.2501 is to describe the framework and architecture of computing power network. It is a new type of network that realizes the optimized resource allocation, by distributing computing, storage, network and other resource information of service nodes through network control plane. It combines network context and user requirements to provide the optimal distribution, association, transaction and scheduling of computing, storage and network resources.

## Slide 5
  Background: requirements on computing in 6G
    IMT-2030 (6G) Promotion Group: White Paper on 6G Network Architecture Vision and Key Technologies
    Deep integration of network and computing power resources can achieve efficient coordination of Cloud, Edge, network and computing power. The network can be aware of and interwork with computing power resources to realize real-time computing power resources discovery, to dynamically schedule for computing power resources and services and to provide wide distribution of computing power and services. The integration of network and computing power can provide better user experience and higher utilization of network and computing power resources.

## Slide 6
  New Requirements in 5G：Computing Power
In 5G network architecture, the computing power is not involved. Only the communication quality index are introduced;
For some 5G scenarios XR and cloud gaming, there are potential requirements for computing power. For example, the type of computing power resources (GPU, FPGA, etc) and the total amount of computing power resources.
  Only non-computing aspects are considered for performance improvement, for example, 5QI enhancement, optimization based on I/P frame recognition, etc;
  Computing aspects are not considered;
Jointly optimizing communication and computing power can further improve better service quality and user experience for 5G user services. This requires the deep integration of network resources and computing power resources of operators

## Slide 7
  Use case 1 - XR : features and bottlenecks
Requirement 3：large computing power
The requirement of computing power is huge for some scenarios(e.g., rendering, modelling).
Requirement 2：high bandwidth
In XR business, high definition picture quality and DPI, such as 4K, 8K or 3D holographic will bring greatly impact to speed and network bandwidth.
Requirement 1：low delay
In the SA1 specification (TS 22.261), the max allowed end-to-end latency has been defined for XR services, and the end-to-end latency is the total PDB of UL and DL direction.
Bottlenecks in 5G network support for XR services
The requirement of computing power is huge for some scenario(e.g., rendering);
Heterogeneous computation power are needed.
Only 3rd party computing power resources are used, the computing power resource from MNO is not fully leveraged. Hence XR services are not closely integrated with MNO’s network

## Slide 8
  Use case 2 - Coordination among devices, network
Group of trusted devices in
  Personal IOT network
  Industry IoT
  V2X scenario
  Additional service needs
  Computing power sharing among group of trusted devices
  Challenges
  Heterogeneous operating systems and computing power of devices from different vendors
  New service model
  Distribution/sharing of computing power (both insider group and outside group ) with network assistance

## Slide 9
  EC : An architecture option for integration computing power into 5G network in REl18
Why choose EC (Edge Computing) as a start point for integration computing power resources into 5G network in Rel18
  EC are supported in Rel17 and early release, EC is aimed to provide closer computing server to the user, low latency are inherent of EC solution, only 3rd party computing power resources are used；
  Introduction of computing power controlled by operators in EC would bring less impact to 5G system in rel18.

## Slide 10
  Potential enhancements for the integration of EC and computing power in rel18:
Rel17 status of EC：
  EAS is owned or deployed by 3rd party, it is difficult to further improve the performance of service, such as the end-to-end delay or improve the QoE.
  R17 Edge computing mainly focuses on how to select an EAS (edge application server) which is nearer to the UE in location；
  The EAS (owned by 3rd party) discovery mechanism does not consider the computing power.
In R18, Potential enhancements for the integration of EC and computing power resources:
  computing power resources from MNO could be fully leveraged;
  Heterogeneous computation power resources could be provided;
  Jointly optimizing communication resource and computing power resources
    select an EAS controlled by MNO, considering both geographic locations and computing power;
    Overall QoS profile/QoS rule includes both communication QoS and computing QoS.
    End to end delay = communication delay + computing delay

## Slide 11
  Computing Power Architecture Example in EC
The EAS/AS (computing node) controlled by operator are deployed in the 5G network
5GC perceives/manages computing node:
  Registration, reporting status information and operator subscribes computing power resource
Computing power resource negotiation and allocation:
  Selection of (E)AS(application server) based on the negotiation of computing power requirement with UE
  5GC allocates and reserves both communication and computing power resources.
  5GC guarantees the low delay.
Computing resource registration, subscription and report
AF sending computing request
PCF deciding policies
SMF(CSCF) doing policies association
SMF(CSCF) selecting EAS

## Slide 12
  Call Flow of MNO controlled computing network

## Slide 13
  Objectives of this SID
  Objective 1: Identification and standardization computing power in 5G;
  Objective 2: Potential architecture enhancement in network architecture e.g. EC to coordinate with computing power;
  Objective 3: For operators controlled (Edge) Application Server(AS/EAS) , design the mechanism of EAS/AS (re-)discovery to satisfy the computing power resource requirement;
  Objective 4: Optimize the end-to-end delay for low delay service.

## Slide 14
THANKS
感 谢 聆 听