## Slide 1
Background material about grp mbr monitoring(S2-2201995) – [by ORACLE, Toyota and OPPO](4/1/2022 SA2 #150)
The next slides illustrates the new functionality proposed by S2-2201995 via a simplistic example.
The AIML FL Group in the example has only two UEs – UE1 and UE2.
Goto next slide

## Slide 2
1. provision the subscription information for the group of UEs, associated with FL operation, in a new entry of the Group Data table in the Subscription Data part of the UDR (consumed by the UDM) with the following configurations for the corresponding S-NSSAI and DNN
Subscription data type | Field | Description
…………. |  | 
Group Data | Internal group identifier | Internal identifiers of the group of UEs that the Group Data belongs to.
 | 5G VN …… | ……
 | Indication of the need to Select the same SMF/PCF/UPF for S-NSSAI/DNN = AIML FL’ | …...
23.502 Table 5.2.3.3.1-2: Group Subscription data types
New table entry
2. During UE Registration procedure (23.502 4.2.2.2.2 step 14b) the AMF retrieves from the UDM the Access and Mobility Subscription data. Based on Internal Group ID-list, AMF knows the UE belongs to the AIML FL group. The AMF retrieves then the new proposed table entry above (Group Data) in Group subscription data types table (23.502 Table 5.2.3.3.1-2). Based on the contents of the above entry <Indication of the need to Select the same SMF/PCF/UPF for S-NSSAI/DNN = AIML FL’>, the AMF knows that later on, when there is an establishment of PDU Session for S-NSSAI/DNN = AIML FL, the same SMF will have to be selected for all members of this internal AIML FL group.

## Slide 3
3. AIML FL UE1 sends an establishment request for a PDU Session (S-NSSAI/DNN = AIML FL). 23.502 Figure 4.3.2.2.1-1 step 2 AMF selects the SMF, which has registered in the NRF as one of the AIML FL SMFs (+ possibly other considerations such as locality, priority, capacity, etc.).
4. The AIML FL SMF knows it needs to select the same UPF and the same PCF for UE1 (in 23.502 4.3.2.2.1 step 4 the SMF downloads the UE subscription from the UDM. Based on Session Management Subscription data. Internal Group ID-list, the SMF knows the subscriber belongs to the AIML FL group. The SMF retrieves then the new proposed table entry above (Group Data) in Group subscription data types table (23.502 Table 5.2.3.3.1-2)(see previous slide). Based on the contents of the above entry <Indication of the need to Select the same SMF/PCF/UPF for S-NSSAI/DNN = AIML FL’>, the SMF knows that the same UPF and PCF will have to be selected for all members of this internal AIML FL group. Alternatively, we can simply have the AMF pass on in step 3 of 23.502 4.3.2.2.1 such an indication to the SMF).
5. AIML FL UE2 sends an establishment request for a PDU Session (S-NSSAI/DNN = AIML FL). 23.502 Figure 4.3.2.2.1-1 step 2 AMF selects the same SMF, which was selected for UE1 (see step 3). Similarly to step 4, the SMF selects the same UPF and PCF, which were previously selected for UE1.
Situation after step 5: the same SMF/UPF/PCF is selected for both UE1 and UE2.