3GPP SA WG2 Meeting #151E	S2-2203817r05

16 – 20 May 2022, Elbonia

Source:	Samsung

Title:	Terminology proposals for FS_eLCS_Ph3

Document for:	Approval

Agenda Item:	9.10

Work Item / Release:	FS_eLCS_ph3 / Rel-18

Abstract of the contribution: This contribution proposes terminology proposals for PRU and Reference UE for FS_eLCS_Ph3.

# 1. Discussion

This contribution proposes PRU/Reference UE terminology proposals to be adopted in TR 23.700-71. Part of this work has been performed within the LOCUS project (Grant Agreement No. 871249), funded by the European Commission within the Horizon 2020 Framework Program.

# 2. Proposal

It is proposed to adopt the following text within TR 23.700-71.

*** Start of the changes ***

## 3.1	Terms

For the purposes of the present document, the terms given in TR 21.905 [1] and the following apply. A term defined in the present document takes precedence over the definition of the same term, if any, in TR 21.905 [1].

Positioning Reference Unit (PRU): As defined in TS 38.305 [5].

Reference UE:	A UE with a location assumed known to the network that can obtain location related information of one or more target UE(s), which may assist the network to improve the positioning performance of target UE(s).

Editor's note:  It is FFS whether a PRU and a Reference UE should be combined into a single entity that is able to function as either or both.

NOTE: Within the FS_eLCS_ph3 study and the TR23.700-71, the Reference UE has no relationship with other Studies, e.g. FS_Ranging_SL, unless clearly mentioned. If a terminology alignment between studies is required, it will be done before starting normative work.

*** End of the changes ***