Pre SA2#152E e-meeting Email Discussion

Source: 	vivo

Title: 	Email discussion on interim conclusion of FS_PIN

# 0. Introduction

There’re 4 architecture alternatives and 28 solutions address to KI#2-KI#7. The SA2#152E meeting is the first meeting for discussing TR conclusions. In order to archive concensus, we should first agree on some key point then we are able to disccuss further.

The potential architecture alternative is as following for better describing the questions, but not imply that it is an agreed alternative:

# 1.	Key points for FS_PIN

## 1.1	New function(s) in 5GC side for PIN

### 1.1.1	Description

All the 4 architecture alternatives propose new function(s) in 5GC side for PIN (e.g., PINMF, PINCTRL, P-NF+P-AF, PIN Application Server, etc.). Some solutions of call flows imply to use existing NF (e.g., AMF, UDM) for PIN.

### 1.1.2	Companies View

Question 1: Only one AF (trusted or 3rd party) for PIN?

Question 2: Only one NF for PIN?

Question 3: One AF (3rd party) and one NF for PIN?

Question 4: Using existing NF (e.g., UDM, AMF) for PIN? And if yes, which NF?

| Company Name | Company View (Yes/No), [NF name] | Notes |
| --- | --- | --- |
| vivo | Question 1: Yes; Question 2: No; Question 3: No; Question 4: No. | There’s no need to have both NF and AF for PIN. From the current study, depends on solutions, the PIN function in 5GC side does not need to provide any service to other NFs, so for release 18, AF is proper for PIN. |
| InterDigital | See response. | We prefer not to answer “yes” or “no” to these questions because it largely depends on what the NF’s are doing. In terms of where PIN information is stored (i.e. PINE IDs, Policies, etc), we prefer to reuse as much of the existing infrastructure as a possible and store this information in the UDR but would not be opposed to creating a new NF (e.g. a PINMF) that can logically be part of the UDR. In terms of what NF sends information to the UE, we prefer to reuse existing procedures and allow the PCF or UDM to send the information. In terms of SA2 work, we do not see a strong need for the AF to be so involved. However, we would agree that it may make sense to allow the AF to provide the 5GC with information that might influence how traffic within a PIN is treated, what PINEs are allowed to join, etc. |
| Qualcomm | Question 1: Yes; Question 2: No; Question 3: No; Question 4: No. | PINEs could be both 3GPP or non-3GPP capable device. In this case, the most feasible solution is to manage PIN and PIN Elements from application layer. AF could be the proper entity to manage and store all PIN related configuration information. Existing 5GC architecture can be enhanced to support traffic differentiation and QoS control of PIN. No new NF is required. |
| Nokia | Question 1: Yes; Question 2: No; Question 3: No; Question 4: No; | There is no need to have a NF as in our opinion the AF shall manage the PIN at the application level. Some changes may be needed in the existing NFs e.g. UDM, UDR, AMF, SMF (depends on solution). But these changes would be to support things like e.g. subscription data handling, subscription authentication/ authorization, PDU session and QoS handling etc. |
| Apple | See response | There is no need for a dedicated NF for PIN within 5GC. Any required configuration and parameter provisioning would following the AF interaction with 5GC using existing interfaces ( via NEF or if trusted directly with NFs ) Internally 5GC uses existing procedures as a base to provision policy and parameters to PEGC, PEMC. |
| Ericsson | Question 1: Yes; Question 2: No; Question 3: No; Question 4: No. | No dedicated NF 5GC is needed. |
| OPPO | Question 1: Yes; Question 2: No; Question 3: No; Question 4: No; | We prefer to leverage AF to manage PIN and store PIN profile. Existing 5GC architecture can be reuse to support the interactions between PIN AF and 5GC NFs. |

### 1.1.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.1.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.2	Signalling between PEGC/PEMC and PIN function(s) in 5GC side (i.e., signalling on Pin3 and Pin4 interfaces)

### 1.2.1	Issue Description

The signalling between PEMC/PEGC and PIN function(s) in 5GC side (i.e., Pin3 and Pin4) can be over CP (i.e., over NAS) or over UP (i.e., via UPF). Even when the PIN function is an NF, the signalling also can be over UP depends on solutions.

### 1.2.2	Companies View

Question 1: Is the signaling over CP?

Question 2: Is the signaling over UP? If yes, should the study of the signaling be offloaded to SA6?

| Company Name | Company View (Yes/No), [Yes/No] | Notes |
| --- | --- | --- |
| vivo | Question 1: No; Question 2: Yes, Yes. | Define PIN service over NAS is not a flexible way that only operator can provide the service. The PIN service is able to be combined with curstomized service operation and UI that the vendor provided for users. Considering the TU left for normative phase, offloading the signalling design to SA6 helps saving TU for SA2. |
| InterDigital Inc. | Question 1: Yes. Question 2: No, No. | The 5GS already has the ability to perform policy provisioning, authorization, etc. We should reuse this existing infrastructure as much as possible rather than asking SA6 to re-create it. Further, our view is that the SA2 enhancements should not rely on SA6 work. Rather, SA6 enhancements for PIN should build on SA2’s architecture improvements. The Rel-18 SA2 enhancements should allow PINEs to connect to the operator’s network independent of whether the PINEs, PEMCs, and PEGCs deploy SA6 based applications. |
| Qualcomm | Question 1: No; Question 2: Yes, Yes. | PIN management, PIN authentication and authorization (i.e., the info exchange between AF and PINE/PEGC/PEMC) can be realized in application layer over user plane. We didn’t see the requirement and benefit to involve NAS impact for this purpose. We think SA6 is the better group than SA2 to study on the application layer capabilities of PIN. AF may use control plane signalling for the purpose of PINE traffic differentiation and QoS control in 5GC. |
| Nokia | Question 1: No Question 2: Yes; other SDO | We do not see the need to have a control plane communication between PEGC/PEMC and the PIN AF. In our view this is application layer communication and shall happen over the user plane. No strong opinion on whether SA6 shall study this. I believe at SA2 we cannot decide SA6 scope. This may be defined by other SDO and outside the scope of 3GPP also? e.g. Thread Specification is an open standard for reliable, cost-effective, low-power, secure, wireless IPv6 communication. It is designed specifically for connected home and commercial applications where IP-based networking is desired and a variety of application layers can be used on the same network. |
| Apple | Question 1: See response Question 2: Yes, No | PEGC and PEMC may be configured by the 5GC based on parameters provisioned by PIN AF (using enhancements to existing NAS signalling). But this does not require that PEGC and PEMC have a logical pin3, pin4 interface with PIN AF enabled by any 5GC NF. Pin3 and pin4 interfaces can be carried over user plane and we don’t think there is a need to standardize pin3 and pin4 interfaces. They are application layer interactions. |
| Ericsson | Question 1: No; Question 2: see Notes | Not clear what is meaning to move the study to SA6. Is it a new SID in SA6 in rel-18 or for further release. |
| OPPO | Question 1: No; Question 2: Yes, see Notes | There’s no need to involve NAS impact, the signalling between PEGC/PEMC and AF can be transmitted over the UP-based PIN specific application mechanism. It’s up to SA6 to decide whether to study this. |

### 1.2.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.2.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.3	Signalling among PEGC, PEMC, and PINE (i.e., Pin1, Pin2, and Pin5)

### 1.3.1	Issue Description

The interaction among PEGC, PEMC, and PINE is over non-3GPP access or sidelink, and do not impact the underlayer protocol. Upper layer is used for interaction among PEGC, PEMC, and PINE, which could use HTTP(S) protocol or others depends on solutions.

### 1.3.2	Companies View

Question 1: Should the study of the signaling be offloaded to SA6?

Question 2: If no for Question 1, which interface needs to be studied in SA2? Pin1, Pin2, and/or Pin5?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| vivo | Question 1: Yes. | The interaction among PEGC, PEMC, PINE shall be studied along with the interaction between PEGC/PEMC and PIN function(s). Considering the TU limitation (2 for normative) of this study, offloading some part of the study to SA6 can save the TU in SA2. |
| InterDigital Inc. | Question 1: No | It is too strong of a statement to say that all signalling is offloaded to SA6. SA2 should define interactions that involve policy provisioning, authorization, etc. We should follow an approach similar to ProSe in the sense that SA2 defines PC5 procedures but does not define applications that run on top of PC5. SA6 should define the application layer interaction on top of what SA2 specifies. For example, SA6 has key issues on AS Discovery, service switch, etc. |
| Qualcomm | Question 1: Yes. | The interaction among PEGC, PEMC, PINEs should be independent of transport layer. It’ more likely based on application layer communication over HTTP/IP. This study should be offloaded to SA6 or external SDOs. |
| Nokia | Question 1: Yes, other SDO? | No strong opinion on whether SA6 shall study this. I believe at SA2 we cannot decide SA6 scope. This may be defined by other SDO and outside the scope of 3GPP also? e.g. Thread Specification is an open standard for reliable, cost-effective, low-power, secure, wireless IPv6 communication. It is designed specifically for connected home and commercial applications where IP-based networking is desired and a variety of application layers can be used on the same network. |
| Apple | Question 1: No (cannot say what SA6 should study) | We are aligned with Nokia’s view. We think 3GPP SA2 PIN solution is independent of the interaction that PINE, PEGC and PEMC might have. Our view is that 3GPP PIN solution would be more acceptable if it does not make any restriction on what protocol is used between PINE, PEGC and PEMC. |
| Ericsson | See Notes | Not clear what is meaning to move the study to SA6. Is it a new SID for SA6 in rel-18 or future release. It can be questioned if it shall be part of the 3GPP scope. |
| OPPO | Question 1: See Notes | Signalling among PEGC, PEMC, and PINE (i.e., Pin1, Pin2, and Pin5) is more likely transmitted over a dedicated PIN protocol layer or application layer. There’s no need to enhance the existing 5GC architecture. This study should be offloaded to SA6 or external SDOs. |

### 1.3.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.3.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.4	Mechanism for policy and parameters provisioning to PEGC for PIN management

### 1.4.1	Issue Description

Different mechanism is proposed by different solutions for provisioning policy and parameters to PEGC for PIN management (KI#3), e.g., UCU described in 4.2.4.2 TS 23.502, UCU described in 4.2.4.3 TS 23.502, Service parameters provisioning described in 4.15.6.7 TS 23.502, etc.

### 1.4.2	Companies View

Question 1: Is "UE Configuration Update procedure for transparent UE Policy delivery" procedure described in clause 4.2.4.3 of TS 23.502 the basis for provisioning policy and parameters to PEGC for PIN management? If not, what is the prefer procedure?

Question 2: Does the policy and parameters for PIN management need to be stored in UDR?

| Company Name | Company View (Yes/No), [procedure description] | Notes |
| --- | --- | --- |
| vivo | Question 1: Yes; Question 2: No. | The policy and parameters for PIN management is a UE policy information and configuration provisioned to PEGC. The PIN function in 5GC side is the place to store the information, and the PIN function will provision the parameters to PCF and PEGC/PEMC, there’s no need to store them in UDR. |
| InterDigital Inc. | Question 1: See response Quesiton 2: Yes | The UE Configuration Update or UE Parameters Update (i.e. Solution #9) are preferred. Storage in the UDR makes the most sense to us. Existing procedures between the UDR and PCF or UDM/UDR and AMF can largely be reused. However, we would also be ok to standardize a PIN NF (i.e. PINMF) that can logically be part of the UDM/UDR. |
| Qualcomm | Question 1: No; Question 2: No. | PIN management should be handled in application layer, among AF, PEMC, PEGC, PINE. The parameters and policy for PIN management can be transferred in user plane. UDR don’t need to store the policy and parameters for PIN management. |
| Nokia | Question 1: No, only URSP and other UE policies needed by PEGC may be delivered. Question 2: No. But some information may be present in UE subscription e.g. PEGC subscription may have information like how many PIN or PINE it can support |  |
| Apple | Question 1: Yes Question 2: Yes | Parameters for PIN management is delivered as part of UE Policy There may be some PIN specific parameters that are part of UE subscription. |
| Ericsson | Question 1: No; Question 2: No. | PIN management shall be handled inside the PIN network. |
| OPPO | Question 1: No Question 2: No | We prefer to send the policy and parameter provisioning messages via application layer. PIN AF is the proper place to store policy and parameters for PIN management. |

### 1.4.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.4.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.5	Mechanism for policy and parameters provisioning for PIN communication

### 1.5.1	Issue Description

Different mechanism is proposed by different solutions for provisioning policy and parameters to PEGC, NG-RAN, SMF, and UPF for PIN communication (KI#4).

### 1.5.2	Companies View

Question 1: Is "PDU Session Modification" procedure the basis for provisioning policy and parameters to PEGC, NG-RAN, SMF, and UPF for PIN communication, e.g., for routing rule provisioning to UPF and PEGC, for QoS rule provisioning to NG-RAN? If not, what is the prefer procedure?

Question 2: Does the policy and parameters for PIN management need to be stored in UDR?

| Company Name | Company View (Yes/No), [procedure description] | Notes |
| --- | --- | --- |
| vivo | Question 1: Yes; Question 2: No. | The policy and parameters for PIN communication is policy information related to a PDU Session assocated with PIN for traffic relay. The PIN function in 5GC side is the place to store the information, and the PIN function will provision the parameters to PCF and PEGC/PEMC, there’s no need to store them in UDR. |
| InterDigital Inc. | Question 1: Yes (or PDU Session Establishment) Quesiton 2: Yes | The UE Configuration Update or UE Parameters Update (i.e. Solution #9) are preferred. For Q2, we understand the policies and parameters to relate to the PCC rules, QoS Profiles, and QoS Rules for the PDU Session. We believe that, as happens today, the PCF should derive the PCC Rules and the SMF should derive the QoS Profiles and QoS Rules. Some new information elements may be needed for PIN and the PCF may derive these new information elements based on information that is obtained from the UDR. |
| Qualcomm | Question 1: Partially agree; Question 2: Yes. | Varity of mechanism specified in TS 23.501 and 23.502 can be reused or extended for provisioning policy and parameters to PEGC. • UE Configuration Update • PDU Session Establishment/Modification • External Parameter Provisioning Provisioning of UE policy is necessary. At the same time, provisioning policy to 5GC (e.g., PCF, UDR) should be taken into account as well AF may provision related configuration to UDR for PINE traffic differentiation and policy control. This info can be stored in UDR as default policy for PINE traffic handling. PCF can retrieve the policy from UDR when the PINE request traffic route via 5GC. |
| Nokia | Question 1: For traffic routing and QoS differentiation different policies can be provided to the PEGC UE, RAN, UPF. So, it is not just PDU session modification procedure. Question 2: Yes. Assumption here is we are talking about policies needed for traffic routing and QoS differentiation |  |
| Apple | Question 1: Yes, (but not limited to this) Question 2: Yes | SM signalling could also be used for provisioning PIN parameters for communication. There may be some PIN parameters linked to UE subscription. |
| Ericsson | Question 1: Yes; Question 2: Yes. | The existing parameters delivery mechanisms (not limited to PDU session modification) in 5GC can be used if needed. |
| OPPO | Question 1: Yes, (but not limited to this) Question 2: See notes | Besides PDU session modification, many other existing parameter provision mechanisms (e.g., External Parameter Provisioning) can also be reused. It depends on the details of the policy and parameters for PIN communication |

### 1.5.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.5.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.6	PEMC can be legacy or not

### 1.6.1	Issue Description

The PEGC and PEMC both are UE, and it is obvious that legacy UE is not able to act as PEGC, but legacy UE is able to act as PEMC depends on solutions.

### 1.6.2	Companies View

Question 1: Is legacy UE able to act as PEMC?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| vivo | Yes | If legacy UE is not able to act as PEMC, when user buys gateways and devices from shop and wants to use PIN service, the user shall change cell phone to enable remote control of the PIN, it is not convienent for user. If the PEMC function resides above OS layer, a legacy UE is able to be a PEMC, i.e., user can download software of PEMC function into a legacy UE. |
| InterDigital | No | We do not believe that PEMC can be a legacy UE. Such an assumption would already rule out many of the solutions in the TR and calls into question why SA2 is working on this topic at all. |
| Qualcomm | Yes | PEMC is an application layer capability, which can be supported via downloading of corresponding software. |
| Nokia | Question 1: Yes | In our view, PEMC is an application. It may run on a UE or any other device e.g. a laptop/pc, tab etc. There is no specific (0r new) 3GPP UE functionality needed for PEMC. Only for PEGC UEs some additional capabilities may be needed for supporting traffic relay from PINE. |
| Apple | No | PEMC is a Rel-18 capability for the UE. So we don’t see how a legacy UE can be a PEMC. There could UE policies applicable for a UE acting as a PEMC. A legacy UE may not interpret these policies. |
| Ericsson | See Notes | It’s “yes” in general. But it may depend on what is required on the PEMC and how information are delivered. |
| OPPO | Question 1: Yes | As mentioned before, PIN management can be handled in application layer. A legacy UE can act as PEMC by downloading software of PEMC function. |

### 1.6.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.6.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.7	Who triggers the authentication procedure with PINE

### 1.7.1	Issue Description

The authentication with PINE is for the purpose that network is able to identify the PINE so that malicious PINE is not able to forge the PINE to use its policy for communication. Depends on solutions, PEMC, AMF, and SMF triggers the authentication procedure with PINE.

### 1.7.2	Companies View

Question 1: Who triggeres the authentication procedure with PINE, SMF, AMF, PEMC, or others?

Question 2: The authentication is triggered during PIN management or PIN communication procedure?

| Company Name | Company View (SMF/AMF/PEMC/…) / (PIN management / PIN communication) | Notes |
| --- | --- | --- |
| vivo | Question 1: SMF; Question 2: PIN communication | The authentication would be based on EAP framework, so the UDM/AAA needs to indicate authentication result to the one who triggers the authentication. The SA1 requirement indicates that 5GS shall support credential downloading, whose User ID is linked to the subscription of the gateway UE, which means the authentication also needs to be able to make the network be able to link the PINE with the subscription of the gateway UE. If PEMC triggers the authentication that involves 5GC to forward the EAP messages over NAS, the PEMC cannot be legacy, and the network is not able to know the authentication result during the authentication procedure, so not able to link the PINE with the subscription of the gateway UE. And there’s an alternative implementation method for PEGC/PEMC to trigger the authentication and forward the EAP messages over 5G UP. If PEGC/PEMC sends the result to 5GC, then it is doubt whether the 5GC can trust the result sendind from a UE. The PIN management is only for provisioning policy and parameters to PEGC for allowing a PINE to connect to the PEGC, and PIN communication is for provisioning policy and parameters to PEGC for traffic relay. The authentication is not needed for PIN management considering there’s no traffic policy provisioned during PIN management procedure, so the authentication is only needed for PIN communication procedure, hence SMF is the proper NF to trigger the authentication, and SMF triggers EAP authentication already is supported for secondary authentication and authorization procedure with different trigger event. |
| InterDigital | Question 1: See response. Question 2: Both | Rather than what entity triggers authentication and authorization, we think that it would be helpful to first agree on when authentication and authorization is triggered. In other words, in what procedures is authentication and authorization triggered? Our opinion is as follows: When a PINE first attempts to join a PIN and first communicates with a PEMC, authentication and authorization should be triggered. This is needed in order to make sure that the PINE is authorized to join the PIN. When a PINE first attempts to communicate with a PEGC, authentication and authorization should be triggered. This is needed so that the PEGC can be sure that the PINE is authorized to communicate within the PIN. |
| Qualcomm | Question 1: PEGC/PEMC. Question 2: Both | The full credential information of PINE should be managed and stored in the Application Server (or AAA server). When a PINE requests to join a PIN or initiate PIN communicate to 5GC, PEMC/PEGC can trigger the authentication and authorization procedures with the PIN AS. The information exchanged for AA can be delivered in user plane of PEGC/PEMC. Authentication and Authorization may be required when PINE joining a PIN, or when PINE initiating communication via PEGC. |
| Nokia | Question 1: PEMC or PEGC may trigger authentication/authorization of the PINE Question 2: Both | While the authentication during PIN management is done at the application layer i.e. the PEMC, PIN AF performs the authentication/authorization of the PINE. This is transparent to 5GS. When the PINE requests for a relay communication via PEGC, additional authentication/authorization may be initiated by the PEGC. |
| Apple | Question 1: PEMC/PEGC Question 2: Both | Authentication during joining a PIN is managed by PEMC. For communication, there could be additional authentication by the PEGC. |
| Ericsson | Question 1: PEMC. Question 2: See Notes | Authentication is on the device level. During the communication, some authorization mechanism probably is needed. |
| OPPO | Question 1: PEGC/PEMC. Question 2: Both | During PIN management, the authentication with PINE is triggered by PEMC. During PIN communication, the authentication with PINE is triggered by PEGC or PEMC. |

### 1.7.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.7.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

# 2.	Summary and way forward proposal

Inputs from xx companies were collected so far.

Editor’s Note: This clause should contain propose way forwards.

# References

[1]		3GPP TR 23.700-88, “Study on Personal IoT Networks”