## Slide 1: Evaluation and interim conclusion for KI#8 (FL)
vivo
2022-07-29

## Slide 2: CONTENT
Observations and Evaluation on Existing Solutions Captured for KI#8
Interim Conclusions for KI#8

## Slide 3: Observations on Existing Solutions Captured for KI#8
Sol. Num. | Main issue to resolve | Main impacts
Sol #21, 22, 23, 24 and 53A | - FL clients discovery by FL server, in case that it determines FL is needed; - FL task interaction between FL server and FL clients | - FL clients registration to NRF; FL clients discovery by FL sever from NRF FL task request and interim result interaction between FL sever and FL clients;
Sol #53B | - FL NFs (FL sever and clients) discovery , in case that normal MTLF determines FL is needed but without FL capability itself | FL server and FL clients registration to NRF; FL sever and clients discovery from NRF
Sol #51 | - Old FL clients status monitoring; - New FL clients selection for FL procedure | Register FL procedure information into NRF dynamically during the Federated Learning processes. Selection of Client NWDAF(s). Monitoring Client NWDAF status updates. Dynamic discovery of new Client NWDAF(s).
Sol #52 | - FL model accuracy monitoring and FL model retraining | MTLF (FL sever) provides Training Accuracy metric to AnLF for FL model; AnLF calculates the Base Accuracy metric in live network for FL model
Notes: Solution 34可以属于第一类，但是没有区分AnLF和MTLF，仅统一是NWDAF

## Slide 4: Observations on Existing Solutions Captured for KI#8-2
Observation 1: Most solutions propose FL clients and FL server registration to NRF and discovery via NRF
Observation 2: FL server communicate with FL clients about FL model training task Info and interim FL results to generate a model without exchanging privacy training data
Observation 3: it looks reasonable that MTLF (rather than AnLF) determine to trigger FL procedure as MTLF is responsible for model training and whether FL is needed or not.
Observation 4: Model sharing issue has been raised in some solutions, which is a general issue and depends on conclusion of KI#5
Observation 5: In addition to FL procedure itself, Solution 52 also propose to consider model accuracy to improve FL Model performance, which is related to KI#1.

## Slide 5: Interim Conclusions for KI#8
Principle 1: FL clients and FL server register their FL related capability to NRF
Principle 2: MTLF(with FL client/sever capability) discover FL clients and FL sever from NRF.
Principle 3: FL server communicates with FL clients about FL model training task Info and interim FL results to generate a model without exchanging privacy training data
Principle 3: MTLF (rather than AnLF) determine to trigger FL procedure as MTLF is responsible for model training and whether FL is needed or not.
Principle 4: Model sharing between FL client and FL sever depends on the conclusion of KI#5
Principle 5: How to improve FL Model performance is related with KI#1 and should be concluded jointly