## Slide 1: SoH Questions for FS_eUEPO
Intel (Rapporteur)

## Slide 2: SoH for KI#1 (URSP in VPLMN) - 1
How to identify the PLMN specific URSP to UE:
  Option A: The RSD is extended to include the VPLMN ID(s) as validation criteria, a URSP Rule can contain RSD for different VPLMN ID(s). (Solution#2, #4 and #29)
  Option B: The Traffic Descriptor in the URSP Rule is extended to include the VPLMN ID.(Solution#3)
  Option C: The PCF provides a list of PSIs associated to the HPLMN and a list of PSIs associated to each of the VPLMN with roaming agreements. (Solution#6)
  Option D: No extensions to the RSD or URSP rule. The PCF provides the URSP Rules and RSD components that are applicable in the VPLMN where the UE is registered and removes them when the UE deregisters. (Solution#1, #2, #3 and 5)
  Evaluation for the solutions can be found in S2-2205529.
  Currently the dispute is on Option A and C. If Option A or C cannot be agreed, then Option D will be the default solution, but Option D is not preferred.
  Q1: Can we proceed with Option A for normative work?
  Yes:
  No:
  Q2: Can we proceed with Option C for normative work?
  Yes:
  No:

## Slide 3: SoH for KI#1 (URSP in VPLMN) -2
Which Network Function in VPLMN provides information to H-PCF to generate VPLMN specific URSP rules:
  Option A: AF in VPLMN provides service parameters (TD, Route selection parameters and precedence, Validation Criteria) to H-PCF (Sol#1, #2, #6). AF influencing URSP generation has been supported in TS 23.502 (Clause 4.15.6.10) and TS 23.548 (Clause 6.6), UDM needs to be enhanced with supporting VPLMN S-NSSAI and DNN.
  Option B: The V-PCF provides the UE Policy assistant information (the mapping from traffic descriptor to DNN, NSSAI, SSC mode, PLMN ID, etc.) to H-PCF.(Solution#3)
  Option C: The V-PCF generates URSP rules and send them to H-PCF for validation and distribution. (Solution#4)
  Option D: The V-PCF provides service parameters (TD, Route selection parameters and precedence, Validation Criteria) to the H-PCF. (Solution #5)
  Evaluation for the solutions can be found in S2-2205529.
  Currently the dispute is on whether to support Option A, Option D or both Options.
  Q1: Can we asupport Option A?
  Yes:
  No:
  Q1: Can we support Option D?
  Yes:
  No:

## Slide 4: SoH for KI#1 (URSP in VPLMN) -3
  Q3: Can we support both Option A and Option D?
  Yes:
  No:

## Slide 5: SoH for KI#1 (URSP in VPLMN) -4
Which PLMN determines the URSP for UE:
  Option A: VPLMN URSP determination in HPLMN (Sol#1, #2, #3, #4, #5, #6, #28 option 1)
  Option B: VPLMN URSP determination in VPLMN (Sol#27, #28 option 2)
  Evaluation for the solutions can be found in S2-2205529.
  Currently the dispute is whether to support Option A or Option B.
  Q1: Can we also support Option A?
  Yes:
  No:
  Q1: Can we also support Option B?
  Yes:
  No:

## Slide 6: SoH for KI#2
The conclusion for KI#2 is very controversial, in order to make progress at this meeting, we will have show-of-hands on basic questions.
Show of hands questions:
  Q1: Does the network need to be aware of whether URSP rule(s) is/are enforced by the UE?
  Yes:
  No:
  Q2: If the answer of Q1 is Yes, does the network need UE assistance in order to determine that?
  Yes:
  No:
  Q3: If the answer of Q2 is “Yes”, whether this should be tied to user consent
  Yes:
  No:
  Q4: If the answer of Q2 is “Yes”, should the UE report the assistance information associated to a PDU Session, out of a PDU Session or both?
    Option A: UE reporting the assistance information associated to a PDU Session to SM-PCF :
    Yes:
    No:
    Option B: UE reporting the assistance information out of a PDU Session to UE-PCF:
    Yes:
    No:
    Support both Optiona A and Option B:
    Yes:
    No:

## Slide 7: Backup for KI#2 (UE reporting based solutions)
UE reporting based solutions:
  Reporting URSP enforcement result at UE:
    Report URSP enforcement result in UCU
      Sol#11 (OPPO)
    Report URSP notification component in UL NAS Transport
      Sol #31 (DT)
  Report URSP Rule related information during PDU Session Establishemt:
    Report URSP Rule ID in PDU Session Est. Request
      Sol#7 (Samsung), Sol #9 option #1 (Lenovo), Sol#12 (Huawei)
    Report URSP Rule Precedence and OSID in PDU Session Est. Req
      Sol#8 (China Unicom)
    Report URSP Rule in PDU Session Est. Req
      Sol#10(vivo)
    Report Rule precedence and App ID in PDU Session Est. Req
      Sol#13 (China Telecom): App ID is for secondary authentication
    Report TD and App ID in PDU Session Est./Mod. Req
      Sol#14 (Orange)
    Report App ID in PDU Session Est. Req
      Sol #15 (NEC)