## Slide 1: Way Forward Discussion for FS_eUEPO
Intel (Rapporteur)

## Slide 2: Focus for Next Meeting (SA2#152E):
Solution update, way forward proposal for each key issue, solution evaluation and conclusion.
TR for information and potential TR approval
  NOTE: No new solution will be handled at next meeting.

## Slide 3: Way Forward for KI#1 (URSP in VPLMN)
How to identify the VPLMN specific URSP to UE
  VPLMN ID in RSD as RSVC (Route Selection Validation Criteria)
    Sol#2 (Lenovo), Sol#4 (Huawei), Sol#29 (InterDigital)
    Can we use this approach as way forward solution?
  VPLMN ID in TD
    Sol#3_Option#1 (vivo)
  VPLMN ID along with PSI
    Sol#6 (Qualcomm)
  Impact to URSP operation for UE in roaming as Validation Criteria corresponding to the VPLMN is included in URSP  The UE in roaming needs to consider Validation Criteria (cf. Currently “NOTE 7: In this Release of specification, inclusion of the Validation Criteria in Roaming scenarios is not considered.” in Table 6.6.2.1-3: Route Selection Descriptor of TS 23.503)
    Sol#1 (Nokia)
  Nothing new is proposed (no impact to URSP and UE)  H-PCF provides VPLMN specific URSP to UE in roaming in the VPLMN (If serving PLMN is changed, the URSP is updated to the UE)
    Sol#3_Option#2 (vivo), Sol#5 (LGE)
Which PLMN determines the URSP for VPLMN and provides it to the UE
  On VPLMN URSP determination in HPLMN:
    AF Guidance to PCF has been supported in clause 4.15.6.10 of TS 23.502, no normative work is required beyond URSP:
      Sol#1 (Nokia), Sol#2 (Lenovo), Sol#6 (Qualcomm)
    Via V-PCF to H-PCF interface, normative work is needed to enable the URSP influence between V-PCF and H-PCF:
      Sol#3 (vivo): VPLMN assistant UE policy info, Sol#4 (Huawei): URSP, Sol#5 (LGE): Service Parameters, Sol#28_Option#1 (Samsung): Info to generate URSP by H-PCF such as TD, RSD
    Can we support both options? VPLMN can determine which option to use.
  VPLMN generates and provisions its own URSP to UE directly:
    Sol#27(Ericsson), Sol#28_Option#2 (Samsung)
    This was controversial.

## Slide 4: Way Forward for KI#2 (UE reporting assistance) (2-1)
UE reporting assistance
  Report URSP Rule ID in PDU Session Est. Request
    Sol#7 (Samsung), Sol #9 option #1 (Lenovo), Sol#12 (Huawei)
    Can we take this proposal as way forward?
  Report URSP Rule Precedence and OSID in PDU Session Est. Req
    Sol#8 (China Unicom)
  Report URSP Rule in PDU Session Est. Req
    Sol#10(vivo)
  Report URSP enforcement result in UCU
    Sol#11 (OPPO)
  Report Rule precedence and App ID in PDU Session Est. Req
    Sol#13 (China Telecom): App ID is for secondary authentication
  Report TD and App ID in PDU Session Est./Mod. Req
    Sol#14 (Orange)
  Report App ID in PDU Session Est. Req
    Sol #15 (NEC)
  Report URSP notification component in UL NAS Transport
    Sol #31 (DT)

## Slide 5: Way Forward for KI#2 (5GC verification) (2-2)
Only CP based verification
  Sol#7 (Samsung), Sol#11 (OPPO), Sol#12 (Huawei), Sol#13 (China Telecom), Sol#14 (Orange), Sol#15 (NEC), Sol#30 (Lenovo), Sol#31 (DT), Sol#32 (Samsung)
  Can we take this as way forward solution?
CP+UP based verification
  Sol#8 (CUC), Sol#9 (Lenovo), Sol#10 (vivo)

## Slide 6: Way Forward proposal for KI#3 (Provision consistent URSP to UE across 5GS and EPS) (2-1)
Enhancing the RSD mapping in EPS:
  RSD with Applicability in EPS enhancement)
    Sol #17 (Nokia)
Dynamic URSP provisioning and updating in EPS:
  Provision URSP to UE in E-UTRAN accessing to 5G via N3IWF
    Sol#34 (vivo): proposes to provision the URSP to UE in EPS by registering the UE to 5GC via E-UTRAN with N3IWF, which relies on the deployment of N3IWF in 5GC and UE triggering the registration. There are some aspects unclear for this solution:
      If the URSP update happens before the UE triggers the URSP provisioning request, how does UE-PCF update the URSP rule to UE?
      Accessing to 5GC via N3IWF was defined to use non-3GPP access, while this proposal uses the 3GPP access (E-UTRAN), which was never studied in early releases and may have significant architecture change.
      The design requires the UE to do dual registration to both EPS and 5GS, it’s very questionable in real deployment.

## Slide 7: Way Forward proposal for KI#3 (Provision consistent URSP to UE across 5GS and EPS) (2-2)
Dynamic URSP provisioning and updating in EPS:
  Provision URSP to UE via ePCO
    Sol# 16 (Ericsson), Sol#18 (Intel, Apple, OPPO), Sol# 19 (NEC), Sol#20 (Samsung), Sol#33 (Intel, NEC, Samsung)
    In principle, Sol#16 and Sol#33 are very similar with some small difference:
      Sol#33: UE reporting URSP Support indication in EPS in initial Attach Request in EPS.
      Sol#16: Try to avoid MME impact without passing any new information by AMF to MME during 5GS to EPS mobility, but it poses some open issues on selecting the same UE-PCF, no PCRTs for UE Policy Control were enforced in MME and SM-PCF determining the UE capability of URSP Support in EPS based on user subscription.
      UE Policy Association handling during mobility from 5GS to EPS.
        For Sol#16, it’s proposed the AMF to notify UE-PCF to delay terminating the UE Policy Association.
        Sol#33 proposes not to terminate the UE Policy Association during 5GS to EPS mobility and update the UE Policy Association in EPS. After the UE Policy Association update in EPS, the UE-PCF can initiate the UE Policy Association termination towards AMF.
    Can we take Sol#33 as way forward?

## Slide 8: Way Forward Proposal for KI#4 (Support standardized and operator-specific traffic categories in URSP)
Solutions without stage 2 impact:
  New standardized value in DNN/Traffic Descriptor
    Sol#21 (Huawei, no impact to stage 2), stage 3 needs to complete the work.
  New standardized value in APP ID
    Sol#25 (China Telecom, no impact to stage 2), stage 3 needs to complete the work.
  New standardized value in Connection Capabilities in TD of URSP rule
    Sol#35 (Vodafone, Application client determining the TD, no impact to stage 2 and 3 impact), stage 3 doesn’t need to work.
  If any above solution is selected, no normative work in stage 2 is needed. Any view?
Traffic Category in TD of URSP rule
  Sol#22 (Lenovo, additional ATC rule in UE Policy)
  Sol#23 (Nokia, UE determining TD by implementation)
  Sol#24 (vivo, UE determining TD by implementation)
  Sol#26 (Apple, Application client determining the TD)
  Can we take this approach (Traffic Category in TD) as way forward and continue to discuss on how the UE determines the TD?

## Slide 9: Rel-18 FS_eUEPO Overall Work Plan
 |  |  |  | Feb, 22 | Apr, 22 | May, 22 | Aug, 22 | Oct, 22 | Nov, 22 | Jan, 23 | Feb, 23 | 
SID/WID | Study TU | Normative TU | Total TU | #149 | #150 | #151 | #152 | #153 | #154 | #154AH | #155 | Total TU
  Overall Work Plan
  SA2#149e, 0.5 TU assigned, 15 documents in maximum:
    TR Skeleton, TR Scope, Architectural Assumption, Key Issues.
  SA2#150e, 1 TU assigned, 30 documents in maximum:
    Key issue update and new solutions. Last e-meeting for new Key Issue.
  SA2#151e, 1 TU assigned, 30 documents in maximum:
    Stabilize solution. Last e-meeting for new solution. Potential TR for information.
  SA2#152(e), 1 TU assigned, 30 documents in maximum:
    Stabilize solution and conclusion, TR for information and potential TR for approval, potential WID discussion and approval.
  SA2#153(e), 0.75 TU assigned, 23 documents in maximum:
    Potential update on solution and conclusions, WID approval and update.
*The Work Plan will be updated and reflected in status report after each meeting.
FS_eUEPO | 4.25 | 1.5 | 5.75 | 0.5 | 1 | 1 | 1 | 0.75 | 0.5 | 0.5 | 0.5 | 5.75