## Slide 1: Evaluation and interim conclusion for KI#3
vivo
2022-07-29

## Slide 2: CONTENT
Observations and Evaluation on Existing Solutions Captured for KI#3
Interim Conclusions for KI#3

## Slide 3: Observations on Existing Solutions Captured for KI#3-1
Sol. Num. | Use case scenario | Which NF to exchange data/analytics | Data/analytics exchange direction | Data types | If new NF services are needed to define | Data/analytics consumer
10 (E) | NA | GEF | VPLMN<-HPLMN | Data + analytics | Not known | VPLMN NWDAF
11 (CATT) | Home routed Slice +SMF selection | NWDAF | VPLMN<-HPLMN | Analytics (slice load analytics, NF load analytics) | N | VPLMN NWDAF
17 (CATT) | Home routed Slice selection | NWDAF | VPLMN->HPLMN | Analytics (Service Experience analytics) | N | HPLMN NWDAF
37(HW) | HR QoS adjusting | NWDAF | VPLMN->HPLMN | Analytics (Service Experience analytics) | N | HPLMN NWDAF
38(Nokia) | NA | NWDAF | VPLMN<-HPLMN | UE Analytics profile (e.g UE mobility pattern…) | Y (new NWDAF_DataRetrieval service) | HPLMN NWDAF
 |  |  | VPLMN->HPLMN | Data |  | VPLMN NWDAF
39 (vivo) | NA | DCCF | VPLMN->HPLMN | Data + analytics | N (reusing existing service but with enhancements) | HPLMN NWDAF/NF consumer
40 (Samsung) | NA | NEF | VPLMN<-HPLMN | Data + analytics | N (reusing existing service but with enhancements) | HPLMN NWDAF
 |  |  | VPLMN->HPLMN | Data + analytics |  | VPLMN NWDAF
Notes: Solution 34可以属于第一类，但是没有区分AnLF和MTLF，仅统一是NWDAF

## Slide 4: Observations on Existing Solutions Captured for KI#3-2
Observation 1: Most solutions focus on architecture enhancements and a few solutions propose use cases and solve the corresponding issue
Observation 2: Both data exchange direction, i.e. from VPLMN to HPLMN, and from HPLMN to VPLMN have been proposed and discussed in different solutions
Observation 3: Both data types, i.e. data and analytics have been proposed and discussed in different solutions
Observation 4: Most solutions propose consider to check user consent information if the exchanged data is UE related data in roaming scenario
Observation 5: Most solutions propose to enhance reuse existing NF services (e.g. NWDAF or DCCF services) to exchange data in roaming scenario, but may with some enhancements, e.g. constraining on the type and amount of data exposed to each PLMN, manipulating data/analytics according to roaming agreement and checking user consent for data collection about UE.

## Slide 5: Interim Conclusions for KI#3
Principle 1: Roaming Data or Analytics about roaming UE can be exchange between HPLMN and VPLMN, or vice versa under user consent assumption.
Principle 2: NWDAF(or DCCF, etc.) is used to exchange data/analytics in roaming scenario between HPLMN and VPLMN, either from HPLMN to VPLMN, or vice versa;
Principle 3: Enhance reuse existing NWDAF/DCCF services (e.g. Data Management service) to exchange data in roaming scenario e.g. constraining on the type and amount of data exposed to each PLMN, manipulating data/analytics according to roaming agreement and checking user consent.