## Slide 1: Discussion on packet loss during multicast MBS delivery and solutions
Huawei, Hisilicon

## Slide 2
5GC
Phase 1: AF/AS create/activate a multicast MBS session, and start to deliver group communication media via the multicast MBS session to the joined UE.
The NG-RAN supports MBS and shared delivery is used. The shared delivery toward NG-RAN is triggered by the 1st joined UE per 7.2.1 in TS 23.247.
MCX AS
Potential packet loss when using multicast MBS shared delivery
Multicast MBS
- active
UL media
Joined & CM-CONNECTED
5GC
MCX AS
Multicast MBS
- inactive
UL media
Joined & CM-IDLE
Phase 2: No one talks in the group for a while.
The multicast MBS becomes inactive, and some UEs enter IDLE mode due to no media transmission
5GC
MCX AS
Multicast MBS
- active
UL media
Phase 3: User A talks again.
The multicast MBS becomes active again due to new media packet is coming.
The UE in IDLE is being paged. The UEs will become connected again.
But, these UEs may not become connected at the same time. The late connected UEs may lose/miss the media packet , as the packet already being transmitted once the 1st UE become connected which triggers the shared delivery restore and start transmitting data again.
Packet is lost/missed!!!
All is caused due to the MC service server is NOT aware of the multicast session status changes, and send the DL packet at the improper moment.
Joined & CM-CONNECTED
Joined & CM-IDLE
User A
User A
User A

## Slide 3
Which happened if packet loss occurs?
In Mission critical service, the packet loss in following case is not acceptable.
  When packet loss happens during the speech packet transmission, the late connected UE may miss/misunderstand the important information from the talker, e.g., command.
  When the packet loss happens during the application level signaling, e.g, in pre-established MBS case, the late connected users will miss e.g., the call request/GroupMapToSession, and unable to join the call or receive the following media via MBS.

## Slide 4
Potential solutions
Options | Brief description | Impacts
A - SA2 | Expose the multicast MBS session status to AF/AS, which enables the AS to activate the MBS session when it is in inactive status. | Changes in SA2: introduce the multicast MBS session status subscription/notification. Impact on SA6: subscribe the multicast MBS session status, activate the inactive MBS session before sending DL data.
B – SA6 solution | Always activate the multicast MBS session before sending DL packet regardless of the MBS session status | Unfeasible solution as the AS is unable to know how long the “silent period” will make the multicast MBS session inactive. The worst case, the AS has to perform the multicast MBS session activation procedure after each silent period no matter how short it is. tremendous burden/signallings exchange on the server as it has to activate the multicast MBS session even if it is already in “active” state No SA2 work.
C – SA6 solution | Repeat the application level signaling several times over the multicast MBS | Burden to the server and UE to handle the redundant packet/message; Cost extra network transmission resources. No SA2 work.
5GC
MCX AS
User A
Joined & CM-IDLE
Multicast MBS
- inactive
1.NOTI
(inactive)
2. Activate MBS
3. MBS activate in 5GC, paging UE etc
4. NOTI
(active)
5. DL media
Option - A
5GC
MCX AS
User A
Joined & CM-IDLE
Multicast MBS
- inactive
Option - B
* N times
Activate MBS for each message/ silent period
5GC
MCX AS
User A
Joined & CM-IDLE
Multicast MBS
- inactive
Option - C
* N time
Message * N
* 1
*2
*N

## Slide 5
Proposals
Option B and C are totally SA6 solutions, but rejected by SA6 due to they are unfeasible at application layer. So they ask SA2 for help.
It is proposed to adopt Option-A, and reply to SA6 along this line.

## Slide 6
Thanks