## Slide 1: Discussion on Roaming UEs to Access the Subscribed Network Using 5G Indirect Network Sharing
China Telecom
3GPP TSG-SA WG2 Meeting #158
21 – 25 August 2023, Gothenburg, Sweden
S2-2309118

## Slide 2: Motivations
As per TR 22.851 [PR 5.4.6-001], Indirect Network Sharing shall support providing services for inbound roaming users of a participating operator.
But the latest standards can’t support above requirement well, especially for scenario that roaming agreement and consequent network interconnection doesn’t exist between hosting operator and home operator.
So, it’s necessary to investigate potential enhancements and scenarios for supporting roaming UEs to access the subscribed network using 5G Indirect Network Sharing, in cases where certain roaming agreements/interconnections may or may not exist.
OP1 and OP3 may or may not have agreement.

## Slide 3: Gap 1
TS 23.501
Figure 4.2.4-3: Roaming 5G System architecture - home routed scenario in service-based interface representation
Figure 4.2.4-1: Roaming 5G System architecture- local breakout scenario in service-based interface representation
GAPs：
As per TS 23.501 roaming architecture, network interconnection must exist between HPLMN and VPLMN. That means participating operator’s partner(HPLMN) must have roaming agreement and network interconnection with hosting operator(VPLMN), which can’t satisfy TR 22.851 [PR 5.4.6-001] requirement.

## Slide 4: Gap 2
TS 23.251
Figure 1: A Gateway Core Network (GWCN) configuration for network sharing. Besides shared radio access network nodes, the core network operators also share core network nodes
GAPs：
GWCN concept can potentially support TR 22.851 [PR 5.4.6-001] requirement, but GWCN currently only supports 2/3/4G sharing, not 5G.
Quotation from TS 23.501 R18: “In this Release of the specification, only the 5G Multi-Operator Core Network (5G MOCN) network sharing architecture, in which only the RAN is shared in 5G System, is supported.”
So, current GWCN specification can’t satisfy TR 22.851 [PR 5.4.6-001] requirement.

## Slide 5: Conclusion and Proposal
Current 5G specifications can’t support roaming UEs to access the subscribed network using 5G Indirect Network Sharing.
Further investigate is necessary for potential enhancements and scenarios.

## Slide 6
Thanks