## Slide 1
China Mobile
SA WG2 Meeting #168 S2-2503534
07 - 11 April, 2025, Goteborg, Sweden
Overall View on 5G-A Rel-20 AIoT

## Slide 2: Overall View on 5G-A Rel-20 AIoT Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1. | Ambient IoT Ph2 | 5G system support for outdoor/roaming use cases and high-end IoT devices (e.g., Type 2 C with DOA capability). Key Work Tasks includes defining - 1. Overall architecture and function enhancement to support for Type C devices and the traffic type of DO-A. 2. Network enhancements for device management, e.g. mobility management and location update, for all types of Ambient IoT devices. 3. Enhancements for roaming. 4. Outdoor services (e.g., Positioning ) | No | SA2 | Yes, Major | SA3 for security, SA5 for charging

## Slide 3
Scenarios and Motivation
  By R19, SA2 has studied network architecture, identifiers, and services to support Ambient IoT indoor application scenarios using low-end Ambient IoT device types without DO-A capability.
  However, SA2 did not study Ambient IoT outdoor application scenarios using high-end IoT devices (e.g., Type-C devices with Do-A capability).
  The study item in Rel-20 is proposed to focus on supporting various outdoor/roaming use cases by using high-end Ambient IoT devices (e.g., Type C devices with DO-A capability).
Proposed Objectives in R20
  Enhancements in architecture, management, and service support for Type C devices and the traffic type of DO-A.
  Enhancements of device management, e.g. mobility management and location, for all types of Ambient IoT devices..
  Study how to manage the devices when the devices move to another PLMN.
  Enhancements to support encryption, authentication, and secure connection of a group of Ambient IoT devices moving between different PLMNs.
  Positioning service
Ambient IoT Ph2