## Slide 1
3GPP TSG SA WG2#169
19-23 May 2025, Fukuoka, Japan
Source: | Samsung
Title: | Protocol Overhead for IMS Voice Transmission over GEO Satellite
Document for: | Discussion
Agenda Item: | 20.1.1
Work Item / Release | FS_5GSAT_Ph4_ARC / Rel-20
Abstract of the contribution: This document discusses the protocol overhead for IMS voice transmission over GEO Satellite.
Compared to S2-2505534, includes the following additions:
the various relationship between L1 rate and codec rate based on the fixed protocol overhead including ROHC header overhead
Summary and way forward proposal
S2-2505534
S2-2505318

## Slide 2: Assumptions
IP Multimedia Subsystem (IMS) client is in the UE and IMS network is in the network
Voice transmission is transferred over IP with potential header compression (e.g., ROHC)
IMS
35,786 km distance from the earth
285ms signal delays
MME
S/P-GW
CP transport: NAS/SRB
UP transport: UP/DRB
UE#1
UE#2
285ms signal delays
S1+EPC: 10ms
EPC
EPC-UE2: 30ms
IMS: 40ms
Protocol Overhead
Codec
Data
ptime (packetization time)
Packetization time (ptime)
The duration of audio represented in a single RTP packet measured in milliseconds (ms)
One packet: Codec data + Protocol Overhead
Two options for delivering voice data that are discussed in SA2
The actual delay depends on the deployments

## Slide 3: Option 1. Voice data transmission over UP/DRB
Overview: Voice data over UP/DRB
Codec Rate | Protocol Overhead | Voice Data | PHY rate
0.6 kbps | 7 B | 6 B | 1.3 kbps
1.2 kbps | 7 B | 12 B | 1.9 kbps
2.4 kbps | 7 B | 24 B | 3.1 kbps
Voice | 
ROHC | 3B*
PDCP | 1B
RLC (UM) | 1B
MAC | 2B
* ROHC: IR state in ROHC, uncompressed RTP/UDP/IP Header to be transferred
Voice data is transmitted over DRB/UP
ROHC is located in eNB
Protocol overhead total 7B for each voice codec data (ptime=80ms)
A-GW
S/P-GW
UE1
UE2
DRB
GTP-U
PHY rate (kbps)
Codec rate (kbps)
ptime: 20ms
ptime: 80ms
ptime: 160ms
ptime: 40ms
Required Physical layer rate
ptime (packetization time)
Protocol Overhead
Codec Data
When the protocol overhead 7B is assumed, at least 1.3 ~ 3.1 kbps physical rate is required for low bit rate codec (for ptime=80)
Chart: PHY rate with 7B overhead
| 0.6 | 1.2 | 2.4
 | 3.4 | 4 | 5.2
 | 2 | 2.6 | 3.8
 | 1.3 | 1.9 | 3.1
 | 0.95 | 1.55 | 2.75

## Slide 4: Option 1a. Voice data transmission over UP/DRB (ROHC 1B)
Overview: Voice data over UP/DRB
Codec Rate | Protocol Overhead | Voice Data | PHY rate
0.6 kbps | 5 B | 6 B | 1.1 kbps
1.2 kbps | 5 B | 12 B | 1.7 kbps
2.4 kbps | 5 B | 24 B | 2.9 kbps
Voice | 
ROHC | 1B*
PDCP | 1B
RLC (UM) | 1B
MAC | 2B
Voice data is transmitted over DRB/UP
ROHC is located in eNB
Protocol overhead total 7B for each voice codec data (ptime=80ms)
A-GW
S/P-GW
UE1
UE2
DRB
GTP-U
L1 rate (kbps)
Codec rate (kbps)
ptime: 20ms
ptime: 80ms
ptime: 160ms
ptime: 40ms
L1 rate vs. Codec rate
ptime (packetization time)
Protocol Overhead
Codec Data
When the protocol overhead 7B is assumed, at least 1.3 ~ 3.1 kbps physical rate is required for low bit rate codec (for ptime=80)
Chart: PHY rate with the protocol overhead (5B per each packet)
| 0.6 | 1.2 | 2.4
 | 6.2 | 6.8 | 8
 | 3.4 | 4 | 5.2
 | 2 | 2.6 | 3.8
 | 1.3 | 1.9 | 3.1
* ROHC header overhead
1) ROHC: IR state in ROHC, uncompressed RTP/UDP/IP Header to be transferred
2) ROHC compressed 1 Byte can be used assuming CID 0 is used.

## Slide 5: Option 2. Voice data transmission over NAS/SRB
A-GW
UE1
UE2
MME
S/P-GW
Voice data over CP NAS
Codec Rate | Protocol Overhead | Voice Data | PHY rate
0.6 kbps | 16 B | 6 B | 2.2 kbps
1.2 kbps | 16 B | 12 B | 2.8 kbps
2.4 kbps | 16 B | 24 B | 4.0 kbps
Voice data is transmitted over SRB/NAS
ROHC is located in MME
Protocol overhead total 18B for each voice codec data (ptime=80ms)
Voice | 
ROHC | 3B*
NAS | 7B**
RRC | 2B
PDCP | 0B
RLC (AM) | 2B
MAC | 2B
* ROHC: IR state in ROHC, uncompressed RTP/UDP/IP Header to be transferred
SRB
S1-AP
Considering NAS layer protocol overhead, it is not appropriate for the IMS voice data transmission
Required Physical layer rate
Chart: PHY rate with a fixe overhead (16B)
| 0.6 | 1.2 | 2.4
 | 7 | 7.6 | 8.8
 | 3.8 | 4.4 | 5.6
 | 2.2 | 2.8 | 4
 | 1.4 | 2 | 3.2
PHY rate (kbps)
Codec rate (kbps)
ptime: 20ms
ptime: 80ms
ptime: 160ms
ptime: 40ms
** NAS overhead can be reduced if NAS reduction is used
Notes: Ptim

## Slide 6: Option 2a. Voice data transmission over NAS/SRB (ROHC 1B)
A-GW
UE1
UE2
MME
S/P-GW
Voice data over CP NAS
Codec Rate | Protocol Overhead | Voice Data | PHY rate
0.6 kbps | 14 B | 6 B | 2.0 kbps
1.2 kbps | 14 B | 12 B | 2.6 kbps
2.4 kbps | 14 B | 24 B | 3.8 kbps
Voice data is transmitted over SRB/NAS
ROHC is located in MME
Protocol overhead total 18B for each voice codec data (ptime=80ms)
Voice | 
ROHC | 1B*
NAS | 7B**
RRC | 2B
PDCP | 0B
RLC (AM) | 2B
MAC | 2B
* ROHC header overhead
1) ROHC: IR state in ROHC, uncompressed RTP/UDP/IP Header to be transferred
2) ROHC compressed 1 Byte can be used assuming CID 0 is used.
SRB
S1-AP
Considering NAS layer protocol overhead, it is not appropriate for the IMS voice data transmission
L1 rate vs. Codec rate
L1 rate (kbps)
Codec rate (kbps)
ptime: 20ms
ptime: 80ms
ptime: 160ms
ptime: 40ms
Chart: PHY rate with the protocol overhead (14B per each packet)
| 0.6 | 1.2 | 2.4
 | 6.2 | 6.8 | 8
 | 3.4 | 4 | 5.2
 | 2 | 2.6 | 3.8
 | 1.3 | 1.9 | 3.1
** NAS overhead can be reduced if NAS reduction is used
Notes: Ptim

## Slide 7: Appendix: 3GPP NAS Protocol Format and Overhead
NAS Message Header Format (as specified in 3GPP TS 24.301 section 8.1)
Field Name | Size | Description
Protocol Discriminator | 4 bits | Identifies the NAS message category (e.g., EMM or ESM)
Security Header Type | 4 bits | Indicates the presence and type of security protection
Message Authentication Code | 4 bytes* | Present if security protection is applied
Sequence Number | 1 byte* | Present if security protection is applied
Message Type | 1 byte | Identifies the specific NAS message
Summary
Security Protection | NAS Header Fields | Header Size
Integrity + Ciphering | PD (4b) + SHT (4b) + MAC (4B) + SN (1B) + MT (1B) | 7 bytes
Ciphering Only | PD (4b) + SHT (4b) + SN (1B) + MT (1B) | 3 bytes
According to TS 24.301, integrity protection is mandatory for NAS signaling, while ciphering is optional. "Ciphering Only" is not explicitly supported or recommended by the 3GPP standard. Most commercial networks always enable integrity protection. |  | 
Notes: Overview:
  The Non-Access Stratum (NAS) protocol, as specified in 3GPP TS 24.301, defines the signaling procedures and message formats exchanged between the User Equipment (UE) and the core network (MME) in the Evolved Packet System (EPS). The NAS protocol operates above the Access Stratum (AS) and is responsible for mobility management, session management, and security procedures

## Slide 8: Observation and a way forward
Observations
  Voice data transmission over User Plane better because UP approach has lesser protocol overhead and requires lesser physical rate to transfer voice data for the same codec rate
  Protocol overhead will impact the requirements for target codec rate also required physical rate
  ptime also can impact to the physical layer rate and codec rate
Proposal for SA2#170
  For further analysis, it is proposed have a consensus on protocol overhead for CP and UP solutions in SA2
    Agree on ROHC overhead at least (in SO state): 3B or 1B
    Agree on NAS/RRC/RLC/MAC protocol overhead including NAS reduction for CP solution
    Agree on PDCP/RLC/MAC protocol overhead for UP solution
Notes: Further consideration
  UP approach requires a bearer setup before transmitting voice data. It requires either
    a pre-established bearer or a dynamically established bearer during call setup procedure.
  If voice service and internet packet service are used simultaneously, a mechanism to prioritize voice service is to be considered. (to compensate the advantage of CP-solution)
  NOTE: The procedure for a dynamical bearer setup may cause additional delay for call setup procedure.