## Slide 1
3GPP TSG SA WG2#169
19-23 May 2025, Fukuoka, Japan
Source: | Samsung
Title: | Protocol Overhead for IMS Voice Transmission over GEO Satellite
Document for: | Discussion
Agenda Item: | 20.1.1
Work Item / Release | FS_5GSAT_Ph4_ARC / Rel-20
Abstract of the contribution: This document discusses the protocol overhead for IMS voice transmission over GEO Satellite
S2-2505318

## Slide 2: Assumptions
This paper assumes following for analysis
  IMS client is implemented in the UE and IMS network is in the operator network.
  Voice transmission is transferred over IP with potential header compression (e.g., ROHC)
IMS
35,786 km distance from the earth
285ms signal delays
SGi
MME
S/P-GW
CP transport option
UP transport option
UE

## Slide 3: Observation #1. IMS voice transmission overhead
The protocol overhead of voice transmission over NAS is significantly higher than the UP-based transmission.
A-GW
UE1
UE2
MME
S/P-GW
Voice data over CP NAS
Voice data over User Plane
Codec Rate | Protocol Overhead | Voice Data | PHY rate
0.6 kbps | 16 B | 6 B | 2.2 kbps
1.2 kbps | 16 B | 12 B | 2.8 kbps
2.4 kbps | 16 B | 24 B | 4.0 kbps
Codec Rate | Protocol Overhead | Voice Data | PHY rate
0.6 kbps | 7 B | 6 B | 1.3 kbps
1.2 kbps | 7 B | 12 B | 1.9 kbps
2.4 kbps | 7 B | 24 B | 3.1 kbps
Voice data is transmitted over SRB/NAS
ROHC is located in MME
Protocol overhead total 18B for each voice codec data (ptime=80ms)
Voice | 
ROHC | 3B*
NAS | 7B
RRC | 2B
PDCP | 0B
RLC (AM) | 2B
MAC | 2B
Voice | 
ROHC | 3B*
PDCP | 1B
RLC (UM) | 1B
MAC | 2B
* ROHC: IR state in ROHC, uncompressed RTP/UDP/IP Header to be transferred
* ROHC: IR state in ROHC, uncompressed RTP/UDP/IP Header to be transferred
Voice data is transmitted over DRB/UP
ROHC is located in eNB
Protocol overhead total 7B for each voice codec data (ptime=80ms)
A-GW
S/P-GW
UE1
UE2
DRB
GTP-U
SRB
S1-AP
Notes: Ptim

## Slide 4: Summary
Based on comparison, voice data transmission over User Plane better because UP approach has lesser protocol overhead and requires lesser physical rate to transfer voice data for the same codec rate.
 | Voice over Control Plane |  |  | Voice over User Plane |  | 
Codec Rate | Protocol Overhead | Voice Data | PHY rate | Protocol Overhead | Voice Data | PHY rate
0.6 kbps | 16 B | 6 B | 2.2 kbps | 7 B | 6 B | 1.3 kbps
1.2 kbps | 16 B | 12 B | 2.8 kbps | 7 B | 12 B | 1.9 kbps
2.4 kbps | 16 B | 24 B | 4.0 kbps | 7 B | 24 B | 3.1 kbps
Notes: Further consideration
  UP approach requires a bearer setup before transmitting voice data. It requires either
    a pre-established bearer or a dynamically established bearer during call setup procedure.
  If voice service and internet packet service are used simultaneously, a mechanism to prioritize voice service is to be considered. (to compensate the advantage of CP-solution)
  NOTE: The procedure for a dynamical bearer setup may cause additional delay for call setup procedure.

## Slide 5: Appendix: 3GPP NAS Protocol Format and Overhead
NAS Message Header Format (as specified in 3GPP TS 24.301 section 8.1)
Field Name | Size | Description
Protocol Discriminator | 4 bits | Identifies the NAS message category (e.g., EMM or ESM)
Security Header Type | 4 bits | Indicates the presence and type of security protection
Message Authentication Code | 4 bytes* | Present if security protection is applied
Sequence Number | 1 byte* | Present if security protection is applied
Message Type | 1 byte | Identifies the specific NAS message
Summary
Security Protection | NAS Header Fields | Header Size
Integrity + Ciphering | PD (4b) + SHT (4b) + MAC (4B) + SN (1B) + MT (1B) | 7 bytes
Ciphering Only | PD (4b) + SHT (4b) + SN (1B) + MT (1B) | 3 bytes
According to TS 24.301, integrity protection is mandatory for NAS signaling, while ciphering is optional. "Ciphering Only" is not explicitly supported or recommended by the 3GPP standard. Most commercial networks always enable integrity protection. |  | 
Notes: Overview:
  The Non-Access Stratum (NAS) protocol, as specified in 3GPP TS 24.301, defines the signaling procedures and message formats exchanged between the User Equipment (UE) and the core network (MME) in the Evolved Packet System (EPS). The NAS protocol operates above the Access Stratum (AS) and is responsible for mobility management, session management, and security procedures