## Slide 1
vivo's view on 6G Native AI Architecture
vivo
2025.08

## Slide 2
Contents
Architectural Motivation
Gap Analysis
Technical Impact
    Overall 6G Native AI Architecture
    Interaction between network functions/services
    IWK & Migration from 5GA AI
  Proposals
    WT scope updates and dependency
    Potential KIs

## Slide 3
Architectural Motivation #1: local decision based on NF’s built-in AI capability
Architectural Motivation: What architectural challenges or opportunities does this WT/KI address?
Architectural Motivation #1:. In 6G AI era with built-in AI/ML capabilities in 6G NF(s), it is worthy to further study whether and how 6G NF leverages AIML to get beyond recommendation rather than statistics/prediction within 6G NF(s), i.e. to do local decision in NF.
Observations:
Usually NWDAF only provides statistics/prediction to consumer, and in R19, AIML_CN further studied whether and how NWDAF additionally to support recommendation, e.g. recommended candidate QoS parameters set.
Recommendation was ruled out in R19 5GA, because only centralized NWDAF is AIML capable and recommendation from NWDAF means it should be aware of NF’s internal service logic, which could have big impact on overall network architecture.
Multi-Objective Optimization
Recommended？
(e.g. recommend QoS parameters set)
Expected Output
(e.g. Service MoS>4)
Fig1: 5G AI/ML supporting statistics/prediction
Fig2: 5G AI/ML additionally supporting recommendation?
Output
(statistics/prediction)
Input data
Inference

## Slide 4
Architectural Motivation #2:Data privacy protection based
on Native AI
Architectural Motivation: What architectural challenges or opportunities does this WT/KI address?
Architectural Motivation #2: In 6G AI era with built-in AI/ML capabilities in 6G NF(s), the NFs will be involved on demand to execute the AI task in a distributed manner i.e. the NFs only need to expose intermediate AI data/information instead of raw data
Observations:
Quite a few use cases have been defined for AI in specs (TS 23.288, 23 cases), but few of them are commercial deployed. One of main reasons is that NWDAF can not gather enough raw data with high quality from data sources, e.g. UE/OAM/CN NFs and AF due to data privacy concerns as shown in Fig 1.
In 5GA, HFL and VFL have been defined to resolve this issue relying on distributed AI among NWDAFs and/or AF. However, they still can’t solve the problem completely, because NFs as data sources may still not provide raw data to NWDAFs as shown in Fig 2.
In addition, the data available for 5G AI is insufficient in terms of quantity and diversity. For example, 3GPP cannot standardize all the input data exhaustively as vendor are not willing to expose their local data.
Fig 1: 5G centralized AI
Fig 2: 5GA distributed AI (e.g. HFL, VFL)
Raw data
NWDAF
UE
RAN
CN NFs
AF
…
NWDAF
NWDAF
NWDAF
AF
Raw data
UE
OAM
CN NFs
AI NF
Fig 3: 6G : Native AI

## Slide 5
Architectural Motivation #3: Service QoE assurance for connectivity service based on native AI
Observations:
For 5G AI, PCF without AI can only statically maps service requirement to QoS parameters for connectivity service, considering the statistics or prediction from NWDAF, which does not work well;
NWDAF can only provide statistics/prediction and cannot perform any decision making on behalf of PCF as NWDAF has no service logic of PCF
UE
RAN
CN
(e.g.UPF)
DN
observed =1.2
observed =0.4
observed =1
UE Local decision on X based on h1
PCF
app codec
RSRP
GBR
MBR
MPLR
expected =0.9
GBR
…..
PDB
expected =2
expected =1
expected =1.2
observed =2
1.2
0.9
1
2
Expected QoE：4.6
Distributed inference
PCF local decision on hi based expected QoE
In 6G era, with the given Expected QoE,
PCF (with AI capability) locally decides the related QoS objectives for UE, RAN, CN for connectivity service;
UE/RAN/CN (with AI capability) locally decides QoS parameters and takes local actions in a collaborative manner.
Connectivity service requirement/intent
RAN Local decision on X based on h2

## Slide 6
Observations:
User’s service is extended to include comprehensive requirements(e.g. Hybrid-modes service), it may have requirements on computing, sensing in addition to communication
User’s service QoE are also extended, it may be impacted by communication QoS, computing QoS and sensing QoS.
With the given the expected QoE, AI agent + NFs with built-in AI capability are to further perform
Task deconstruction (AI agent in NW): expected QoE-> communication service objective + computing service objective + sensing service objective
Hybrid service QoS decision(NF with AI capability): with the corresponding service objectives, performs local decision to derive the service policy/QoS profiles. e.g. for connectivity, computing and sensing service respectively.
Architectural Motivation #4: Service QoE assurance for Hybrid Service based on native AI
observed
NW AI agent
Computing service domain
…..
…..
expected
Sensing service domain
Connectivity service domain
Hybrid Service requirement/intent
CMF
Computing nodes
SCF
Sensing entities
Expected QoE matrix
PCF local decision on hi based expected QoE
Connectivity local model output
Computing local model output
Sensing local model output
observed
expected
observed
expected
Local/collaborative decision on computing parameters X based on h2
Local/collaborative decision on sensing parameters X based on h3
Local/collaborative decision on connectivity parameters X based on h1
PCF
(for connectivity)
…..

## Slide 7
Gap Analysis: Limitations on 5G AI
Gap Analysis: What are the limitations or gaps in existing architecture (from Rel-15 to Rel-20) that this proposal aims to resolve?
5G NWDAF(Network Data Analytics Function) provides analytics to consumers e.g. 5GC NFs to assist intelligent procedures
Data collection framework for AIML in 5G
  DCCF (Data Collection Coordination Function) is to coordinate data collection to avoid duplication data collection
  ADRF(Analytics Data Repository Function) is to store and retrieve the collected data and analytics
  MFAF (Messaging Framework Adaptor Function) is a logical Messaging Framework to improve the data exchange
Limitations of 5G AI
  Only NWDAF has AIML capability and other 5G NF has no AIML capability
  NWDAF only provides statistics/prediction to NF consumer, which will be taken into account by NF consumer to make decision
  Data collection framework for AIML is defined ,which is not extended to support other cases e.g. energy efficiently
  NWDAF communication with RAN is not supported
NEF
NWDAF
AF
PCF
AMF
SMF
UPF
Nnef
Nnwdaf
Naf
Npcf
Namf
Nsmf
N4
UDR
Nudr
CHF
Nchf
OAM
RAN
UE

## Slide 8
Technical Impact: Overall 6G Native AI Architecture
UE data
reporting
/exchange
Key Features：
Uniform
AI agent
Data Repository
Function
Data Control
Function
UP Function
Computing
Function
Sensing Function
eSBI/ABI for Control Plane
DBI for data plane
AI
AI
AI
Data Process
Function
CP Function
AI
Data Framework
AI
AI
AI
RAN data reporting
UPF Functionality
(e.g. UPF QoS，FAR，PDR)
AI inference
AI coordination
AI decision making
AI training
AI performance monitoring
AI capability
Data collection and transfer (internal and external)
Data/cache storage
Data capability
Requirement analysis
tasks scheduling
AI inference
Uniform AI coordination
AI decision making
AI training
AI performance monitoring
Data collection and transfer (internal and external)
Data/cache storage
Data capability
Service intent interpreting
Tasks scheduling
User/UE intent
Requirement
analysis
Fig 3:Internal structure of NF/entities with AI capability
Fig 2: Internal structure of AI agent
Fig 1: 6G Native AI architecture --- Built-in AI capability in all entities(on demand)
Service requirement from other entity
Service requirement from AI agent
Centralized AI agent is to support: service intent interpreting, requirement analysis, tasks deconstruction and scheduling.
6G entities(e.g. UE, RAN and NF) equipped with built-in AI capability on demand, which provides internal assistance (e.g. local decision) for their basic functionalities based on request from AI agent or other entity.
Both AI agent and 6G entities with built-in AI capability support AI related services: AI decision making, AI training, AI inference and performance monitoring, which can be invoked by consumers.
Uncertain and comprehensive service request from user can rely on AI agent’s analysis and orchestration, but traditional deterministic processes (e.g. registration and SM procedure) can also be independent of AI agent, i.e., allowing a fallback to using only entities with AI capability.
All of AI related intermediate data/information exchange, including ML models, are based on data plane capability

## Slide 9
Technical Impact: Definition of 6G Native AI capability Levels
Level 1: 6G Architecture with built-in AI capability (NF local AI in use)
Level 2: 6G Architecture with built-in AI capability and AI agent
(local AI+ data/model/result/AI services interacting with other NF)
Level 3: 6G Architecture with built-in AI capability and AI agent
(collaborative decision making for task across UE/RAN/Core )
Level 0: 6G Architecture with built-in AI capability (AI not in use )
Key point: Native AI is only a basic architecture design that inherently supports AI capabilities, it allows the network and devices to still work normally without operating AI (i.e. fall back to legacy mechanisms ).

## Slide 10
Technical Impact: 6G services and Native AI
Day1 6G Native AI = 6G with build-in AI capability + partially AI based service(s)
Service Types | Possibility of Day1 Feature
AIML assisted connectivity services | AI based QoS/Policy Yes Instead of NF’s internal rule based static strategy, high chance to generate QoS/policy with assistance of built-in AI capability
 | AI based SM/MM Probably Possible to combine with AI to improve the efficiency and performance of basic MM/SM process, e.g. paging, RA configuration for UE (TBD).
 | ….
AIML assisted beyond connectivity services (e.g. sensing, computing) | Case by case - Computing service may combine well with AI natively; - For 6G sensing, day 1 may focus on basic features definition. Lately leverage AI to improve the service performance and efficiency by using the native AI capabilities within each 6G entities.
Key points for 6G Native AI:
6G Architecture is designed with built-in AI capability from day 1 and easily to support any new service for future proof.
Partial 6G service(s) could be based on AI from day 1.

## Slide 11
Technical Impact: 6G UE with AI capability
(for open discussion )
AI agent
AI capability
Data storage
Data collection and transfer
(internal and external)
e.g. user intent/APP intent
a. UE intent
UE
e.g. APP intent
e.g. UE intent
Option 1: UE modem invokes independent AI capability module on demand to perform local AI.
Option 2: UE modem uses embedded AI capability to perform local AI actions.
Option 1/2: Interaction between AP module and UE modem , interaction between UE modem and data plane module, and interaction between UE modem and AI capability in option 1, can be standardized in 3GPP.
Option 1/2: Whether and how AP module coordinates with AI agent is out scope of 3GPP.
NAS (e.g. MM, SM)
AS (e.g. RRC,)
AI inference
AI decision making
AI training
AI performance monitoring
Service intent interpreting
Tasks scheduling
Requirement
analysis
User intent
b. App/user intent
UP
UE AP module
UE Modem
AI coordination
AI agent
AI capability
Data storage
Data collection and transfer
(internal and external)
e.g. user intent/APP intent
a. UE intent
NAS (e.g. MM, SM)
AS (e.g. RRC,)
User intent
b. App/user intent
UP
UE AP module
UE Modem
AI capability
UE
Option 2:UE modem with built-in AI capability/agent
Option 1:UE modem and independent AI capability/agent
…
…

## Slide 12
Technical Impact：IWK & Migration from 5G AI
Technical Impact: How would this WT/KI influence:
Interworking or migration from 5G to 6G?
Considerations on IWK & migration from 5G to 6G
It is propose to develop 6G Architecture with the support of native AI/ML, which will consider AI/ML related work in SA2 and other related working groups, e.g. AI/ML lifecycle framework and data collection framework.
  In 5GA, R15-R18 eNA (enablers for Network Automation) is a pre-study for AIML in SA2, which is to study and specify how to collect data and feed back data analytics to the network, but AI/ML algorithm is not in the scope
  In R19 and R20 , SA2 FS_AIML_CN is to further investigate and identify potential architecture enhancements to support AI/ML including AI based positioning, VFL, signaling storm prevention and UE data collection for UE side model training
In case of interworking and inter-system change between 5G and 6G, how to handle AIML activities e.g.
  6G with AI to 5G without AI
  6G with AI to 5G with AI

## Slide 13
Proposals: WT scope updates and dependency
WT scope
Dependency on WT#1.1 (e.g. New NAS) and WT#1.2 (e.g. SBA enhancement, QoS framework for AI service).
Dependency on WT#5, e.g. AI related data collection, distribution, AI results exposure and AI model delivery over 6G data plane.
WT dependency
It proposes to keep WT#3 scope as it is:
WT#3: Study how to support and enable use of AI in 6G (e.g. AI agent, framework).
NOTE 4: The term AI agent refers to the general concept of agents autonomously performing tasks on behalf of users, systems, and/or applications. As the SA1 work is still in progress, adapting the definition of AI agent from SA1 and the use of the term AI agent will be determined as part of the study. AI agent does not imply any specific solution.
Notes: WT#4: Study the integration of Sensing and Communication over 3GPP access, considering the sensing modes to be supported and other sources of sensing data.
NOTE 5: The detailed scope of WT#4 will be determined considering the scope and work of R20 FS_Sensing_ARC.

## Slide 14
Proposals: Potential KIs
Potential KIs
Key Issue #X: Study how to support and enable native AI for Network (i.e. AI4NET) in 6G, including:
AI native architecture for 6G system
  6G Architecture supports for native AI using, e.g. distributed AI with built-in AI capability 6G entities and/or uniform AI agent
  How to support interaction among e.g. built-in AI capability 6G entities and/or uniform AI agent
  Whether and how to support connectivity services and/or beyond connectivity services assisted by AI , and how to fall back to legacy mechanisms i.e. procedures without AI
How to use unified data collection framework to support AI related activities e.g. data collection, data storage, data exposure, data privacy and security management, model sharing/delivery, etc.
  Note: UE data collection in 5GA and 5GC data collection framework for AI/ML will be considered
Whether and how to define unified AI framework across SA/RAN e.g. Unified AI terminology/feature and Unified AI lifecycle management
How to support multi-vendors AI Model sharing among 6G NFs and/or UE.

## Slide 15
THANK
YOU