## Slide 1
vivo’s view on 6G Data Framework
2025.08

## Slide 2
Contents
Architectural Motivation
Gap Analysis
Technical Impact
    Overall 6G Architecture for data framework
    Interaction between network functions/services
    IWK & Migration from 5GC data collection architeture
  Proposals
    WT scope updates and dependency
    Potential KIs

## Slide 3
Architectural Motivation: Common Data Framework for multiple purposes in 6G
Data category | Data provider | Data Consumer | Data volume
Sensing data collection (e.g. measurement) | UE, RAN | CN, RAN, UE | Related to use cases: e.g. data rate of measurement is about 10Mbps for objects creating hazards on roads
AI/ML data collection (e.g. UE side model, network model) | CN, RAN, UE, AF | CN, RAN, UE | Related to AI model: e.g. the data volume is about 10k bytes to 100M bytes. For RAN/CN data collection, see TR38.843 and TS 23.288 respectively.
Energy Efficiency | UE,RAN,CN,OAM | CN,OAM,UE | Related to use cases e.g. could be similar to data volume for charging
Network Exposure in core network | 5GC NF, AF | 5GC NF, AF | Related to use cases, in 5. 20, TS 23.501, and clause 4.15, TS 23.502
… | … | … | 
5G
UE
MDT/SON/AI
NF
DCCF
CN: AI + Energy
UE
gNB
Positioning/AI/
Energy Saving
CN:LMF/
MTLF/SF
AF
…
NEF
gNB
OAM
UE
OTT Server: AI
gNB
CN
AI
Network Exposure
…
6G
Energy Saving
Sensing
/Positioning
6G
UE
Data provider
Data consumer
A unified data life cycle management
Key Aspects:
  Common data framework to improve data collection/exposure efficiency and avoid duplication data collection
  UE data visibility/controllability is essential for user consent as the user only consent the fully visible data reporting
  Network and UE on-demand access to the common data service.

## Slide 4
Gap Analysis: Limitations on 5GC data collection architecture for AI
Gap Analysis: What are the limitations or gaps in existing architecture (from Rel-15 to Rel-20) that this proposal aims to resolve?
5GC data collection architecture：
  DCCF(Data Collection Coordination Function) is to coordinate data collection signaling (e.g. data request/subscription, data response/notify) between data consumers and data sources;
  Message framework is to receive and distribute data from data sources to data consumer according to DCCF’s control;
  Data can be stored to ADRF on demand.
Fig1: Data Collection architecture for AI using DCCF in 5GC
Limitations:
  Data collection architecture was only defined for AI use cases, other services, e.g. LCS, energy service are not applicable.
  The data source is only CN NF/OAM and does not include RAN or UE.
  The data consumer is only CN NF (i.e. NWDAF) or OAM and does not include RAN or UE.
  SBA HTTP protocol based on JSON format is not very efficient for massive data transmission.
  Data authorization, security and privacy, and data preprocessing are fragmented, which are performed in different nodes, e.g. NEF, DCCF, ADRF.

## Slide 5
Technical Impact: Overall 6G data framework
Fig: Common data framework in 6G architecture
AI agent
Data Repository
Function
Data Control
Function
UP Function
Sensing Control
Function
Sensing Process
Function
eSBI/ABI/xBI for Control Plane
RAN AI/Sensing Data
UE AI/Sensing Data
AI
AI
AI
Data Process
Function
AI
RAN(e.g. Sensing entity )
UE
CP Function
AI
DBI for Data Framework
AI
Key Features：
Common data framework to support multiple purposes e.g. AI/ML or Sensing service related data handling, including data collection, data storage, data exposure, data privacy and security management, model sharing/delivery, etc;
New functions are introduced at least including Data Control Function, Data Processing Function and Data Repository Function;
Sperate data signaling control and data transmitting/processing with standardized eSBI interface between them;
New Data based interface ( i.e. DBI) can be defined for data framework, data sources and data consumers access to the data framework using DBI;
New protocol for efficient data transferring and exposing can be defined for DBI;
UE can be data source and also can be data consumer of the data framework.

## Slide 6
Technical Impact：IWK & Migration from 5G data collection
Technical Impact: How would this WT/KI influence:
Interworking or migration from 5G to 6G?
Considerations on IWK & migration from 5G to 6G
6G native data framework is a completely new architecture for data handling for multiple purpose e.g. AI and Sensing and expected to be non-backward compatible with 5GA architecture;
It is proposed to develop 6G Architecture with the native support of common data framework, which will take 5G existing related work in SA2 into account.
  In 5G, R17 eNA Ph1(enablers for Network Automation) was a pre-study for AIML in SA2, which studied and specified how to collect/expose data using DCCF, MFAF and NEF;
  In R19, SA2 AIML_CN is to further investigate and identify potential architecture enhancements to support UE data collection for UE side model training.
  In R20, SA2 AIML_CN_Ph2 could be further extended to investigate and identify potential architecture enhancements to support ML model parameters or training data set for two sided model.
  In R20, SA2 FS_ISAC is also to investigate how to collect and transfer sensing related data from RAN.

## Slide 7
Proposals: WT scope updates and dependency
WT scope
Dependency on WT#1.1 (e.g. New NAS) and WT#1.2 (e.g. SBA enhancement, QoS framework, network exposure framework).
Dependency on WT#3, 4, e.g. AI and Sensing related data collection, distribution, data or sensing results exposure over 6G data plane.
WT dependency
It proposes to keep WT#5 scope as it is:
WT#5: Study data framework for all aspects related to efficient and scalable data handling including, for example, data collection, distribution, processing, storage, data access and data exposure, with consideration of access control/user consent and privacy where relevant. The example of data may include data for AI and Sensing. This WT can also study any potential enhancements on system and procedure needed for user consent framework.
NOTE 6: The work split with SA3, SA5 and RAN WGs will require TSG coordination
Notes: WT#4: Study the integration of Sensing and Communication over 3GPP access, considering the sensing modes to be supported and other sources of sensing data.
NOTE 5: The detailed scope of WT#4 will be determined considering the scope and work of R20 FS_Sensing_ARC.

## Slide 8
Proposals: Potential KIs
Potential KIs
Key Issue #X: Study how to enable native data framework in 6G, including:
Architecture design to support efficient and scalable data handling including data collection, distribution, processing, storage for multiple services, e.g. AI and Sensing.
Study how to support massive data transferring/exposing between data source(s) and data consumer(s).
  How to enable data service consumed by UE, 6G NF(s) or 3rd party AF on demand.
How to ensure data visibility/controllability and user consent.
How to differentiate the traffic for data framework and the UE regular traffic.

## Slide 9: Thank you