## Slide 1: Study on IMS Architecture Enhancement NWM Discussion Summary
Pallab Gupta, Nokia (Moderator)
S2-2506691
3GPP TSG-WG SA2 Meeting #170
Goteborg, Sweden, 25-29 August, 2025

## Slide 2: Study on IMS Architecture Enhancement Moderator summary from NWM
NWM discussion was conducted between 27-June to 12-Aug, 2025
  This report lists the key technical areas to be potentially studied based on company inputs collected through NWM
  The technical areas listed in this report does not reflect any consensus to study them. It only identifies the key technical areas for further discussion on scoping of the WTs for the study on IMS Architecture Enhancement
  The report also provides a summary of initial company views on each of the technical areas identified, wherever inputs were available.
  Companies listed in this report against a specific category/view is based on the moderator‘s interpretation from the NWM comments.

## Slide 3: WT#1: Whether and how to simplify and enhance the IMS architecture
1. Merging control plane, media plane entities
Simplify/optimize the IMS control plane by e.g., converging P/S/I-CSCF
Simplify/optimize the IMS media plane by e.g., converging MF, MRF and IMS-AGW.
3. Enhancements on the ISC interface
Simplification of the iFC mechanism for service triggering. How to support dynamic triggering of AS and efficient AS chaining without unnecessary anchoring to unused servers.
Enhance the redundancy and flexibility on the ISC interface and to study the introduction of an IMS AS “set” concept to improve AS resiliency and scalability.
How to reduce SIP dependency towards AS by migration to SBI in close coordination with 5G new calling and Data Channel services’ evolution.
4. Security
Investigate alternatives to avoid the second authentication in IMS as the core network has authenticated UE (this would probably need co-ordination with SA3).
Security enhancement to P-CSCF to eliminate the core network breach risk for traffic coming from internet, such as wireline access.
2. Modernize IMS architecture
Modernize IMS architecture and procedure for control plane and media plane entities, by supporting SBI, QUIC, Agent2Agent (A2A), MCP (Model Context Protocol)
Interworking and migration between the legacy IMS and the new enIMS.
Based on the inputs in NWM the WT#1 can be overall grouped into 4 categories as below:

## Slide 4: WT#1: Whether and how to simplify and enhance the IMS architecture
 | Some supporting comments | Some comments with concerns
1. Merging control plane, media plane entities | "Having multiple control plane NF entities i.e. I/P/S-CSCF bring heavy cost of signaling procedures and complexity of new service deployment“ "Multiple media plane NF entities, i.e. IMS-AGW, MF, MRF not only complicates the media negotiation and establishment procedures but also creates conflicts.“ Proposing companies: Boost Mobile, KPN, China Mobile, Huawei, ZTE, China Telecom, vivo, MediaTek, NEC, AT&T, DT, China Unicom | "In the IMS implementation, some IMS network entities can be combined or collocated to simplify the deployment and procedures" "Standard does not prevent collocating these CSCFs. Similarly different kind of GWs also can be combined without any standardization impact“ "It is unclear what the actual problems are being described, a lot of the “asks” can be solved via implementations (e.g. CSCF can be combined, media functions can be combined)“ Companies raising concerns: Ericsson, Qualcomm, Samsung, Verizon, TMO USA, Nokia, Apple,
2. Modernize IMS architecture | "Modernize and simplify the IMS network architecture and procedures for the control plane and media plane NFs, protocols and Call flows including SBA, Cloud and AI native network with SBI, QUIC, A2A(Agent2Agent), MCP(Model Context Protocol)" "Study how remaining Diameter interfaces (i.e., Cx, Dx, Sh, Zh, ) can be replaced by Service-Based Interfaces (SBI) to modernize communication protocols and simplify integration (e.g. to run IMS in containers).“ Proposing companies: Vivo, NEC, DT | "The design of the existing access agnostic IMS architecture based on the SIP protocol took many releases to complete. We have some concerns that changes to IMS architecture will introduce the need for interworking and migration procedures that will further increase complexity. In real deployments, IMS functionalities can be collocated that could simplify the procedures.“ "IMS remains the 3GPP platform to provide multimedia services and shall remain G- and access-agnostic, using the same architecture, procedures and protocols for any kind of access, including wireless access of any generation, WLAN access, Wireline access and NTN. The UE to IMS network interface as well as interfaces between IMS networks shall remain backward compatible and based on SIP RFCs.“ Companies raising concerns: Apple, Nokia, Qualcomm, Samsung, Ericsson

## Slide 5: WT#1: Whether and how to simplify and enhance the IMS architecture
 | Some supporting comments | Some comments with concerns
3. Enhancement on ISC Interface | "IMS relies on the iFC (initial Filter Criteria) mechanism for service triggering. Based on the iFC mechanism, any AS which may potentially be used during the call shall be triggered when every SIP message in the call is received by the S-CSCF….. This may lead to waste of network resources since the invoked AS may not be used at all during the call...“ "Current ISC relies on S-CSCF receiving a FQDN in initial Filter criteria from HSS and then S-CSCF using DNS to determine AS(s) to be associated with a registration / new session. DNS based load distribution is not good enough.“ Proposing companies: Boost Mobile, KPN, China Mobile, Huawei, ZTE, China Telecom, TMO USA, vivo, MediaTek, NEC, AT&T, DT, China Unicom, Nokia* | "We need clarification on what is meant by iFC simplification. This is quite ambiguous. What is the problem that we are trying to address or solve here.“ "Changes to IMS internal interfaces must be clearly and duly justified (e.g. replacing SIP at ISC or replacing H.248).“ Companies raining concerns: Ericsson, Nokia (for replacing SIP at ISC),
4. Security | "to develop quantum safe algorithms in 6G, with a resulting need to replace all exiting secure hardware modules used for user authentication - it would be beneficial to investigate alternatives to the full up second authentication of IMS once the core network has been authenticated....“ "focus more on network security. Specifically, the security enhancement to P-CSCF to eliminate the core network breach risk for traffic coming from internet, such as wireline access.“ Proposing companies: AT&T, TMO USA, DT | 

## Slide 6: WT#2: Whether and how to enhance the IMS architecture and procedures to support new services. The output of this work task shall be independent of WT#1.
1. Native AI support in IMS
Introduce AI capabilities into the operators network and offer new AI service in the 6G era.
How to support new AI services defined by SA1 e.g., personal AI assistant, language translation, intelligent immersive calling etc.
How to invoke capabilities offered by the 6G core (computing, sensing, data framework, etc.) and AI capabilities that are provided by the 3rd party
How to support the transmission, understanding, generation, synchronization, and transcoding of multi-modal data in IMS network.
How to support multi-modality network rendering in the IMS network.
2. Support for new types of devices
How to support terminals that do not support the full IMS stack, such as wearables, augmented reality (AR) glasses, and robotics can leverage IMS networks.
3. Exposure enhancements
enhance the exposure of the IMS media layer to AI systems that can monitor and adapt the actual voice/video or other media service supported by IMS, according to the ”realtime” conditions experienced by the user.
exposure of IMS capabilities to leverage the NEF in all cases so as to open up further development of IMS services either inside the PLMN or alongside 3rd parties.
Based on the inputs in NWM the WT#2 can be overall grouped into 3 categories as below:

## Slide 7: WT#2: Whether and how to enhance the IMS architecture and procedures to support new services. The output of this work task shall be independent of WT#1.
 | Some supporting Comments | Some comments with concerns
1. Native AI support in IMS | "In addition, use cases like personal AI assistant service might also need to invoke the AI capabilities that are provided by the 3rd party. For example, personal AI assistant service needs to interact with 3rd party’s AI agents to book a flight and/or a hotel for its subscriber." "Many 6G use cases defined in SA1 leverage AI capabilities. It is important to introduce AI capabilities into the operators’ network and offer new AI service in the 6G era, e.g. UE AI agent to IMS AI agent communication.“ “There are many 6G use case scenarios utilizing AI capabilities are defined in SA1. However, current standardized IMS architecture only covers human-controlled session control. AI has to be invocable both inside the operator’s domain (e.g., voice enhancement, live transcription) and externally (e.g., cloud AI platforms) without breaking SIP/IMS session control principles.” “Immersive and multi-modality communication would need assistance from the network side, e.g., network rendering, modality transformation, media generation etc” Proposing companies: Boost Mobile, KPN, China Mobile, Huawei, ZTE, China Telecom, Oppo, Verizon, NEC, DT, Turkcell, Orange, Nokia | "Even if UE include AI agents and if Applications and/or IMS include AI agents keeping the standard SIP based UE to network interface is key to keep IMS access agnostic and to have a deterministic UE and network behaviour allowing interoperability tests." "In general, the existing IMS architecture can already support variety of data channel-based media processing capabilities e.g., AR and Avatar communication. Any potential SA2 modifications for the new services (such as supporting of AI based media processing) are expected to be alignment CRs, leveraging mechanisms like SA4 WID and TEI20. " "After enhancing the IMS architecture to provide data channel we think various kind of services can be addressed but would be interested to know some specific service which is not possible with existing framework. Regarding introducing AI to IMS architecture, we would like first to understand what is missing from the current IMS specifications and see the progress in 6G and once it gets some good progress then we can consider may be in next release if the proposed scenarios is not for 6G Day 1 service.“ Companies raising concerns: Qualcomm, Samsung

## Slide 8: WT#2: Whether and how to enhance the IMS architecture and procedures to support new services. The output of this work task shall be independent of WT#1.
 | Some supporting comments | comments with concerns
2. Support for new Types of devices | “Various new types of terminals have been introduced in 3GPP TR 22.870 [1] to support corresponding use cases. For examples, immersive calling would require AR glasses; AI agent collaboration involves robots; intelligent home requires multiple sensors. However, not all new terminals that would support full IMS stacks, e.g., SIP/SDP. ” “The expectation is that new UE types would not need to support full IMS stack and would not require to support SIP but could still connect to IMS to directly work with Service platforms like 5G new calling services. Or to interconnect with SIP to provide a common set of services (for that an interworking is needed)” Proposing companies: Boost Mobile, KPN, China Mobile, Huawei, ZTE, China Telecom, Oppo, Verizon, NEC, DT, Turkcell, Orange | 
3. Exposure enhancements | “We support enhancing the exposure of the IMS media layer to AI systems that can monitor and adapt the actual voice/video or other media service been supported by IMS, according to the ”realtime” conditions been experienced by the user.” “Currently, there is little or limited exposure of IMS capabilities. In the future, mobile network operators may be interested in offering API-related services of their IMS capabilities in a coherent and coordinated manner between IMS and 6GC.” Proposing companies: TMO USA, DT, Turkcell, NEC |