## Slide 1: Discussion on AIoT Device ID length extension
Huawei, HiSilicon
3GPP TSG-WG SA2 Meeting #170
Goteborg, SE, 25th Aug – 29th Aug, 2025
S2-2507272

## Slide 2
EPC ID lengths can vary from 64 to 496 bit
The RFID EPC length refers to the number of bits used to represent the EPC code in an RFID tag.
The EPC length can vary from 64 bits to 496 bits.
EPC memory more than 128 bit is supported by many RFID chipset manufactures
Refences:
https://www.as-rfid.com/info/rfid-epc-length-what-you-need-to-know-79904550.html
https://www.atlasrfidstore.com/rfid-insider/rfid-tag-basics-what-is-high-memory/#:~:text=*%20TegoCHIPXM%208k%20(EPC%20496%20bits%2C%20User,Track%20(EPC%20448%20bits%2C%20User%20256%20bits)
RFID IC’s most popular memory (more than 128 bit) options (2)
EPC memory option | RFID IC
EPC 160 bits | UCODE 12C
EPC 224 bits | UCODE DNA, UCODE DNA City
EPC 256 bits | Impinj Monza 4i, UCODE G2iM
EPC 448 bits | UCODE DNA Track, UCODE 7XM
EPC 496 bits | Impinj Monza 4E, Tego Edge Tag/Chip Combo, TegoCHIPXM 1k

## Slide 3
Identification for healthcare and logistics products requires long Identifiers
Healthcare product
Unique Device Identification (UDI) is used to identify the medical product, including UDI-DI and UDI-PI
Example of label containing UDI
Source: https://www.gs1.org/industries/healthcare/udi
Label example
from GS1.org
Trade Item
Trade item, such as a pallet, both a GTIN and an SSCC may be used. making it possible to track the logistic unit in transit
Example of Trade Item Barcode
Coding length of the example UDI: ~ (26*4 + 40*8) = ~424 bit
Data Delimiters | Identifier | Data Type | HR Field Size | DB Field Size | Example Data
(01) | Device Identifier (DI) | Numeric | 16 | 14 | 51022222233336
(11) | Manufacturing/Production Date | Numeric | 8 | 6 (YYMMDD) | 141231
(17) | Expiration Date | Numeric | 8 | 6 (YYMMDD) | 150707
(10) | Batch/Lot Number | Alphanumeric | 22 | 20 | A213B1
(21) | Serial Number | Alphanumeric | 22 | 20 | 1234
Data Delimiters | Identifier | Data Type | DB Field Size | Example Data
(02) | GTIN | Numeric | 14 | 05412345678909
(37) | COUNT | Numeric | 2 | 64
(10) | BATCH | Numeric | 6 | 879654
(00) | SSCC | Numeric | 18 | 254123400897650024
Coding length of the example Trade Item data:
~ (40*4) = ~160 bit
Source: https://www.gs1us.org/resources/data-hub-help-center/about-the-serial-shipping-container-code-sscc

## Slide 4
Proposal of AIoT Permanent ID length option extension
Observation 1:
Healthcare industry uses UDI as product identifier, whose length normally exceeds 200 bit
Observation 2:
Trade Item Barcode can use composite GS1 AI (GTIN + SSCC), and the coding length is the combination of the coding length for each individual GS1 AI
Observation 3:
Current Ambient IoT Permanent ID length options (i.e. 96 bit or 128 bit) cannot meet the requirement of above-mentioned use cases.
Observation 4:
RFID chipset supports high memory, and the most popular length options are 256 bit, 496 bit
Feasibility consideration
RAN1 agreed a maximum TB size of around 1000 bits in PHY for R2D and D2R directions can be supported.
In case that Identification Information within the AIoT Device Permanent ID length is 496 bit, the corresponding filtering information is assumed less than 600 bit, which does not exceed maximum TB size.
Proposal:
Based on the analysis, it is proposed to update the length options of the Identification Information to support
96, 128, 256 bit, 496 bit

## Slide 6
TS 23.269 defines AIoT Device Permanent ID and its structure includes the “Identification Information”, similar to RFID tag EPC Identifier .
The supported lengths of Identification Information are 96 bit or 128 bit.
TS 23.003 has specified the two type of Identification Information
The bit 4 and bit 3 (of ID type) indicates the type of Identification Information:
- (value 00) the type of Identification Information contains an Electronic Product Code (EPC), as defined in clause 14 of GS1 TDS Release 2.1
- (value 01) the type of Identification Information contains an unstructured information
Current agreements on AIoT Device Permanent ID
Identification Information supports 96/128 bit length, and EPC/unstructured information type