## Slide 1: R20 AIoT key issue 1 conclusion way forward
Huawei, OPPO (rapporteurs)

## Slide 2
Key issue 1 progress after SA2#172, Oct 2025
Current situation
Key issue 1 has already used the 0.5 TU planned in the SID, and not been completed yet.
Guidance from SA2 Chair
For this, and the other studies that are due to complete in November we (SA2) will need to discuss during the November work planning sessions how to handle the situation if parts of a study are not complete.
Down-scoping is one option. Continuing some study work in February is another option, but requires agreement in SA2 and an understanding of where the additional TU(s) will come from (from the normative budget for that item, or from the buffer, for example).
Allocating additional time for 5G Advanced studies in November over and above the budget will be challenging

## Slide 3
Overall consideration of key issue 1 conclusion in future meeting
General principles
Very limited time will be allocated to discuss the remaining issues, i.e. editor’s notes in the TR
For each editor’s note, conclusion options are listed (see next slides).
If consensus cannot be reached, the feature will be dropped
Nov meeting workplan
Rapporteurs provides the conclusion options before the meeting and collects the feedback from all companies
Use the drafting session to discuss companies’ feedback and decide the conclusion way forward
Endorse the conclusion way forward for Feb meeting
Feb meeting workplan
Finalize key issue 1 conclusion within very limited time, based on the endorsement in November meeting

## Slide 4
Handling of editor’s notes
Conclusion aspect | Editor’s note | Open issue(s) description
UE reader authorization and revocation | Whether and what additional subscription information for the UE Reader is needed is FFS. | Two more subscription data for further discussion (other proposals were dropped): Validity information: valid time duration and area that allowed for UE to act as an AIoT Reader AF ID information indicating that the UE reader belongs to the designated AF
Conclusion options:
Option 1: not to support additional subscription information
>> LGE, Huawei, CATT, ZTE, sony, OPPO, Qualcomm
Option 2: agree “Validity information”: valid time duration and area that allowed for UE to act as an AIoT Reader
>> Samsung. CMCC, Lenovo, Tejas NW, Ericsson, Interdigital, ZTE, vivo, Futurewei, Docomo
Option 3: agree “AF ID information” indicating that the UE reader belongs to the designated AF
>> CMCC, Lenovo, Ericsson, Nokia, Interdigital, vivo, Sony, OPPO, Futurewei, Docomo
Rapporteurs’ proposal: option 3
Endorsement: option 1

## Slide 5
Conclusion aspect | Editor’s note | Open issue(s) description
UE reader authorization and revocation | Whether to inform the UE about the authorization information is FFS. | Two options have been discussed Option 1: YES. UE need to got authorization result, similar like other legacy features e.g., ProSe, V2X Option 2: NO. UE is authorized or not is controlled by whether it can get radio resource from RAN. RAN will decide based on authorization indication from CN, together with UE reader radio capability, available radio resource in the serving cell.
Conclusion options:
Option 1: yes. UE needs to be informed of the authorization information, i.e. authorized indication.
>> interdigital, vivo, CATT, ZTE, OPPO, Samsung, Lenovo, Docomo
Option 2: no. UE does NOT need to be informed of the authorization information
>> LGE, Ericsson, Huawei , Nokia, Futurewei, Qualcomm
Handling of editor’s notes
Rapporteurs’ proposal: option 1
Endorsement:
SA2 does not agree to pursue it further at this point of time.

## Slide 6
Conclusion aspect | Editor’s note | Open issue(s) description
UE reader authorization and revocation | Whether UE reader capability is provided to AMF is FFS. | Two UE reader capability have been discussed: UE MM capability, provided from UE to AMF via NAS. AMF based on UE subscription information in the UDM, and the UE MM capability, to authorize or revoke the UE as reader UE radio capability, provided from UE to RAN, and RAN provides it to AMF. AMF based on the UE radio capability, and available radio resource in the UE serving cell, to authorize or revoke the UE as reader NOTE: UE radio capability can be left to RAN WG to decide
Conclusion options:
Option 1:agree “UE MM capability”, indicating UE is capable to operate as AIoT reader, provided by UE to AMF
>> Sony, Tejas NW, Samsung, Interdigital, ZTE, Futurewei, Huawei, Ericsson, Docomo, vivo, CATT, Nokia, OPPO, Lenovo, Spreadtrum, QC, LGE
Option 2: agree “UE radio capability”, indicating the supported frequency bands used to AIoT operation, provided by RAN to AMF
>> LGE
Handling of editor’s notes
Rapporteurs’ proposal: option 1
Endorsement: option 1, “UE radio capability”, can leaves to RAN decision

## Slide 7
Conclusion aspect | Editor’s note | Open issue(s) description
UE reader selection | How to select UE reader(s) based on the AF provided area information is FFS | SA2#171 discussed two UE reader types: (1) fixed UE reader (2) mobile UE reader. In case that AF provided area information, the open issue is: Whether and how to select the mobile UE reader?
Conclusion options:
(question clarification: AF only provides area, no UE reader ID)
Option 1: only fixed UE reader will be selected
>> OPPO, Huawei, Ericsson, NEC, CATT, Lenovo, Futurewei
Option 2: both fixed and mobile UE reader selected
>> LGE, Interdigital, ZTE, Samsung, Sony, Nokia, Xiaomi, Tejas NW, Philips, Qualcomm
Rapporteurs’ proposal: option 1
Handling of editor’s notes
Endorsement:
If only area information is provided by AF, how to select the UE reader will not be defined by SA2.

## Slide 8
Conclusion aspect | Editor’s note | Open issue(s) description
AIOTF Discovery and Selection for UE reader ID | How to discover and select AIOTF when AF provides UE reader ID is FFS | When AF provides the UE reader ID e.g. GPSI to the NEF, how the NEF selects the AIOTF based on the AF input (e.g. translate GPSI to SUPI)? Due to the lack of time, the solution are not discussed in the study phase. From all the proposed solutions, two candidate options : Query UDM Query NRF
Conclusion options:
Option 1: NEF query the UDM
>> LGE, Nokia, Interdigital, OPPO, Samsung
Option 2: NEF query the NRF
>>
Handling of editor’s notes
Rapporteurs’ proposal: option 1
Endorsement: option 1

## Slide 9
Conclusion aspect | Editor’s note | Open issue(s) description
UE reader ID allocation | Whether and how to allocate the UE reader ID | Open issue 1: what identifier is used to identify UE reader by UE, RAN, and CN NF? Option 1: existing UE identifier, like NG-AP ID or GPSI; Option 2: new identifier (AIoT specific UE ID) Open issue 2: how to allocate the UE reader ID? (Dependency on UE reader selection) Option 1: allocated by AIOTF Option 2: allocated by AMF
Open issue 1, conclusion options:
Option 1: existing UE identifier (UE NG-AP ID)
>> Interdigital, Sony, Tejas NW, Huawei, Ericsson (only mobile UE reader case), Nokia, Samsung, OPPO, CATT, QC, LGE
Option 2: new UE identifier
>> LGE
Open issue 2, conclusion options:
Option 1: allocated by AIOTF
Option 2: allocated by AMF
>> LGE
Handling of editor’s notes
Rapporteurs’ proposal: UE NGAP ID is used as UE reader ID
Endorsement: option 1, and coordination with RAN3 is needed.

## Slide 10
Summary of endorsement in SA2#172
Conclusion aspect | Editor’s note | Endorsed way forward in SA2#172
additional subscription information | Whether and what additional subscription information for the UE Reader is needed is FFS. | Not to support additional subscription information
UE reader authorization and revocation | Whether to inform the UE about the authorization information is FFS. | SA2 does not agree to pursue it further at this point of time.
UE reader authorization and revocation | Whether UE reader capability is provided to AMF is FFS. | Agree to support “UE MM capability”, i.e. indicating the UE is capable to operate as AIoT reader. It is provided by UE to AMF. Whether to support “UE radio capability”, will leave to RAN decision.
UE reader selection | How to select UE reader(s) based on the AF provided area information is FFS | If only area information is provided by AF, how to select the UE reader will not be defined by SA2.
AIOTF Discovery and Selection for UE reader ID | How to discover and select AIOTF when AF provides UE reader ID is FFS | NEF query the UDM, by providing the UE identity, to get the serving AMF of UE. NEF selects the AIOTF based on the mapping information of AMF and AIOTF locally configured.
UE reader ID allocation | Whether and how to allocate the UE reader ID | In case that AF provided UE ID to the NEF, AMF UE NG-AP ID and AMF set ID is used to identify the UE reader between NG-RAN and AIOTF. Coordination with RAN3 is needed.