## Slide 1: 3GPP SA2 Discussion Paper Open Issues for LIPA and SIPTO @ Local Network
Agenda: 8.4 / LIMONET
Source: NEC
S2-122311

## Slide 2: LIPA vs. SIPTO@LN
LIPA
  A new service that enables users to access content in the Local Network (Home/Enterprise)
  LIPA is a new end-user service
SIPTO@LN
  A feature that enables the mobile operator to offload “selected IP Traffic” in the Local Network (i.e. reduce the traffic load towards the core network
  SIPTO@LN is a new operator feature

## Slide 3: Release 11 Status for LIPA Mobility
Architecture 1 | Architecture 2
Basic Principles | 
UE establishes dedicated LIPA PDP context to L-GW L-GW selection is done by the CN based on APN | L-GW, located on Iuh/S1 path, offloads traffic of LIPA or SIPTO enabled bearers using NAT (transparently to UE) Resp. L-GW is dynamically preconfigured on H(e)NB via HMS
For Further Study issues: | 
How tunnels between the H(e)NBs and the L-GW are established How to secure the Gn/S5 tunnel Handover procedures over the Sxx interface Discovery of LIPA mobility area | Whether it is a deployment issue to have only a single L-GW per LHN Whether there is a security or reliability concern to route all traffic through the L-GW
   Current working assumption: Architecture 1 will be used as baseline for “LIPA mobility”

## Slide 4: Stage 1 Requirements for SIPTO
TS 22.101
It shall be possible to perform Selected IP Traffic Offload for pre-Release 10 UEs.
TS 22.220
The SIPTO policies may be defined per APN or per IP flow:
  SIPTO policies per APN indicate whether all traffic associated with a specific APN is subject to offload;
  SIPTO policies per IP flow are routing policies indicating which APN to use for a specific IP flow. The Operator may provide routing policies to the UE that assist the UE in routing the IP flows towards an appropriate APN. This is applicable for UE regardless of whether or not it has established IP connectivity to the local enterprise/residential network.
The mobile operator shall be able to configure the SIPTO policies either statically or dynamically.

## Slide 5: Release 11 Status for LIPA Mobility
LIPA service from UE perspective – Architecture 1
SGSN
HNB
HNBGW
GGSN
UE
IP Point of Presence (Default APN)
L-GW
IP PoP (LIPA APN)
Traffic Offload Policies
and enforcement
UE maintains separate PDN connections – one for Operator provided services and one for LIPA – and has 2 IP addresses.
Traffic routing (i.e. PDN connection selection) in UE can be solved because Local Network has a dedicated IP sub-network and normal IP routing functionality can be applied.
Arch-1:
Home / Enterprise Network
PDN Connection
UE Requirements:
Support to handle multiple simultaneous PDN Connections
Support for normal IP routing functionality

## Slide 6: Release 11 Status for LIPA Mobility
HNB
SSGN
GGSN
UE
HNBGW
L-GW
LIPA service from UE perspective – Architecture 2
UE requires only a single PDN connections and has only 1 IP addresses.
L-GW routes LIPA traffic (i.e. traffic destined to the local subnet) to the local network (transparently to the UE).
Arch-2:
Home / Enterprise Network
UE Requirements:
No specific functionality needed
Traffic Offload Policies and enforcement
LIPA
IP Point of Presence (Default APN)

## Slide 7: Release 11 Status for SIPTO@LN
SIPTO@LN service from UE perspective – Architecture 1
SGSN
HNB
HNBGW
GGSN
UE
IP Point of Presence (Default APN)
L-GW
SIPTO@LN (SIPTO APN)
Traffic Offload Policies
and enforcement
UE maintains separate PDN connections for Default APN and SIPTO APN and has 2 IP addresses.
IP flow routing (i.e. PDN connection selection) must be handled by UE based upon operator policies.
Arch-1:
Home / Enterprise Network
UE Requirements:
Support to handle multiple simultaneous PDN Connections
Support for operator-controlled IP flow routing functionality (i.e. to assign IP flows to PDN connections)  New functionality defined in OPIIS?
Internet

## Slide 8: Release 11 Status for SIPTO@LN
HNB
SSGN
GGSN
UE
HNBGW
L-GW
SIPTO@LN
SIPTO@LN service from UE perspective – Architecture 2
UE requires only a single PDN connections and has only 1 IP addresses.
IP flow routing (i.e. traffic offload functionality) is provided by the L-GW based on operator policies (transparently to the UE)
Arch-2:
Home / Enterprise Network
Internet
UE Requirements:
No specific functionality needed
Traffic Offload Policies and enforcement
IP Point of Presence (SIPTO enabled APN)

## Slide 9: Conclusions
Facts:
There is no mandatory requirement for pre-Rel-10 UEs to support …
  multiple simultaneous PDN connections
  functionality to assign IP flows to PDN connections based on operator policies (scope of OPIIS Rel-12)
It cannot be assumed that pre-Rel-10 UEs support (1) + (2)
Conclusion:
If operators want to offer/use SIPTO@LN services for pre-Rel-10 UEs (current Stage 1 Requirement!), then one solution that does not involve specific UE functionality is required
Architecture 1 option for Standalone L-GW is not suitable for SIPTO@LN with pre-Rel-10 UEs
Proposals:
Take this discussion paper and conclusion into account in the architecture discussion for SIPTO@LN in Rel-12
To satisfy the stage-1 requirements for SIPTO@LN, standardize either:
  a single solution that has no UE impacts, or
  a basic solution without UE impact + a future solution with the relevant UE functionality
If companies do not agree with the stage-1 requirements, an LS to SA1 to clarify the requirement must be sent

## Slide 10: Why SIPTO@Macro does not require special UE functionality?
eNB
S-GW
P-GW
UE
Local S/P-GW
UE requires only a single PDN connection – as all the traffic can be routed to a Local P-GW
The operator can still have full control on how each IP flow is routed at the Local P-GW
 This is different to the SIPTO@LN case, where the network “beyond” the L-GW cannot be controlled by the Mobile Operator
RAN
Internet
UE Requirements:
No specific functionality needed
Traffic Offload Policies and enforcement
Operator Services