## Slide 1: ECN based UPCON Notification Solutions
Source: Sprint
April 8, 2013
SA WG2 Meeting #96 S2-130831
San Diego, CA, USA - 8 -12 April, 2013

## Slide 2: Congestion Notification and Mitigation Process
3GPP UPCON Architecture and Scope
Operator O&M
Congestion Detection
Congestion Notification& reporting
Congestion Mitigation (policy rules, enforcement)
remediation
eNB
P-GW
PCRF/PCEF

## Slide 3: Congestion Detection
Network entities
  eNB detects congestion based on preset threshold (e.g. percent usage)
  Other network entities may detect congestion
Solution
  IETF 3168 Explicit Congestion Notification (ECN), Active Queue Management (AQM) concept
    Queues know themselves best – let them actively manage queue congestion detection
    detects congestion before queue overflow
    allows routers to separate policies for queuing or dropping packets from policies for indicating congestion

## Slide 4: Congestion Notification & Reporting
Network Entities
  EPC entities, e.g. eNB, MME, S-GW, P-GW, optionally UE
Level of granularity?
  Per Flow, Per UE, EPS entities
Three levels of Notifications
  Simple Notification – All congestion will use IETF RFC 3168 ECN.
  Proxied Simple Notification – This function allows for the P-GW or eNB to proxy ECN functionality when an end-point (a UE) does not support ECN but the other IP endpoint supports ECN. This allows the framework to support legacy device (e.g. non ECN supporting capable devices).
  Entity Notification – This may be delivered by a number of options, e.g. GTP-U header delivery, eNB to MME communication.
Three levels of reporting
  Simple Notification Reporting – Extending PCC Rule filters in PCRF to process ECN related information.
  Entity Reporting – Integration of the Entity Notifications into the PCC in such a manner minimize the impact on adding signalling to PCRF.
  Correlation Reporting – Reports and combination of data in order to facilitate correlation and isolation of congestion.

## Slide 5: Congestion Mitigation
Congestion Mitigation is intends to relieve the immediate congestion issue
Utilizing existing PCC interface and procedures to report congestion.
  For examples, Online Charging (Ro), threshold monitoring (Gx) or usage reporting (Gx),
PCRF or OCS receives congestion indication and information, then perform correlate and isolate congestion.
PCRF will select the mitigation policy for the derived congestion issue and enforce mitigation policy.

## Slide 6: Congestion Remediation
Congestion remediation is an added value of Congestion Management. It is an operational and maintenance function to resolve the underlying congestion issues. Some examples of remediation action are:
  cell split / small cell is necessary
  Gating control
  Limitation of session admission

## Slide 7: ECN Limitations
Issues:
  Many devices do not have ECN capability, this is a major limitation as it will take year for ECN support to become widely supported. A UE CAN detect ECN support from an end point because it signals ECT (ECN Capable Transport) upon the first connection set up
  Not all operator’s network entities have ECN capability
  Black holes in the intermediate routers (i.e. backhaul)
Solutions:
  For issue 1: UE Proxy at the eNB, P-GW proxy for the other end point
  For issue 2: mandate support of ECN (RFC 3168) within EPC (i. e. between eNB and P-GW, including backhaul routers)
  For issue 3: operators mandate ECN support in its network including backhaul to avoid ECN black holes

## Slide 8: UPCON Requirements
The EPC entities (i.e. S-GW, P-GW) shall transfer the RAN congestion indication and information from the eNB to the PCRF/PCEF.
The granularity of congestion indication shall include but not limited to subscriber, IP flow, and network entity.
The P-GW shall receive the RAN UPCON information and provide the RAN UPCON information to PCRF/PCEF.
The PCRF shall process the RAN UPCON information and select and enforce policy rule to address the congestion.
The RAN UPCON notification shall not add additional signalling to the network
The eNB and P-GW may act as congestion indication proxies to support UE that doesn’t have the congestion indication capability.
The EPC entities shall support congestion indication.

## Slide 9: Extension of mitigation policy
Possible extensions
  Extend bandwidth limitation to Per-Flow, e.g. limit ADC identified video SDF has per flow limits but not aggregate limits
  Allow service specific action in Rules, especially ADC rules
    Allows PCC to use service specific actions for an Application ID, e.g. Content-Type ‘Video’ may have

## Slide 10: Summaries
An UPCON management process was described.
RAN UPCON notification solution was proposed based on IETF RFC 3168 ECN.
ECN limitations were identified and solutions provided to overcome these limitations.
UPCON requirements were listed.
Extensions of mitigation policy were introduced.