## Slide 1: Discussion on UE behaviour after rejecting Non UE detectable emergency call in IMS
NTT DOCOMO, Qualcomm Inc.
Deutsche Telekom, SOFBANK MOBILE, NSN, Sharp, NEC, Fujitsu, Hitachi
TSG SA WG2 Meeting#99
23-27 September 2013, Xiamen, China
S2-133545
(Revision of S2-133307)

## Slide 2: Background
In a specific deployment where IMS emergency call is not supported in the network, operator (P-CSCF) is given a choice to reject the incoming call with 380 (Alternative Service).
  E.g., LTE network supports VoLTE but not IMS emergency or operator supports IMS emergency and needs SRVCC
SIP 380 can include XML to indicate that the alternative service type is ‘emergency’
  And UE moves to CS domain when rejected

## Slide 3: Problem
Current TS23.167 has two contradicting statements
  Subclause 7.1.2 and H.2
It is unclear which procedure the UE performs in the CS domain, after being rejected with 380:
  Non UE detectable emergency call; or
  UE detectable emergency call

## Slide 4: TS23.167 – Subclause 7.1.2
In the case that the P-CSCF detects that this is a request to establish an emergency session, based upon operator policy
  P-CSCF may reject the session initiation request [.. Rest is omitted]
    if a dialled number is available, attempt to initiate a call to the dialled number in the CS domain as follows
      For systems based on TS24.008, the ME and/or (U)SIM may contain emergency numbers [..]
      If the dialled number is not on the ME and/or (U)SIM [..] the UE will attempt a normal call.

## Slide 5
UE
P-CSCF
MSC
Non UE detectable Emergency call: Subclause 7.1.2 behaviour illustrated
Initiate Emergency Call
INVITE (normal call)
380 (Alternative Service), which includes “emergency” indicator
UE check if the call being initiated is Non-UE detectable or detectable
If Non-detectable:
INVITE (emergency call)
If detectable:
Setup (normal call)
If Non-detectable:
Emergency Setup
If detectable or if there is no dialed number:
UE check if the dialed number is Non-UE detectable or detectable in the CS domain
Reselect 2G/3G

## Slide 6: TS23.167 H.2
A bit contradicting text exists… which reads UE always perform emergency call (i.e. Emergency Setup) in CS domain.
    “If the UE initiates a non UE detectable emergency session, and the session initiation request is rejected by the P CSCF with an indication that this is an emergency session, the UE shall select a domain according to the requirements for domain priority and selection in clause H.5 and attempt an emergency call on that domain (i.e. a UE detectable emergency session or a CS emergency call).”

## Slide 7
UE
P-CSCF
MSC
Initiate Emergency Call
INVITE (normal call)
380 (Alternative Service), which includes “emergency” indicator
UE check if the call being initiated is Non-UE detectable or detectable
If Non-detectable:
INVITE (emergency call)
If detectable:
Emergency Setup
Perform domain selection as in 23.167 Annex H.5
Non UE detectable Emergency call: Subclause H.2 behaviour illustrated
INVITE (emergency call)
If PS domain is selected:
If CS domain is selected:

## Slide 8: Requirements 1
In Japan there’s a national regulation to allow user to add “prefix” (184 or 186) to indicate whether user wants to show his/her number to PSAP
  184: don’t show caller’s number
  186: show caller’s number (explicit indication)
This type of call in CS domain MUST be non-UE detectable emergency call using normal SETUP message because as CS Emergency Setup cannot have:
  Dialed digits
  Any category or IE to express the presence of 184 / 186
The call in CS domain MUST be non-UE detectable emergency call
Using normal SETUP message.

## Slide 9: Requirements 2 ?
Requirements *may* exist in some regions which demands the UE to perform “UE detectable emergency call” using EMERGENCY SETUP message in CS domain, after “Non UE detectable emergency call” is rejected by 380 in IMS domain.

## Slide 10: Analysis
On H.2:
  If this behaviour is used, then the Japanese regulation cannot be fulfiled as 184/186 prefix cannot be delivered.
  In addition, for some operators in the EU, some emergency calls may be mis-routed for emergency numbers not stored on the USIM if the call is retried in the CS domain as an emergency call without the dialed number.
  This behavior may be needed if the dialed digits identify a common emergency service with no additional information (e.g. 911 in US, 999 in UK) but is not valid for all operators.

## Slide 11: Related topic…
CT1 agreed on the following CR
7.1.2 anyway needs to be corrected to allow for domain selection as in annex H.5 – e.g. in case an sos URN is included in the 380 response.

## Slide 12: Proposal
Three alternatives exist for retrying an emergency call after receipt of a 380 response for an initially undetected IMS emergency call.
Alt1:  Corresponds to DOCOMO CR
  correct that text in TS23.167 H.2 so that UE supports the behaviour specified in section 7.1.2 when the CS domain is selected.
  correct the text in 7.1.2 to allow for domain selection as in H.2
  To make sure that the UE performs “dialled number / emergency number mapping” if the UE moves to the CS domain, after the non UE detectable call in IMS domain is rejected with 380
Alt2:  Corresponds to Qualcomm CR
  P-CSCF to indicate the UE in 380 whether UE shall re-attempt “Detected” or “Non Detected” emergency in CS domain if the CS domain is selected
Alt.3:  Corresponds to RIM CR
  If the CS domain is selected, UE to perform Emergency Setup if Emergency URN is indicated in 380; else do the behaviour specified in 7.1.2

## Slide 13: Alt.1 Illustrated
UE
P-CSCF
MSC
Initiate Emergency Call
INVITE (normal call)
380 (Alternative Service), which includes “emergency” indicator
UE check if the call being initiated is Non-UE detectable or detectable
If Non-detectable:
INVITE (emergency call)
If detectable:
Setup (normal call)
If Non-detectable:
Emergency Setup
If detectable or if there is no dialed number:
UE check if the dialed number is Non-UE detectable or detectable in the CS domain
Perform domain selection as in 23.167 H5. If CS domain selected:

## Slide 14: Alt.2 Illustrated
UE
P-CSCF
MSC
Initiate Emergency Call
INVITE (normal or emergency)
380 (Alternative Service), which includes “emergency” indicator + new IE
If the new optional IE is included in 380:
Normal Setup using the dialled number
When the optional new IE doesn’t exist, or there’s no dialled number
Emergency Setup, even if UE cannot detect the number
Perform domain selection as in 23.167 H.5. If CS domain selected:

## Slide 15: Alt.3 Illustrated
UE
P-CSCF
MSC
Initiate Emergency Call
INVITE (normal or emergency)
380 (Alternative Service), which includes “emergency” indicator (+ emergency URN)
Else:
Normal Setup using the dialled number
Reselect 2G/3G
If (URN exists in 380 and corresponds to a CS domain emergency service) or (there is no dialed number) or (the dialed number is detected in the CS domain):
Emergency Setup
Reselect 2G/3G
Perform domain selection as in 23.167 H.5. If CS domain selected:

## Slide 16: [Added on 24 Sept] Alt.4
Alt.1-3 all indicate “emergency” to the UE
But then UE is aware it’s emergency
  So it’s no longer a UE Non-Detected emergency but UE detected emergency.
    Complex UE logic is required to convert “detected emergency” into “non detected”
The requirement discussed in this paper can be rephrased as:
  Reject Normal Call and re-attempt it in CS domain
New alternative
  P-CSCF doesn’t indicate ‘emergency’ to the UE in 380
  Introduce a new XML body (details for Stage 3) to just indicate that ‘UE re-attempt in CS domain’

## Slide 17: [Added on 24 Sept] Alt.4 Illustrated
UE
P-CSCF
MSC
Initiate Emergency Call
INVITE (normal)
380 (Alternative Service), which includes “normal CS call” indicator
Normal Setup using the dialled number
Reselect 2G/3G (CS domain)
Quick analysis
The very complex emergency call logic the UE can remain untouched
New logic is needed, but that should be straightforward (no need to do dialled number analysis etc. Just re-attempt the call in CS domain)
Protocol impact is there, but can be minimal (just add a new type in XML body)
Maybe used for other scenarios as well, if network want to ask UE to re-attempt any normal call in the CS domain for whatever reasons e.g. IMS not working, congestion,
Depending on Local policy

## Slide 18: Conclusion
It is proposed to SA2 to discuss
  Whether “Requirement 2” exists; and
  the solution alternatives  People happy with ALT.4!?
Whichever option is selected, CT1 update would still be needed also.
  7.1.2 and Annex H needs to be corrected to the new domain selection logic and treatment of a returned sos URN in a 380 response
    Except for Alt 3, the sos URN could be ignored if the CS domain is selected.
It may also be useful to send a LS to CT1 to clarify SA2’s ‘intentions’ ….