3GPP TSG-SA WG3 Ad Hoc Meeting 	( S3-090555

# Sophia-Antipolis, France, 23-26 Mar 2009

| CR-Form-v9.4 |
| --- |
| CHANGE REQUEST |
| ( | 33.401 | CR | 0202 | ( rev | - | ( Current version: | 8.3.1 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( | X | ME |  | Radio Access Network | x | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correction of KeNB derivations |
| --- | --- |
| Source to WG: ( | China mobile, Alcatel Shanghai Bell, ZTE, Nokia Corporation, Nokia Siemens Networks |
| Source to TSG: ( | SA3 |
| Work item code: ( | SAES |  | Date: ( | 12/03/2009 |
| Category: ( | F |  | Release: ( | Rel-8 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) |
| Reason for change: ( | As it is described that KeNB derives from KASME and NAS COUNT in Figure 6.2-3, It’s a confused description since KeNB is derived from uplink NAS COUNT, not from downlink NAS COUNT. |
| Summary of change: ( | Correction of KeNB derivations in EPS key hierarchy. |
| Consequences if ( not approved: | Ambiguous description of KeNB derivations causing confusion. |
| Clauses affected: ( | 6.2 |
|  | Y | N |  |  |
| Other specs ( |  |  | Other core specifications ( |  |
| affected: |  |  | Test specifications |  |
|  |  |  | O&M Specifications |  |
| Other comments: ( |  |

================= START OF FIRST CHANGE 1==================

## 6.2	EPS key hierarchy

Requirements on EPC and E-UTRAN related to keys:

a)	The EPC and E-UTRAN shall allow for use of encryption and integrity protection algorithms for AS and NAS protection having keys of length 128 and for future use the network interfaces shall be prepared to support 256 bit keys.

b)	The keys used for UP, NAS and AS protection shall be dependent on the algorithm with which they are used.

c)	As part of the initial attach request from the UE, ME shall signal the UE security capabilities to the MME.

Figure 6.2-1: Key hierarchy in E-UTRAN

The key hierarchy (see Figure 6.2-1) includes following keys: KeNB, KNASint, KNASenc, KUPenc, KRRCint and KRRCenc

KeNB is a key derived by UE and MME from KASME when the UE goes to ECM-CONNECTED state or by UE and target eNB during eNB handover.

Keys for NAS traffic:

- KNASint is a key, which shall only be used for the protection of NAS traffic with a particular integrity algorithm This key is derived by UE and MME from KASME , as well as an identifier for the integrity algorithm using the KDF as specified in Annex A.

- KNASenc is a key, which shall only be used for the protection of NAS traffic with a particular encryption algorithm. This key is derived by UE and MME from KASME,,as well as an identifier for the encryption algorithm using the KDF as specified in Annex A.

Keys for UP traffic:

- KUPenc is a key, which shall only be used for the protection of UP traffic with a particular encryption algorithm. This key is derived by UE and eNB from KeNB, as well as an identifier for the encryption algorithm using the KDF as specified in Annex A.

Keys for RRC traffic:

- KRRCint is a key, which shall only be used for the protection of RRC traffic with a particular integrity algorithm. KRRCint is derived by UE and eNB from KeNB, as well as an identifier for the integrity algorithm using the KDF as specified in Annex A.

- KRRCenc is a key, which shall only be used for the protection of RRC traffic with a particular encryption algorithm. KRRCenc is derived by UE and eNB from KeNB as well as an identifier for the encryption algorithm using the KDF as specified in Annex A.

Intermediate keys:

- NH is a key derived by UE and MME to provide forward security as described in clause 7.2.8. The NH is sent by the MME to the eNB using S1signalling.

- KeNB* is a key derived by UE and eNB when performing an horizontal or vertical key derivation as specified in clause 7.2.8 using a KDF as specified in Annex A.

Figure 6.2-2 shows the dependencies between the different keys, and how they are derived from the network nodes point of view. Figure 6.2-3 shows the corresponding relations and derivations as performed in the ME.

Figure 6.2-2: Key distribution and key derivation scheme for EPS (in particular E-UTRAN) for network nodes. The basic derivations are covered in the figure, but derivations performed at,
e.g. inter-RAT mobility is not shown.  Two dashed input to a KDF means one of the input is taken depending on condition met.

Figure 6.2-3: Key derivation scheme for EPS (in particular E-UTRAN) for the ME.
The basic derivations are covered in the figure, but derivations performed at,
e.g. inter-RAT mobility is not shown. Two dashed input to a KDF means one of the input is taken depending on condition met.

As the figures 6.2-2 and 6.2-3 show, the length of KASME and KeNB is 256 bits, the length of  NH is 256bits, and 256-bit NAS, UP and RRC keys are always derived from KASME and KeNB respectively. In case the encryption or integrity algorithm used to protect NAS, UP or RRC requires a 128-bit key as input, the key is truncated and the 128 least significant bits are used.

NOTE: Figures 6.2-2 and 6.2-3 do not include the key handling branches for forward security. This is described in clause 7.2.8 and Figure 7.2.8.1-1.

The function Trunc takes as input a 256-bit string, and returns a truncated output as defined in Annex A.7.

================= END OF FIRST CHANGE1 ==================

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

# Text boxes

NH

KDF

256

128

256

Trunc

KUPenc

KUPenc

KDF

KeNB*

256

256

Physical cell ID, EARFCN-DL

256

UP-enc-alg,

Alg-ID

RRC-int-alg,

Alg-ID

RRC-enc-alg,

Alg-ID

256

256

128

128

256

256

Trunc

Trunc

KRRCint

KRRCenc

128-bit

keys

KRRCint

KRRCenc

256-bit

keys

KDF

KDF

NAS UPLINK COUNT

NAS-int-alg,

Alg-ID

NAS-enc-alg,

Alg-ID

256

256

256

128

128

256

256

Trunc

Trunc

KNASint

KNASenc

128-bit

keys

KNASint

KNASenc

256-bit

keys

KDF

KDF

KDF

KDF

256

KASME

KeNB

network-ID

256

256

KDF

Ks

Trunc

128

256

256

KUPenc

KUPenc

KDF

KeNB*

eNB

eNB

KeNB

256

Physical cell ID, EARFCN-DL

256

256

UP-enc-alg,

Alg-ID

RRC-int-alg,

Alg-ID

RRC-enc-alg,

Alg-ID

256

256

128

128

256

256

Trunc

Trunc

KRRCint

KRRCenc

128-bit

keys

KRRCint

KRRCenc

256-bit

keys

KDF

KDF

NAS UPLINK COUNT

NAS-int-alg,

Alg-ID

NAS-enc-alg,

Alg-ID

256

256

256

128

128

256

256

Trunc

Trunc

KNASint

KNASenc

128-bit

keys

KNASint

KNASenc

256-bit

keys

KDF

KDF

KDF

KDF

256

KASME

KeNB

network-ID

256

256

KDF

Ks

HSS

MME

ME

256

KeNB

NH

256

KeNB

NH

NH

KDF