3GPP TSG-SA WG3 Meeting AdHoc meeting 	(S3-090557

# Sophia Antipolis, France, 23-26 March 2009

| CR-Form-v9.4 |
| --- |
| CHANGE REQUEST |
| ( | 33.401 | CR | 0204 | ( rev | - | ( Current version: | 8.3.1 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME | X | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correction of EPS AS/NAS Security Context definition |
| --- | --- |
| Source to WG: ( | China Mobile, Nokia Corporation, Nokia Siemens Networks |
| Source to TSG: ( | SA3 |
| Work item code: ( | SAES |  | Date: ( | 18/02/2009 |
| Category: ( | F |  | Release: ( | Rel-8 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) |
| Reason for change: ( | As the Next Hop (NH) parameter and Next Hop Chaning Counter (NCC) parameter used for KeNB derivation, they are used for AS communication during handover and can be stored in eNodeB. So the two parameters should belong to EPS AS security context instead of EPS NAS security context. |
| Summary of change: ( | Added NH and NCC in EPS AS security context definition and delete them from EPS NAS security context definition. Related descptions in specification are updated. |
| Consequences if ( not approved: | Unclear specification causing confusion about NH and NCC. |
| Clauses affected: ( | 3.1, 7.2.6.3, 7.2.8.4.3 |
|  | Y | N |  |  |
| Other specs ( |  | N | Other core specifications ( |  |
| affected: |  | N | Test specifications |  |
|  |  | N | O&M Specifications |  |
| Other comments: ( |  |

## ********************** start change 1**********************************

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in TR 21.905 [1], in TS 33.102 [4] and the following apply. A term defined in the present document takes precedence over the definition of the same term, if any, in TR 21.905 [1].

Access Security Management Entity: entity which receives the top-level keys in an access network from the HSS. For E-UTRAN access networks, the role of the ASME is assumed by the MME

Activation of security context: the process of taking into use a security context.

Authentication data: Data that is part of a security context or of authentication vectors.

Chaining of KeNB: derivation of a new KeNB from another KeNB (i.e., at cell handover)

Current security context: The security context which in a given system (E-UTRAN or UTRAN/GERAN respectively) with a registered UE has been taken into use by the given system most recently. Note that, in E-UTRAN, a current security context originating from a mapped context may exist simultaneously with a native context, while, in UTRAN/GERAN, only one security context can exist at a time. A current security context exists in MME and SGSN respectively whenever a UE is registered. When the UE is simultaneously registered with both, MME and SGSN, then current EPS and UMTS security contexts exist simultaneously.

ECM-CONNECTED state:  This is as defined in TS 23.401 [2]. The term ECM-CONNECTED state corresponds to the term EMM-CONNECTED mode used in TS 24.301 [9].

ECM-IDLE state: As defined in TS 23.401 [2]. The term ECM-IDLE state corresponds to the term EMM-IDLE mode used in TS 24.301 [9].

EPS-Authentication Vector: KASME, RAND, AUTN, XRES

EPS security context: A state that is established between a user and a serving network domain. At both ends "EPS security context data" is stored, that consists of the EPS NAS security context, and the EPS AS security context.

EPS AS security context: the cryptographic keys at AS level with their identifiers, the Next Hop parameter NH, the Next Hop Chaining Counter parameter NCC used for next hop access key derivation, the identifiers of the selected AS level cryptographic algorithms and counters used for replay protection. Note that the EPS AS security context only exists when the UE is in ECM-CONNECTED state and is otherwise void.

NOTE: NH and NCC need to be stored also at the MME during connected mode.

EPS NAS security context: This context consists of KASME with the associated key set identifier, the keys KNASint and KNASenc, the UE security capabilities, the identifiers of the selected NAS integrity and encryption algorithms, and the uplink and downlink NAS COUNT values. In particular, separate pairs of NAS COUNT values are used for cached and mapped EPS NAS security contexts, respectively.The distinction between native and mapped EPS security contexts also applies to EPS NAS security contexts.

Legacy security context: A security context which has been established according to TS 33.102 [4].

Mapped security context: Security context created by converting the current security context in the source system to a security context for the target system in inter-system mobility, e.g., UMTS keys created from EPS keys.

Native EPS security context: An EPS security context whose KASME was created by a run of EPS AKA.

Re-derivation of NAS keys: derivation of new NAS keys from the same KASME but including different algorithms (and no freshness parameter)

Refresh of KeNB: derivation of a new KeNB from the same KASME and including a freshness parameter

Re-keying of KeNB: derivation of a new KeNB from a new KASME (i.e., after an AKA has taken place)

Re-keying of NAS keys: derivation of new NAS keys from a new KASME

UE Security capabilities: The set of identifiers corresponding to the ciphering and integrity algorithms implemented in the UE. This includes capabilities for EPS AS and NAS, and includes capabilities for UTRAN and GERAN if these access types are supported by the UE.

UE EPS security capabilities: The UE security capabilities for EPS AS and NAS.

## ********************** end change 1**********************************

## ********************** start change 2**********************************

#### 7.2.6.3	ECM-CONNECTED to ECM-IDLE transition

On ECM-CONNECTED to ECM-IDLE transitions the eNB does no longer need to store state information about the corresponding UE. In particular eNB shall delete the current AS keys from its memory.

In particular, on ECM-CONNECTED to ECM-IDLE transitions:

MME and the UE shall keep the EPS NAS security context stored.

MME shall delete NH and NCC.

If the USIM supports EMM parameters storage, then the ME shall update the EPS NAS security context parameters on the USIM with its current values of the native EPS NAS security context and mark the EPS NAS security context on the USIM as valid. Otherwise, the ME shall update the EPS NAS security context in its non-volatile memory with the current values of the native EPS NAS security context and mark the EPS NAS security context in its non-volatile memory as valid.

## ********************** end change 2**********************************

## ********************** start change 3**********************************

##### 7.2.8.4.3	S1-Handover

When an S1-handover is performed, the source eNB shall not send any keys to the MME in the S1 HANDOVER REQUIRED message.

Upon reception of the HANDOVER REQUIRED message the source MME shall send the {NH, NCC} pair  and the EPS NAS security context to the target MME in the S10 FORWARD RELOCATION REQUEST message if source MME is different from target MME. The target MME shall store locally the {NH, NCC} pair received from the source MME.

The target MME shall achieve forward security by computing a fresh {NH, NCC} pair from the {NH, NCC} pair received from the source MME using the function defined in Annex A.4. The target MME shall then send the fresh {NH NCC} pair to the target eNB within the S1 HANDOVER REQUEST.

Upon receipt of the S1 HANDOVER REQUEST from the target MME, the target eNB shall compute the KeNB to be used with the UE by performing the key derivation defined in Annex A.5 with the fresh{NH, NCC} pair in the S1 HANDOVER REQUEST and the target PCI and its frequency EARFCN-DL. The target eNB shall include the NCC value from the fresh {NH,NCC} pair into the HO Command to the UE and remove any existing unused stored {NH, NCC} pairs.

NOTE: The source eNB may be the same as the target eNB and the source MME may be the same as the target MME in the description in this subclause.

## ********************** end change 3**********************************

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.