| 3G CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- |
|  | TS 33.102 | CR | Xxx | Current Version: | 3.0.0 |  |
| 3G specification number ( |  | ( CR number as allocated by 3G support team |
| For submission to TSG | SA | for approval | X | (only one box should |
| list TSG meeting no. here ( | for information |  | be marked with an X) |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM |  | ME | X | UTRAN | X | Core Network |  |
| (at least one should be marked with an X) |
| Source: | SA3 | Date: |  |
| Subject: | Cipher key lifetime |
| 3G Work item: | UTRAN Security |
| Category: | F Correction |  |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature |  |  |  |  |
| shall be marked | C Functional modification of feature |  |  |  |  |
| with an X) | D Editorial modification | X |  |  |  |
| Reason for change: | The sections describing the cipher key lifetime are replaced by a reference to the mechanisms on the integrity key lifetime. This to assure consistency. |
| Clauses affected: | 6.6.6 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

### 6.6.6	Cipher key lifetime

A mechanism is needed to ensure that a particular cipher key is not used for an unlimited period of time to avoid attacks using compromised keys. Authentication and key agreement which generates new cipher keys is not mandatory at call set-up, and there is therefore the possibility of unlimited and malicious re-use of compromised keys. The lifetime of the cipher key is controlled by the mechanism described in 6.4.6.