TSG SA WG3#6, Sophia Antipolis, 29 September – 1 October                                                         S3-99327

| DRAFT 3G CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- |
|  | TS 33.105 | CR | Xxx | Current Version: | V3.0.0 |  |
| 3G specification number ( |  | ( CR number as allocated by 3G support team |
| For submission to TSG | SA#5 | for approval | X | (only one box should |
| list TSG meeting no. here ( | for information |  | be marked with an X) |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM | X | ME |  | UTRAN |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | TSG SA WG3 | Date: | 99-10-01 |
| Subject: | Resources for cryptographic algorithms in the USIM |
| 3G Work item: | Security |
| Category: | F Correction |  |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature |  |  |  |  |
| shall be marked | C Functional modification of feature | X |  |  |  |
| with an X) | D Editorial modification |  |  |  |  |
| Reason for change: | Due to progress in TSG T WG3, additional information is available on the resources for cryptographic algorithms in the USIM. This information gives the requirements to design authentication and key agreement algorithms (f0 – f5). |
| Clauses affected: | 5.1.5 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

### 5.1.5	Implementation and operational considerations

The functions f1—f5 and f1* shall be designed so that they can be implemented on an IC card equipped with a 8-bit microprocessor running at 3.25 MHz with 8 kbyte ROM and 300byte RAM and produce AK, MAC-A and RES in less than 500 ms, and CK and IK in less than 500 ms.

The functions f0—f5 and f1* shall be designed so that they can be implemented either in software or in hardware in the AuC on a X6-bit microprocessor running at X7 MHz and with X8 kbits of memory and produce MAC-A, XRES, CK, IK and AK in less than X9 ms.