TSG SA WG3 #9, Helsinki, 7-9 Dec, 1999-12-09							S3-994zz

| 3G CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- |
|  | TS 33.102 | CR | Xxx | Current Version: | V3.2.0 |  |
| 3G specification number ( |  | ( CR number as allocated by 3G support team |
| For submission to TSG | SA#6 | for approval | x | (only one box should |
| list TSG meeting no. here ( | for information |  | be marked with an X) |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM | x | ME |  | UTRAN |  | Core Network | x |
| (at least one should be marked with an X) |
| Source: | Siemens AG | Date: | 09-12-99 |
| Subject: | Authentication and key agreement |
| 3G Work item: | Security |
| Category: | F Correction |  |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature |  |  |  |  |
| shall be marked | C Functional modification of feature | x |  |  |  |
| with an X) | D Editorial modification |  |  |  |  |
| Reason for change: | Remove option no longer needed, add parameter to be managed |
| Clauses affected: | Annex F |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

# Annex F (Informative): Example uses of AMF

## F.1	Support multiple authentication algorithms and keys

A mechanism to support the use of multiple authentication and key agreement algorithms is useful for disaster recovery purposes. AMF may be used to indicate the algorithm and key used to generate a particular authentication vector.

The USIM keeps track of the authentication algorithm and key identifier and updates it according to the value received in an accepted network authentication token.

## F.2 	Changing list parameters

This mechanisms is used in conjunction with the list mechanism described in Annex C.2.

Parameters which may be used to manage a list are the number of entries in a list (the list size) and an upper limit on the admissible difference SEQMS  - SEQ between the highest batch number SEQMS  in the list and an accepted batch number SEQ. A mechanism to change these parameters dynamically is useful since the optimum for these parameters may change over time. AMF is used to indicate the maximum admissible list size or maximum admissible difference SEQMS  - SEQ to be used by the user when verifying the authentication token and deciding whether it is still accepted.

The USIM keeps track of the maximum admissible list size and maximum admissible difference SEQMS  - SEQ and updates them according to the value received in an accepted network authentication token providing that SEQ > SEQMS. .

## F.3	Setting threshold values to restrict the life times of cipher and integrity keys

According to section 6.4.3, the USIM contains a mechanism to limit the amount of data that is protected by an access link key set. The AMF field may be used by the operator to set this limit in the USIM.

The USIM keeps track of the limit to the key set life time and updates it according to the value