| 3G CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- |
|  | 33.102 | CR | 034 | Current Version: | 3.2.0 |  |
| 3G specification number ( |  | ( CR number as allocated by 3G support team |
| For submision to TSG | SA #6 | for approval | X | (only one box should |
| list TSG meeting no. here ( | for information |  | be marked with an X) |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM |  | ME |  | UTRAN |  | Core Network | X |
| (at least one should be marked with an X) |
| Source: | TSG SA WG 3 | Date: | 1999-Dec-9 |
| Subject: | Distribution of authentication data within one serving network domain |
| 3G Work item: | Security |
| Category: | F Correction |  |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature |  |  |  |  |
| shall be marked | C Functional modification of feature | X |  |  |  |
| with an X) | D Editorial modification |  |  |  |  |
| Reason for change: | The modification allows that the user is authenticated using local authentication after a location/routing area update in a new MSC/VLR or SGSN. The use of that options lowers the number of quintets that are used by avoiding authentication and key establishment when there is no reason for from a security viewpoint. The secure reduction of the number of authentication and key agreement protocol runs results in a reduced amount of required signalling and Authentication Centre activity. |
| Clauses affected: | 6.3.4 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: | The changes bring TS 33.102 in line with TS 23.060, especially section 6.8.1.2, that describes the information elements sent from one SGSN to another SGSN on an intersystem change for PS services. |

<--------- double-click here for help and instructions on how to create a CR.

### 6.3.4	Distribution of IMSI and temporary authentication data within one serving network domain

The purpose of this procedure is to provide a newly visited MSC/VLR or SGSN with temporary authentication data from a previously visited MSC/VLR or SGSN within the same serving network domain.

The procedure is shown in Figure 10.

Figure 10: Distribution of IMSI and temporary authentication data within one serving network domain

The procedure shall be invoked by the newly visited MSC/VLRn (resp. SGSNn) after the receipt of a location update request (resp. routing area update request) from the user wherein the user is identified by means of a temporary user identity TMSIo (resp. P-TMSIo) and the location area identity LAIo (resp. routing area identity RAIo) under the jurisdiction of a previously visited MSC/VLRo or SGSNo that belongs to the same serving network domain as the newly visited MSC/VLRn or SGSNn.

The protocol steps are as follows:

- The MSC/VLRn (resp. SGSNn) sends a user identity request to the MSC/VLRo (or SGSNo), this message contains TMSIo and LAIo (resp. P-TMSIo and RAIo).

- The MSC/VLRo (resp. SGSNo) searches the user data in the database.

If the user is found, the MSC/VLRo (resp. SGSNo) shall send a user identity response back that

  - shall include the IMSI,

  - may include a number of unused authentication vectors (quintets or triplets) and

  - may include the current security context data: CK, IK and KSI (UMTS) or Kc and CKSN (GSM).

The MSC/VLRo or SGSNo subsequently deletes the authentication vectors which have been sent and the data elements on the current security context.

If the user cannot be identified the MSC/VLRo or SGSNo shall send a user identity response indicating that the user identity cannot be retrieved.

- If the MSC/VLRn or SGSNn receives a user identity response with an IMSI, it creates an entry and stores any authentication vectors and any data on the current security context that may be included.

If the MSC/VLRn or SGSNn receives a user identity response indicating that the user could not be identified, it shall initiate the user identification procedure described in 6.2.