| TSG SA WG3 #9, | Document | S3-99512 |
| --- | --- | --- |
| Helsinki, 07- 09 December 1999 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 33.102 | CR | XXr1 | Current Version: | 3.2.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: | SA#9 | for approval | x |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM | x | ME |  | UTRAN / Radio |  | Core Network | X |
| (at least one should be marked with an X) |
| Source: | Ericsson | Date: | 1999-12-03 |
| Subject: | SQNLO in GSM |
| Work item: | Release 99 |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature | x |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | X |
|  |  |  |  | Release 00 |  |
| Reason for change: | The SQNLO cannot be sent back to the VLR/SGSN if it contains more than one octet. The MM message “Location update request” contains 18 octets of max 20 and inclusion of a new IE means always that one octet is needed for IE type identifier so only one octet would remain for the SQNLO. As a result, the support for window and list mechanisms cannot be implemented in GSM. Consequently the support for window and list mechanisms should be removed from the TS 33.102, otherwise UMTS authentication cannot be applied to GSM (even for USIM in R99 GSM network). |
| Clauses affected: | 6.3.7 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.