| TSG SA WG3 #9, S3-99___ Helsinki, Finland, 7th–9th December 1999 |
| --- |
| 3G CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | TS 33.102 | CR |  | Current Version: | V3.2.0 |  |
| 3G specification number ( |  | ( CR number as allocated by 3G support team |
| For submission to TSG | SA#9 | for approval | x | (only one box should |
| list TSG meeting no. here ( | for information |  | Be marked with an X) |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM |  | ME |  | UTRAN | X | Core Network | x |
| Source: | T-Mobil | Date: | 06.12.1999 |
| Subject: | Corrections in Figure 14 |
| 3G Work item: | Security |
| Category: | F Correction |  |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature |  |  |  |  |
| shall be marked | C Functional modification of feature |  |  |  |  |
| with an X) | D Editorial modification |  |  |  |  |
| Reason for change: | Correction of parameters to be transmitted between UMTS or UMTS-capable MSC/VLR or SGSN and GSM BSS regarding to Interoperation of UMTS users |
| Clauses affected: | Sections 6.3.4 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

### 6.8.1	Interoperability for UMTS users

Figure 14: Interoperability for UMTS Users

# Text boxes

UMTS

HLR/AuC

UMTS

MSC/VLR or SGSN

GSM

MSC/VLR or SGSN

Non-UMTS capable

UMTS Access Network

UMTS AV

(RAND, XRES, CK, IK, AUTN)

GSM Data

(RAND, Kc)

UMTS Data

(RAND, CK, IK, AUTN)

GSM Data: Kc and

UMTS Data: RAND, AUTN

GSM AV

(RAND, SRES, Kc)

GSM

MSC/VLR or SGSN

UMTS capable

GSM Data: Kc and

UMTS Data: RAND, AUTN

UMTS AV

(RAND, XRES, CK, IK, AUTN)

GSM

Access Network

GSM

Access Network

GSM

Access Network