| 3GPP/SMG Meeting TSG SA WG3#9 | Document | S3-99528 |
| --- | --- | --- |
| Helsinki,Finland, 99-12-07/09 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 33.102 | CR | 38 | Current Version: | 3.2.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: | SA#6 | for approval | x |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | Non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME |  | UTRAN / Radio |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | S3 | Date: | 1999-12-08 |
| Subject: | Clarification on system architecture |
| Work item: | Security |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature | X |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | X |
|  |  |  |  | Release 00 |  |
| Reason for change: | The UMTS system architecture with respect to the PS and CS domains is introduced in order to clarify access security procedures and mechanisms |
| Clauses affected: | 4 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

# 4	Overview of the security architecture

Figure 1 gives an overview of the complete 3G security architecture.

Figure 1 : Overview of the security architecture

Five security feature groups are defined. Each of these feature groups meets certain threats, accomplishes certain security objectives:

-	Network access security (I): the set of security features that provide users with secure access to 3G services, and which in particular protect against attacks on the (radio) access link;

-	Network domain security (II): the set of security features that enable nodes in the provider domain to securely exchange signalling data, and protect against attacks on the wireline network;

-	User domain security (III): the set of security features that secure access to mobile stations

- Application domain security (IV): the set of security features that enable applications in the user and in the provider domain to securely exchange messages.

- Visibility and configurability of security (V): the set of features that enables the user to inform himself whether a security features is in operation or not and whether the use and provision of services should depend on the security feature.

Figure 2 gives an overview of the UE registration and connection principles within UMTS with a CS service domain and a PS service domain. As in GSM/GPRS, user (temporary) identification, authentication and key agreement will take place independently in each service domain. User plane traffic will be ciphered using the cipher key agreed for the corresponding service domain while control plane data will be ciphered and integrity protected using the cipher and integrity keys from either one of the service domains. In clause 6 the detailed procedures are defined and when not otherwise stated they are used in both service domains.

Figure 2: Overview of the UE registration and connection principles within UMTS for the separate CN architecture case when the CN consists of both a CS service domain with evolved MSC/VLR, 3G_MSC/VLR, as the main serving node and an PS service domain with evolved SGSN/GGSN, 3G_SGSN and 3G GGSN, as the main serving nodes, (Extract from RS23.121 – Figure 4-8)