3GPP TSG-SA3 Meeting #100e 	S3-201837

# e-meeting, 17 – 28 Augest 2020						  							merge of S3-201622 and S3-202024

# Source:	Huawei, Hisilicon, Interdigital, Ericsson

# Title:		5G ProSe: New Key issue on authorization in the UE-to-Network relay scenario

# Document for:	Approval

Agenda Item:	5.10

# 1	Decision/action requested

This contribution proposes a new Key issue on authorization in the UE-to-Network relay scenario

# 2	References

[1]	3GPP TR 23.752: "Study on system enhancement for Proximity based Services (ProSe) in the 5G System (5GS) ".

# 3	Rationale

TR 23.752 [1], key issue #3 describes the issue on the support of UE-to-Network Relay, i.e.

“--	How to authorize a UE to be a 5G UE-to-Network Relay and how to authorize a UE to access 5GC via a 5G UE-to-Network Relay.

…

NOTE 1: Security and privacy aspects will be handled by SA WG3.”

The above authorizaiton issue shall be studied.

# 4	Detailed proposal

It is proposed to approve the following key issue.

*************** Start of the changes ****************

## X.Y	Key issue #X.Y: Authorization in the UE-to-Network relay scenario

### X.Y.1	Key issue details

3GPP system has to be able to authorise a UE to access 5GC via a 5G UE-to-Network Relay and to authorise a UE to perform as a UE-to-Network Relay. Without a proper authorisation, unauthorised entities will be able to access 5GC via UE-to-Network Relay or act as UE-to-Network Relays creating a vulnerability and causing possible (D)DOS attacks or leading to unauthorised service usage on both 5GS and UE-to-Network Relay.

TR 23.752 [aa], key issue #3 describes the issue on the support of UE-to-Network Relay, i.e.

“-How to authorize a UE to be a 5G UE-to-Network Relay and how to authorize a UE to access 5GC via a 5G UE-to-Network Relay.

…

NOTE 1: Security and privacy aspects will be handled by SA WG3”

From the security point of view, whether the UE can play the UE-to-Network Relay role shall be assured by the Remote UE. On the contrary, whether the UE can play the remote UE rule shall be assured by the UE-to-Network relay.

This key issue is to study the authorization issue in the UE-to-Network relay scenario.

### X.Y.2	Threats

An attacker may impersonate the UE-to-Network Relay.If the authorization of the UE-to-Network relay role is not supported, the attacker UE could play the UE-to-Network relay role, and force a UE to camp on to it by passing all the message on between the UE and the network. It may then deny the UE services between the two UEs, such as drop the message.

An attacker may impersonate the Remote UE.If the authorization of the remote UE is not supported, the attacker UE could play the remote UE role, and arbitrarily consume the services provided by the UE-to-Network relay. The charging of the attacher UE as a remote UE may not be supported.

### X.Y.3	Potential security requirements

The 5GS shall support to authorize the UE as a UE-to-Network relay in the UE-to- Network relay scenario.

The 5GS shall support to authorize the UE as a Remote UE in the UE-to-Network relay scenario.

*************** End of the changes ****************