3GPP TSG-SA3 Meeting #100e 	S3-20xxxx

# e-meeting, 17 -28 August 2020

Title:	[DRAFT] LS on Successful authentication event on the UE for 5G AKA

Response to:

Release:

Work Item:	TEI16

Source:	SA3

To:	CT1

Cc:	CT4

Contact Person:

#### Name:	Vlasios Tsiatsis

Tel. Number:

E-mail Address:	vlasios.tsiatsis@ericsson.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

1. Overall Description:

SA3 received a LS reply from CT4 (S3‑201513/C4-203568) specifying that the latest KAUSF shall be maintained on the network. SA3 would like to specify the same behaviour for the UE side, i.e. the latest shall be maintained on the UE and to be used for e.g. UPU, SoR procedures.

SA3 can specify in an SA3 specification that the latest KAUSF shall be maintained upon successful authentication.

The event upon which the UE determines the successful authentication for EAP-AKA’ is well defined as the network explicitly sends a success notification to the UE (Step 11, clause 6.1.3.1, TS 33.501). However, such explicit notification by the network is not provided in the case of 5G AKA authentication method.

SA3 would like to ask following question:

If SA3 defines in TS 33.501 that UE shall store the latest KAUSF after successful primary authentication, does CT1 have enough information to specify stage 3 behaviour, i.e. the event upon which the UE shall store the KAUSF ?

2. Actions:

To CT1 group.

ACTION: 	SA3 kindly requests CT1 to take the information into account and provide feedback.

3. Date of Next TSG-SA WG3 Meetings:

SA3#100e-Bis	12-16 October 2020	e-meeting

SA3#101e	9 - 20 November 2020	e-meeting

# Comments

to be removed after LS is approved

Do we need to CC CT4 ?