3GPP TSG-SA3 Meeting #100e 	S3-202048

# e-meeting, 17 -28 August 2020

Title:	Draft LS Response on Clarification on AAA-Server address

Response to:	S3-201512 (C4-203452)

Release:	Release-16

Work Item:	eNS

Source:	SA WG3

To:	CT WG4, SA WG2

Cc:

Contact Person:

Name:	Henrik Normann

Tel. Number:

E-mail Address:	henrik.normann@ericsson.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

1. Overall Description:

SA3 thanks CT4 for the LS pointing to inconsistencies in stage 2 specifications with regards to the handling of the AAA-S address in NSSAA procedures.

SA3 has checked the NSSAA procedure as described in 33.501 and would like to answer CT4 questions as follows:

- Whether the AAA-S address is conveyed by AMF to the AUSF/NSSAAF in step4?

Currently the AMF does not provide the AAA-S address to the NSSAAF in step 4 of the NSSAA procedure described in section 16.3 of TS 33.501.

SA3 would like to point out that sharing of information should be on a need to know basis. Sharing the address of the 3rd party AAA server with a visited network (vPLMN) which does not have any business relationship or any SLA with the 3rd party vendor can cause a security threat to the 3rd party vendor and should not be done unless there is a clear consensus from the 3rd party vendor. Especially since the HPLMN may have a wide range of roaming partners it is not desirable to share such information with all of them.

2. Actions:

To CT WG4 group.

ACTION: 	SA3 kindly requests CT4 to take into consideration the answer above.

To SA WG2 group.

ACTION: 	SA3 kindly requests SA2 to take into consideration the answer above.

3. Date of Next TSG-SA WG3 Meetings:

SA3#100e-Bis	12-16 October 2020	e-meeting

SA3#101e	9 - 20 November 2020	e-meeting