# 3GPP TSG-SA3 Meeting #101e 	draft_S3-202904-r1

# e-meeting, 9 – 20 November 2020	Revision of S3-20xxxx

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 33.535 | CR | 0038 | rev | - | Current version: | 16.1.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Kaf lifetime expiration in clause 5.2 |
| --- | --- |
| Source to WG: | ZTE |
| Source to TSG: | S3 |
| Work item code: | AKMA |  | Date: | 2020-10-29 |
| Category: | B |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | When the current AKMA Anchor Key is not changed, the new AKMA Application Key cannot be established. |
| Summary of change: | Modify the new AKMA Application Key establishment when the Kaf lifetime expires. |
| Consequences if not approved: | A new Kaf cannot be established. |
| Clauses affected: | 5.2 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

*** 1st CHANGE***

## 5.2	AKMA key lifetimes

The KAKMA and A-KID are valid until the next successful primary authentication is performed (implicit lifetime), in which case the KAKMA and A-KID are replaced.

AKMA Application Keys (KAF) shall use explicit lifetimes based on the operator's policy. The lifetime of KAF shall be sent by the AAnF as described in clauses 6.2 and 6.3. In case that a new KAKMA is established, the KAF can continue to be used until its lifetime expires. When the KAF lifetime expires, a new  KAF is established based on the new KAKMA, which is generated after a new successful primary authentication.

Editor’s Note: How to trigger to establish a new KAKMA when the KAF lifetime expires is FFS.

*** END OF CHANGES***