3GPP TSG-SA3 Meeting #103-e 	S3-211559-r1

# e-meeting, 17 - 28 May 2021											Revision of S3-20xxxx

# Source:	ZTE

# Title:	Add evaluation for solution 4.5

# Document for:	Approval

Agenda Item:	5.5

# 1	Decision/action requested

Add evaluation for solution #4.5.

# 2	References

[1]	3GPP TR 33.846 v0.11.0

# 3	Rationale

Propose to add evaluation for solution #3.2.

# 4	Detailed proposal

Changes to clause 6.4.5.3.

**** START OF CHANGES ****

#### 6.4.5.3	Evaluation

In the solution, SQNMS is not sent in Authentication failure, which prevent the leakage of SQNMS even with repeated RAND or AUTN. Instead USIM calculates AUTS during the registration step using a newly generated RANDMS value.

The solution requires changes on UE, AMF and UDM.

The solution may be applicable to EPS.

**** END OF CHANGES ****