# 3GPP TSG-SA3 Meeting #103e	draft_S3-211931-r3

# e-meeting, 17 – 28 May 2021	revision of S3-21xabc

# Source:	CATT

# Title:	pCR to TR33.847- Conclusion of KI#12

# Document for:	Approval

Agenda Item:	5.9

# 1	Decision/action requested

Approve the pCR below

# 2		Rationale

Add conclusions to Key Issue #12.

# 3	Detailed proposal

#### *** BEGIN CHANGES ***

## 7.Y	Conclusions for Key Issue #12

For Key Issue #12, the following is taken as conclusions:

-	If the principle for the eV2X PC5 unicast link establishment in TS 33.536 [8] is reused (i.e. both signalling and user plane have on-demand security negotiation), it is concluded that the key-hashed using KNRP is used to protect the initiating UE’s security policies and security capabilities within the Direct Security Mode Command message. This aims to prevent the bidding-down attack caused by unprotected PC5 signalling link.

-	It is concluded that the security mechanism in Solution #7 is taken as the basis for normative work if signalling has mandatory security protection and user plane uses on-demand security negotiation. This solution satisfies the security requirements of Key Issue #12

-	It is concluded that the security mechanism in Solution #23 is taken as the basis for normative work for implementations that support Direct Discovery.

#### *** END OF CHANGES ***