3GPP TSG-SA WG3(Security) Meeting #55 	( S3-xxxxxx

# Shanghai, China, 11-15 May 2009

| CR-Form-v9.4 |
| --- |
| CHANGE REQUEST |
| ( | SpecNumber | CR |  | ( rev | - | ( Current version: | 8.6.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | GBA DIAMETER based Zn reference point to support TLS |
| --- | --- |
| Source to WG: ( | China Mobile |
| Source to TSG: ( | TSG SA WG3 |
| Work item code: ( | SEC7-GAA2 |  | Date: ( | 18/02/2008 |
| Category: ( | B |  | Release: ( | Rel-8 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) |
| Reason for change: ( | Current specification requires the Diameter based GBA Zn reference point to be secured acording to NDS/IP while the Diameter based Zn’ reference point is required to be secured using TLS. This means the network operator should maintain two kinds of security mechanisms- IPSEC and TLS- at the same time on its BSFs and accordingly increase the operator’s cost. What is more, as specified by TS 33.210, NDS/IP mainly faces to the network managed by a single administrative authority. While in practise, some NAFs may be managed by a third part SP though these NAFs are located in the home network . In this case, it is not proper to secure Zn reference point using IPSEC. From the point of view of implementation, TLS is easier than IPSEC in many cases, especially when NAT transversal is considered. Additionally, IPSEC is suite to establish a connection that is stable for a certain period. If the NAF will seldom acquire KS_NAF from a certain BSF, IPSEC is not a economical method. In this case, TLS is a better option, since TLS session can easily be closed when the tcp connection is closed and be reused after a while. According to the above analysis, we propose to add TLS as an option to secure the Diameter based Zn reference point. |
| Summary of change: ( | To allow the Diameter based Zn to be secured using TLS as an option. |
| Consequences if ( not approved: | The GBA will be less flexible in implementation. |
| Clauses affected: ( | Section 4.4.6 |
|  | Y | N |  |  |
| Other specs ( |  |  | Other core specifications ( |  |
| affected: |  |  | Test specifications |  |
|  |  |  | O&M Specifications |  |
| Other comments: ( |  |

### 4.4.6	Requirements on reference point Zn

The requirements for reference point Zn are:

-	mutual authentication, confidentiality and integrity shall be provided;

-	If the BSF and the NAF are located within the same operator's network, the DIAMETER based Zn reference point shall be secured according to NDS/IP [13] or be secured using TLS as specified in RFC 2246[28];

-	If the BSF and the NAF are located in different operators' networks, the DIAMETER based Zn' reference point between the Zn-Proxy and the BSF shall be secured using TLS as specified in RFC 2246 [28];

NOTE 1:	Annex E specifies the TLS profile that shall be applied.

-	An HTTP based Zn/Zn' reference point shall be secured using TLS as specified in RFC 2246 [28];

NOTE 1b:		Annex E specifies the TLS profile that shall be applied.

-	The BSF shall verify that the requesting NAF is authorised to obtain the key material or the key material and the requested USS;

-	The NAF shall be able to send a key material request to the BSF, containing NAF's public hostname used by the UE's corresponding request. The BSF shall be able to verify that a NAF is authorized to use this hostname, i.e. the FQDN used by UE when it contacts the NAF;

-	The BSF shall be able to send the requested key material to the NAF;

-	The NAF shall be able to get a selected set of application-specific USSs from the BSF, depending on the policy of the BSF and the application indicated in the request from the NAF over Zn;

-	The NAF shall be able to indicate to the BSF the single application or several applications it requires USSs for;

NOTE 2:	If some application needs only a subset of an application-specific USS, e.g. only one IMPU, the NAF selects this subset from the complete set of USS sent from BSF.

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.