# 3GPP TSG-SA3 (Security)	S3-100492

# SA3#59, 26-30 April 2010, Lisbon, Portugal	revision of S3-10xyzw

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 33.210 | CR | 0028 | ( rev | - | ( Current version: | 9.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correction of explanations of abbreviations CSCF and IKEvx |
| --- | --- |
| Source to WG: ( | Nokia Corporation, Nokia Siemens Networks |
| Source to TSG: ( | SA3 |
| Work item code: ( | TEI9 |  | Date: ( | 08/04/2010 |
| Category: ( | F |  | Release: ( | 9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | The abbreviation CSCF was defined differently in different 3GPP specifications. The terminology of 33.203 on IMS security should be used also in 33.210. In addition the definitions of IKEv1 and IKEv2 are aligned with the related RFCs 2401 and 4306 |
| Summary of change: ( | The definition of CSCF in 33.210 is corrected to be the same as in 33.203. The definitions of IKEv1 and IKEv2 are aligned with the RFCs. |
| Consequences if ( not approved: | Different definitions of the term “CSCF” in 3GPP specifications. Diverging definition of IKE from the RFCs. |
| Clauses affected: ( | 3.3 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

*********************** start of change ************************

## 3.3	Abbreviations

For the purposes of the present document, the following abbreviations apply:

AAA	Authentication Authorization Accounting

AES		Advanced Encryption Standard

AH	Authentication Header

BG	Border Gateway

CS	Circuit Switched

CSCF	Call Session Control Function

DES	Data Encryption Standard

DoI	Domain of Interpretation

ESP	Encapsulating Security Payload

GTP	GPRS Tunnelling Protocols

IESG	Internet Engineering Steering Group

IETF	Internet Engineering Task Force

IKE	Internet Key Exchange

IKEv1	Internet Key Exchange version 1

IKEv2	Internet Key Exchange version 2

IP		Internet Protocol

IPsec	IP security  - a collection of protocols and algorithms for IP security incl. key mngt.

ISAKMP	Internet Security Association Key Management Protocol

IV		Initialisation Vector

MAC	Message Authentication Code

NAT	Network Address Translator

NDS	Network Domain Security

NDS/IP	NDS for IP based protocols

NE	Network Entity

PS	Packet Switched

SA	Security Association

SAD	Security Association Database (sometimes also referred to as SADB)

SEG	Security Gateway

SIP	Session Initiation Protocol

SPD	Security Policy Database (sometimes also referred to as SPDB)

SPI	Security Parameters Index

TISPAN	Telecoms & Internet converged Services & Protocols for Advanced Networks

TrGW	Transition Gateway

*********************** end of change ************************

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.