3GPP TSG-SA WG3-LI Meeting #37 	( SA3LI10_043r2

# New York, USA, 4th-6th May 2010

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 33.106 | CR | 0014 | ( rev | - | ( Current version: | 9.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | H(e)NB LI Support |
| --- | --- |
| Source to WG: ( | TPS |
| Source to TSG: ( | SA3 |
| Work item code: ( | LI10 |  | Date: ( | 06/05/2010 |
| Category: ( | B |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | The current version of 33.106 does not describe LI requirments concerned with the use of H(e)NB. |
| Summary of change: ( | The CR adds appropriate references and proposes a new section that provides specific LI support for H(e)NB |
| Consequences if ( not approved: | LI support for H(e)NBs will not be provided to LE. |
| Clauses affected: ( | 2, 3, 5.X |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

*** FIRST MODIFICATION to Section 2***

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies.

[1]	European Union Council Resolution on the Lawful Interception of Telecommunications (17. January 1995)

[2]	ETSI TS 101 331: "Telecommunications security; Lawful Interception (LI); Requirements of Law Enforcement Agencies".

[3]	ETSI ES 201 158: "Lawful Interception; Requirements for network functions".

[4]	ETSI ES 201 671: "Handover Interface for the lawful interception of telecommunications traffic".

[5]	GSM 01.33: "Lawful Interception requirements for GSM".

[6]	GSM 02.33:" Lawful Interception - stage 1".

[7]	GSM 03.33: "Lawful Interception - stage 2".

[8]	J-STD-025-A: "Lawfully Authorized Electronic Surveillance".

[9]	3GPP TS 33.107: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3G Security; Lawful interception architecture and functions".

[10]	3GPP TS 33.108: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3G Security; Handover interface for Lawful Interception".

[X]	3GPP TS 22.220:  “Service Requirements for Home NodeBs and Home eNodeBs.

*** END OF First MODIFICATIONS ***

*** SECOND MODIFICATION  --Section 3 ***

# 3	Definitions and abbreviations

## 3.1	Definitions

For the purposes of the present document, the following terms and definitions apply.

Interception Area: is a subset of the Public Lands Mobile Network (PLMN) service area comprised of a set of cells which define a geographical zone.

Location Dependent Interception: is interception within a PLMN service area that is restricted to one or several Interception Areas (IA).

Network Based Interception: Interception that is invoked at a network access point regardless of Target Identity.

Subject Based Interception: Interception that is invoked using a specific Target Identity

Target Identity: A technical identity that uniquely identifies a target of interception. One target may have one or several identities.

## 3.3	Abbreviations

For the purposes of the present document, the following abbreviations apply:

CC	Content of Communication

CSG	Closed Subscriber Group

HeNB	Home eNodeB

H(e)NB	HNB and HeNB

HNB	Home NodeB

IA	Interception Area

IP	Internet Protocol

IRI	Intercept Related Information

LDI	Location Dependent Interception

LEA	Law Enforcement Agency

LEMF	Law Enforcement Monitoring Facility

3GMS	Third Generation Mobile Communications System

VHE	Virtual Home Environment

*** END OF MODIFICATIONS ***

*** THIRD MODIFICATION  -- New Section ***

# 5.X	Lawful Interception for Home Node B and Home enhanced Home Node B (H(e)NB)

HNB and HeNB are jointly referred to as H(e)NB, as defined in [X].  The location of the H(e)NB is the location information used by the operator to verify the location for H(e)NB activation.

For the purpose of LI, a target may be a subscriber attached to a H(e)NB, a Closed Subscriber Group (CSG), or it is a national issue to allow targeting a H(e)NB itself.

The LI requirements for H(e)NB local routing, selected IP traffic offload (SIPTO) or local IP access (LIPA) are FFS.

Interception should be done in such a manner to avoid detectability by the target or others.

When a target receives service from the PLMN via a H(e)NB, the following applies:

- the interception capabilities shall take place as for normal PLMN use

- H(e)NB information (e.g., location and identification) shall also be provided to the LEMF

- If available, the location reported for the target is the H(e)NB location where the target’s MS is attached

- Target attachment to the H(e)NB and handovers to/from the H(e)NB shall be reported to the LEMF

- There may be national requirements to identify specific information that is required to be reported

When the target is the CSG, the PLMN operator shall report the following:

- modifications (e.g., additions, deletions, changes in time limits for temporary CSG Members) of the CSG list for the H(e)NB

- When available, the access method (e.g., via MS/UE or web) the H(e)NB Hosting Party used to modify the CSG list, if multiple access methods are allowed

- CSG member’s handovers to/from the H(e)NB

- CSG members attachments to the H(e)NB

- CSG members communications via the H(e)NB

- It is a national option whether interception on CSG members’ communications continues after handover occurs from the H(e)NB

When the target is the H(e)NB, then the PLMN operator shall report the following:

- activation and deactivation of the targeted H(e)NB

- IP address information regarding the secure tunnel endpoints between the H(e)NB and the Femto Security Gateway in the home network

- modifications (e.g., additions, deletions, changes in time limits for temporary CSG Members) of the CSG list for the H(e)NB

- When available, the access method (e.g., via MS/UE or web) the target used for the modification of the CSG list, if multiple access methods are allowed

- handovers to/from the H(e)NB.

- MS/UE registrations on the H(e)NB

- communications via the H(e)NB

- It is a national option whether interception on H(e)NB communications continues after handover occurs from the H(e)NB

NOTE:  The requirements for the CSG are FFS.

*** END OF MODIFICATIONS ***

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.