3GPP TS 33.515 V16.1.0 (2019-12)

Technical Specification

3rd Generation Partnership Project;

Technical Specification Group Services and System Aspects;

5G Security Assurance Specification (SCAS) for the Session Management Function(SMF)

network product class

(Release 16)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP..
The present document has not been subject to any approval process by the 3GPP Organizational Partners and shall not be implemented.
This Specification is provided for future development work within 3GPP only. The Organizational Partners accept no liability for any use of this Specification.
Specifications and Reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organizational Partners' Publications Offices.

Keywords

5G, Security, Assurance, SMF, product, class

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 2019, 3GPP Organizational Partners (ARIB, ATIS, CCSA, ETSI, TSDSI, TTA, TTC).

All rights reserved.

UMTS™ is a Trade Mark of ETSI registered for the benefit of its members

3GPP™ is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners
LTE™ is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners

GSM® and the GSM logo are registered and owned by the GSM Association

Contents

Foreword	4

1	Scope	6

2	References	6

3	Definitions of terms, symbols and abbreviations	6

3.1	Terms	6

3.2	Symbols	6

3.3	Abbreviations	6

4	SMF-specific security requirements and related test cases	7

4.1	Introduction	7

4.2 	SMF-specific security functional adaptations of requirements and related test cases	7

4.2.1	Introduction	7

4.2.2	Security functional requirements on the SMF deriving from 3GPP specifications and related test cases	7

4.2.2.1	Security functional requirements on the SMF deriving from 3GPP specifications	7

4.2.2.1.1	Priority of UP security policy	7

4.2.2.1.2	TEID uniqueness	8

4.2.2.1.3	Security functional requirements on the SMF checking UP security policy	9

4.2.2.1.4	Charging ID Uniqueness	9

4.2.3	Technical Baseline	10

4.2.3.1	Introduction	10

4.2.3.2	Protecting data and information	10

4.2.3.2.1	Protecting data and information – general	10

4.2.3.2.2	Protecting data and information – unauthorized viewing	10

4.2.3.2.3	Protecting data and information in storage	10

4.2.3.2.4	Protecting data and information in transfer	10

4.2.3.2.5	Logging access to personal data	10

4.2.3.3	Protecting availability and integrity	10

4.2.3.4	Authentication and authorization	10

4.2.3.5	Protecting sessions	11

4.2.3.6	Logging	11

4.2.4	Operating Systems	11

4.2.5	Web Servers	11

4.2.6	Network Devices	11

4.2.7	Void	11

4.3	SMF-specific adaptations of hardening requirements and related test cases	11

4.3.1	Introduction	11

4.3.2	Technical baseline	11

4.3.3	Operating systems	11

4.3.4	Web servers	11

4.3.5	Network devices	11

4.3.6	Other SMF-specific adaptations of hardening requirements and related test cases	11

4.4	Network functions in service-based architecture	12

Annex A (informative):	Change history	13

# Foreword

This Technical Specification has been produced by the 3rd Generation Partnership Project (3GPP).

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of the present document, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	or greater indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the document.

In the present document, modal verbs have the following meanings:

shall		indicates a mandatory requirement to do something

shall not	indicates an interdiction (prohibition) to do something

The constructions "shall" and "shall not" are confined to the context of normative provisions, and do not appear in Technical Reports.

The constructions "must" and "must not" are not used as substitutes for "shall" and "shall not". Their use is avoided insofar as possible, and they are not used in a normative context except in a direct citation from an external, referenced, non-3GPP document, or so as to maintain continuity of style when extending or modifying the provisions of such a referenced document.

should		indicates a recommendation to do something

should not	indicates a recommendation not to do something

may		indicates permission to do something

need not	indicates permission not to do something

The construction "may not" is ambiguous and is not used in normative elements. The unambiguous constructions "might not" or "shall not" are used instead, depending upon the meaning intended.

can		indicates that something is possible

cannot		indicates that something is impossible

The constructions "can" and "cannot" are not substitutes for "may" and "need not".

will		indicates that something is certain or expected to happen as a result of action taken by an agency the behaviour of which is outside the scope of the present document

will not		indicates that something is certain or expected not to happen as a result of action taken by an agency the behaviour of which is outside the scope of the present document

might	indicates a likelihood that something will happen as a result of action taken by some agency the behaviour of which is outside the scope of the present document

might not	indicates a likelihood that something will not happen as a result of action taken by some agency the behaviour of which is outside the scope of the present document

In addition:

is	(or any other verb in the indicative mood) indicates a statement of fact

is not	(or any other negative verb in the indicative mood) indicates a statement of fact

The constructions "is" and "is not" do not indicate requirements.

# 1	Scope

The present document contains requirements and test cases that are specific to the SMF network product class. It refers to the Catalogue of General Security Assurance Requirements and formulates specific adaptions of the requirements and test cases given there, as well as specifying requirements and test cases unique to the SMF network product class.

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TS 23.501: "System Architecture for the 5G System".

[2]	3GPP TS 33.117: "Catalogue of general security assurance requirements".

[3]	3GPP TS 23.060: "General Packet Radio Service".

[4]	3GPP TR 33.926: "Security Assurance Specification (SCAS) threats and critical assets in 3GPP network product classes".

[5]	3GPP TS 29.281: "General Packet Radio System (GPRS) Tunnelling Protocol User Plane (GTPv1-U) ".

[6]	3GPP TS 32.255: "Charging Management; 5G Data Connectivity Domain Charging".

[7]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[8]	3GPP TS 33.501 (Release 15): "Security architecture and procedures for 5G system".

# 3	Definitions of terms, symbols and abbreviations

## 3.1	Terms

For the purposes of the present document, the terms given in 3GPP TR 21.905 [7] and the following apply. A term defined in the present document takes precedence over the definition of the same term, if any, in 3GPP TR 21.905 [7].

## 3.2	Symbols

Void.

## 3.3	Abbreviations

For the purposes of the present document, the abbreviations given in 3GPP TR 21.905 [1] and the following apply. An abbreviation defined in the present document takes precedence over the definition of the same abbreviation, if any, in 3GPP TR 21.905 [1].

CHF	Charging Function

SCAS	Security Assurance Specification

SMF	Session Management Function

TEID	Tunnel Endpoint Identifier

UDM	Unified Data Management Function

UPF	User Plane Function

# 4	SMF-specific security requirements and related test cases

## 4.1	Introduction

SMF specific security requirements include both SMF-specific security functional requirements in relevant specifications as well as security requirements introduced in the present document derived from the threats specific to SMF as described in TR 33.926 [4].

## 4.2 	SMF-specific security functional adaptations of requirements and related test cases

### 4.2.1	Introduction

Present clause contains SMF-specific security functional adaptations of requirements and related test cases.

### 4.2.2	Security functional requirements on the SMF deriving from 3GPP specifications and related test cases

#### 4.2.2.1	Security functional requirements on the SMF deriving from 3GPP specifications

##### 4.2.2.1.1	Priority of UP security policy

Requirement Name: Priority of UP security policy

Requirement Reference: TS 23.501 [1], clause 5.10.3

Requirement Description: "User Plane Security Policy from UDM takes precedence over locally configured User Plane Security Policy." as specified in TS 23.501 [1], clause 5.10.3

Threat References: TR 33.926 [4], clause J.2.2.1 Non-compliant UP security policy handling

Test Case:

Test Name: TC_UP_POLICY_PRECEDENCE_SMF

Purpose:

Verify that the user plane security policy from the UDM takes precedence at the SMF under test over locally configured user plane security policy.

Pre-Conditions:

Test environment with AMF and UDM may be simulated.

Both UDM and SMF under test are configured with UP security policy, and the UP security policies are different.

There is no Session Management Subscription data in SMF.

Execution Steps

1)	The tester triggers PDU session establishment procedure by sending Nsmf_PDUSession_CreateSMContext Request message to the SMF.

2)	The SMF under test retrieves the Session Management Subscription data using Nudm_SDM_Get service from UDM, where the Session Management Subscription data includes the user plane security policy stored in UDM.

3)	The tester captures the Namf_Communication_N1N2MessageTransfer message sent from the SMF under test to the AMF.

Expected Results:

There is a Security Indication IE in the N2 SM information contained in the Namf_Communication_N1N2MessageTransfer message, which is the same with the UP security policy configured in the UDM.

Expected format of evidence:

Evidence suitable for the interface, e.g., Screenshot containing the operational results.

##### 4.2.2.1.2	TEID uniqueness

Requirement Name: TEID uniqueness.

Requirement Reference: TS 23.501[1], clause 5.8.2.3.1, TS 29.281 [5], clause 5.1, TS 23.060 [3], clause 14.6

Requirement Description:

"Allocation and release of CN Tunnel Info is performed when a new PDU Session is established or released. This functionality is supported either by SMF or UPF, based on operator's configuration on the SMF" as specified in TS 23.501[1], clause 5.8.2.3.1.

"Tunnel Endpoint Identifier (TEID): This field unambiguously identifies a tunnel endpoint in the receiving GTP-U protocol entity. The receiving end side of a GTP tunnel locally assigns the TEID value the transmitting side has to use" as specified in TS 29.281[5], clause 5.1.

"The TEID is a unique identifier within one IP address of a logical node." as specified in TS 23.060 [3], clause 14.6.

Threat References: TR 33.926 [4], clause J.2.2.2, Failure to assign unique TEID for a session.

TEST CASE:

Test Name: TC_TEID_ID_UNIQUENESS_SMF

Purpose:

Verify that the TEID generated by SMF under test for each new GTP tunnel is unique per PDU session.

Pre-Conditions:

Test environment is set up with a UPF, which may be real or simulated. The tester is able to trace traffic between the SMF under test and the UPF. The SMF under test is configured to generate the TEIDs.

Execution Step

1)	The tester intercepts the traffic between the UPF and the SMF under test.

2)	The tester triggers the maximum number of concurrent N4 session establishment requests that the SMF under test can handle.

3)	The tester captures the N4 session establishment requests sent from the SMF under test to the UPF and verifies that the F-TEID created in each generated request is unique.

Expected Results:

The F-TEID set in each different N4 session establishment request is unique.

Expected format of evidence:

Files containing the triggered GTP messages (e.g. pcap trace).

##### 4.2.2.1.3	Security functional requirements on the SMF checking UP security policy

Requirement Name: UP security policy check.

Requirement Reference: TS 33.501 [8], clause 6.6.1

Requirement Description:

"The SMF shall verify that the UE's UP security policy received from the target ng-eNB/gNB is the same as the UE's UP security policy that the SMF has locally stored. If there is a mismatch, the SMF shall send its locally stored UE's UP security policy of the corresponding PDU sessions to the target gNB. This UP security policy information, if included by the SMF, is delivered to the target ng-eNB/gNB in the Path-Switch Acknowledge message. The SMF shall log capabilities for this  event and may take additional measures, such as raising an alarm. "

Threat References: TR 33.926 [4], clause J.2.2.4, Unchecked UP security policy.

TEST CASE:

Test Name: TC_UP_SECURITY_POLICY _SMF

Purpose:

Verify that the SMF checks the UP security policy that is sent by the ng-eNB/gNB during handover.

Pre-Conditions:

The SMF under test is preconfigured with a UE UP security policy.

Execution

1. The tester sends the Nsmf_PDUSession_SMContextUpate Request message to the SMF under test. A UE UP security policy different than the one preconfigured at the SMF under test is included in the Request message.

2. The tester captures the Nsmf_PDUSession_SMContextUpdate Response message sent from the SMF under test.

Expected Results:

The preconfigured UE security policy is contained in the ‘n2SmInf’ IE in the captured Response message.

Expected format of evidence:

Files containing the triggered GTP messages (e.g. pcap trace).

##### 4.2.2.1.4	Charging ID Uniqueness

Requirement Name: Charing ID uniqueness.

Requirement Reference: TS 32.255 [6], clause 5.1.2

Requirement Description: :

"-	The SMF shall support PDU session charging using service based interface.

-	The SMF shall collect charging information per PDU session for UEs served under 3GPP access and non-3GPP access.

- Every PDU session shall be assigned a unique identity number for billing purposes per PLMN. (i.e. the Charging Id). "

Threat Reference: TR 33.926 [4], clause J.2.2.3, "Failure to assign unique Charging ID for a session"

TEST CASE:

Test Name: TC_CHARGING_ID_UNIQUENESS_SMF

Purpose:

Verify that the charging ID generated by the SMF for each PDU session is unique.

Pre-Conditions:

Test environment is set up with a Charging Function (CHF), which may be real or simulated, and the SMF under test. The tester is able to capture the traffic between the SMF under test and the CHF.

Execution Step

1)	The tester intercepts the traffic between the SMF under test and the CHF.

2)	The tester triggers the establishment of the maximum number of concurrent PDU sessions that the SMF under test can handle.

3)	The tester captures each Charging Data Request [initial] sent from the SMF under test to the CHF, and verifies the charging ID contained in the ‘PDU Session Charging Information’ IE in each Charging Data Request [initial] is unique.

Expected Results:

The charging ID in each Charging Data Request [initial] is unique.

Expected format of evidence:

Files containing the Charging Data Request [initial] messages (e.g. pcap trace).

### 4.2.3	Technical Baseline

#### 4.2.3.1	Introduction

The present clause provides baseline technical requirements.

#### 4.2.3.2	Protecting data and information

##### 4.2.3.2.1	Protecting data and information – general

There are no SMF-specific additions to clause 4.2.3.2.1 of TS 33.117 [2].

##### 4.2.3.2.2	Protecting data and information – unauthorized viewing

There are no SMF-specific additions to clause 4.2.3.2.2 of TS 33.117 [2].

##### 4.2.3.2.3	Protecting data and information in storage

There are no SMF-specific additions to clause 4.2.3.2.3 of TS 33.117 [2].

##### 4.2.3.2.4	Protecting data and information in transfer

There are no SMF-specific additions to clause 4.2.3.2.4 of TS 33.117 [2].

##### 4.2.3.2.5	Logging access to personal data

There are no SMF-specific additions to clause 4.2.3.2.5 of TS 33.117 [2].

#### 4.2.3.3	Protecting availability and integrity

There are no SMF-specific additions to clause 4.2.3.3 of TS 33.117 [2].

#### 4.2.3.4	Authentication and authorization

There are no SMF-specific additions to clause 4.2.3.4 of TS 33.117 [2].

#### 4.2.3.5	Protecting sessions

There are no SMF-specific additions to clause 4.2.3.5 of TS 33.117 [2].

#### 4.2.3.6	Logging

There are no SMF-specific additions to clause 4.2.3.6 of TS 33.117 [2].

### 4.2.4	Operating Systems

There are no SMF-specific additions to clause 4.2.4 of TS 33.117 [2].

### 4.2.5	Web Servers

There are no SMF-specific additions to clause 4.2.5 of TS 33.117 [2]

### 4.2.6	Network Devices

There are no SMF-specific additions to clause 4.2.6 of TS 33.117 [2].

### 4.2.7	Void

## 4.3	SMF-specific adaptations of hardening requirements and related test cases

### 4.3.1	Introduction

The present clause contains SMF-specific adaptations of hardening requirements and related test cases.

### 4.3.2	Technical baseline

There are no SMF-specific additions to clause 4.3.2 of TS 33.117 [2].

### 4.3.3	Operating systems

There are no SMF-specific additions to clause 4.3.3 of TS 33.117 [2].

### 4.3.4	Web servers

There are no SMF-specific additions to clause 4.3.4 of TS 33.117 [2].

### 4.3.5	Network devices

There are no SMF-specific additions to clause 4.3.5 of TS 33.117 [2].

### 4.3.6	Other SMF-specific adaptations of hardening requirements and related test cases

There are no SMF-specific additions to clause 4.3.6 of TS 33.117 [2].

## 4.4	Network functions in service-based architecture

There are no SMF-specific additions to clause 4.4 of TS 33.117 [2].

Annex A (informative):
Change history

| Change history |
| --- |
| Date | Meeting | TDoc | CR | Rev | Cat | Subject/Comment | New version |
| 2019-09 | SA#85 |  |  |  |  | Change control version | 16.0.0 |
| 2019-10 |  |  |  |  |  | EditHelp review | 16.0.1 |
| 2019-12 | SA#86 | SP-191138 | 0003 | - | F | Adding missing abbreviations | 16.1.0 |
| 2019-12 | SA#86 | SP-191138 | 0004 | 1 | F | Corrections for clean-up and alignment | 16.1.0 |