3GPP TSG-SA3 LI Meeting #07 	Tdoc (S3_LI_168

San Diego, USA, 12 – 14 November 2002

| CR-Form-v7 |
| --- |
| CHANGE REQUEST |
| ( | 33.108 | CR | CRNum | ( rev | - | ( Current version: | 5.1.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | New requirement on interworking |
| --- | --- |
| Source: ( | Nokia |
| Work item code: ( | Security |  | Date: ( | 01/11/2002 |
| Category: ( | B |  | Release: ( | Rel-6 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) |
| Reason for change: ( | This is a Rel-6 CR. Normally, operators have to support the LI functionality in order to be able offer commercial PS domain services to the customers. An operator may wish to build a PS domain network with SGSNs from different vendors. 3GPP decided not to define stage 3 spec for interception and X-interfaces. Therefore, the requirement to mandate the interworking of SGSNs manufactured by different vendors by far was never addressed. This significantly restricts the free competition on the market, because operators have to incorporate into existing networks only such SGSNs, which are compliant with the some proprietary stage 3 spec of the X2 and X3 interfaces. Therefore, interoperability problems of LI nature have negative implications on building competitive commercial systems. It is proposed to enhance the LI specs by an new requirement. This requirement will give the operators an opportunity to build a truly multi-vendor commercial UMTS networks. In order to support the new requirement the following matter should be addressed. De facto, two ways of coding the Correlation number are actually in use. One offers to compose the parameter by combining the Charging ID with the GGSN ID. Another one makes the parameter from PDP ID, MCC/MNC and DF ID. It is proposed to assign different ASN.1 tags to those different compositions. Hence, once LEMF receives the parameter, it would know which way has been used by the DF/MF. This change in ASN.1 module would require to increment the version value of the IRI-Parameters. |
| Summary of change: ( | It is proposed to enhance the LI specs by an new requirement. This requirement will give the operators an opportunity to build a truly multi-vendor commercial UMTS networks. Besides, it is proposed to assign different ASN.1 tags to different ways of coding the Correlation number parameter. Hence, once LEMF receives the parameter, it would know which way has been used by the DF/MF. This change in ASN.1 module would require to increment the version value of the IRI-Parameters. |
| Consequences if ( not approved: | Operators will be restricted in their freedom to select new SGSN for incorporation into their network. |
| Clauses affected: ( | 4.3; B.3 |
|  | Y | N |  |  |
| Other specs ( | x |  | Other core specifications ( | TS 33.106 |
| Affected: |  | X | Test specifications |  |
|  |  | x | O&M Specifications |  |
| Other comments: ( | Related Tdoc is S3_LI_167 |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at http://www.3gpp.org/specs/CR.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://ftp.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2001-03 contains the specifications resulting from the March 2001 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

## 4.3	Functional requirements

A lawful authorization shall describe the kind of information (Intercept Related Information (IRI) only, or IRI with Content of Communication (CC)) that is required by this LEA, the interception subject, the start and stop time of LI, and the addresses of the LEAs for delivery of CC and/or IRI and further information.

A single interception subject may be the subject of interception by different LEAs. It shall be possible strictly to separate these interception measures.

If two targets are communicating with each other, each target is dealt with separately.

Handover solutions shall provide for the interworking of intercepting network elements manufactured by different vendors.

IRI-Parameters		::= SEQUENCE

{

hi2DomainId				[0]	OBJECT IDENTIFIER,  -- 3GPP HI2 domain

iRIversion				[23] ENUMERATED

{

…,

version3(3)

-- the sending entity shall include version3 when the implementation

-- complies with Rel-6 TS 33.108 starting from version 6.1.0 onwards

} OPTIONAL,

-- if not present, it means version 1 is handled. Therefore, starting

-- from version2 onwards, inclusion of the iRIversion is mandatory

lawfulInterceptionIdentifier	[1] LawfulInterceptionIdentifier,

-- This identifier is associated to the target.

timeStamp				[3] TimeStamp,

-- date and time of the event triggering the report.)

initiator 				[4] ENUMERATED

{

not-Available		(0),

originating-Target	(1),

-- in case of GPRS, this indicates that the PDP context activation

-- or deactivation is MS requested

terminating-Target	(2),

-- in case of GPRS, this indicates that the PDP context activation or

-- deactivation is network initiated

...

} OPTIONAL,

locationOfTheTarget		[8] Location OPTIONAL,

-- location of the target subscriber

partyInformation 		[9] SET SIZE (1..10) OF PartyInformation OPTIONAL,

-- This parameter provides the concerned party, the identiy(ies) of the party

--)and all the information provided by the party.

serviceCenterAddress	[13] PartyInformation OPTIONAL,

-- e.g. in case of SMS message this parameter provides the address of  the relevant

-- server within the calling (if server is originating) or called (if server is

-- terminating) party address parameters

sMS						[14] SMS-report OPTIONAL,

-- this parameter provides the SMS content and associated information

national-Parameters		[16] National-Parameters OPTIONAL,

gPRSCorrelationNumber	[18] GPRSCorrelationNumber OPTIONAL,

gPRSevent 				[20] GPRSEvent OPTIONAL,

-- This information is used to provide particular action of the target

-- such as attach/detach

sgsnAddress 			[21] DataNodeAddress OPTIONAL,

gPRSOperationErrorCode 	[22] GPRSOperationErrorCode OPTIONAL,

ggsnAddress 			[24] DataNodeAddress OPTIONAL,

qOS						[25] UmtsQos OPTIONAL,

networkIdentifier		[26] Network-Identifier OPTIONAL,

sMSOriginatingAddress 	[27] DataNodeAddress OPTIONAL,

sMSTerminatingAddress 	[28] DataNodeAddress OPTIONAL,

iMSevent				[29] IMSEvent OPTIONAL,

sIPMessage				[30] OCTET STRING  OPTIONAL,

servingSGSN-number		[31] OCTET STRING (SIZE (1..20))	OPTIONAL,

servingSGSN-address		[32] OCTET STRING (SIZE (5..17)) 	OPTIONAL,

-- Octets are coded according to 3GPP TS 23.003 [25]

...

}

GPRSCorrelationNumber ::= CHOICE

{

ChragingIdGgsnId	[1]	OCTET STRING (SIZE(8..20))

-- as in subclause ‘Definition of ULIC header version 0’

PdpIdMccMncDfId		[2] OCTET STRING (SIZE(8..20))

-- four octets of PDP ID followed by Operator ID (MCC and MNC),

-- and followed by one octet of DF ID

...

}

# Comments

Document numbers are allocated by the Working Group Secretary.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least three digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/ .
The list is also included in a MS Excel file included in the zip file containing the CR cover sheet template.

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. correction).

Enter the number of each clause which contains changes.

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.

# Text boxes

*** Next Modification ****

*** Next Modification ****