3GPP TSG-SA3 LI Meeting #09 	Tdoc S3LI03_059r1

Vienna, Austria, 20 – 22 May 2003

Respective CR to 3GPP TS 33.108 is given in S3LI03_040

CR from TC LI on Data Link Establishment and Sending part for ROSE operation

ETSI/TC LI#02	02litd029r2

Benalmadena, 4-6 March 2003

| ETSI TC-LI | Document | TS101671CR042r2 |
| --- | --- | --- |
| CHANGE REQUEST | CR status: |  |
|  | TS 101 671 | CR | 042r2 | Current Version: | 2.5.1 |  |
|  |  |  |  | Affected version of the standard ( |
| SEC-LI specification number ( |  | ( CR number as allocated by chair |
| For submission to: | TC-LI#02 | for approval | X | strategic |  | editorial |  |  |
| list expected approval meeting # here ( | for information |  | non-strategic |  |  |  |  |
| Source: | ALCATEL – AQSACOM | Date: | 6th March 2003 |
| Subject: | Data Link Establishment and Sending part for ROSE operation |
| Work item: | RTS/SEC-003017 |
| Category: | F Correction | X |  |
|  | A Corresponds to a correction in an earlier release |  |  |
| (only one category | B Addition of feature |  |  |
| shall be marked | C Functional modification of feature |  |  |
| with an X) | D Editorial modification |  |  |
| Reason for change: | TS101671 sections C.1.2.3 (Data Link Management) and C.1.2.1 (Sending part) related to ROSE operations can be considered as confusing. That CR gives a rewording for clarification of that ambiguity with more accuracy. When separation between those both parts becomes more clear the TS 101671 makes clear the data link establishment shall be intitiated either by MF or by LEMF. That CR doesn’t intend to restrict the behavior to only one side inititiation and therefore, for backwards compatibility reasons, proposes that both currently allowed options are maintained. |
| Clauses affected: | Annex C.1.2.1, C.1.2.3 and C.1.2.3.1 |
| Other specs | ES 201 671 v2.1.1 | x | ( List of CRs: | Similar change |
| affected: |  |  | ( List of CRs: |  |
| The version number |  |  | ( List of CRs: |  |
| should be included |  |  | ( List of CRs: |  |
|  |  |  | ( List of CRs: |  |
| Other comments: |  |

### C.1.2.1	Sending part

To request the sending of data to a peer entity, the LI_Application provides the ASE_HI, the address of the peer entity, the nature of the data and the data.

On receiving a request of the LI_Application:

if the data link toward the peer entity address is active, the ASE_HI, from the nature of the data provided, encapsulates this data in the relevant RO-Invoke operation.

if the data link toward the peer entity address is not active, the ASE_HI  reports the data link unavailabability to LI_Application.

Note :	Until the data link is established by the LI_Application according to C.1.2.3.1, the request of the LI_Application cannot be successfully processed by ASE_HI.
.

*********** NEXT MODIFICATION *********

### C.1.2.3	Data link management

This function is used to establish or release a data link between two peer LI_Applications entities (MF and LEMF).

#### C.1.2.3.1	Data link establishment

Depending on a per destination address configuration data, the data link establishment may be required either by the LEMF LI_Application or by the MF LI_Application.

To request the establishment of a data link toward a peer entity, the LI_Application provides, among others, the destination address of the peer entity (implicitly, this address defined the protocol layers immediately under the ASE_HI: TCP/IP, X25, …). On receipt of this request, the ASE_HI request the establishment of the data link with respect of the rules of the under layers protocol.

# Comments

Document numbers are allocated by the Working Group Secretary.