3GPP TSG-SA3 LI Meeting #09                                                        Tdoc S3LI03_066

Vienna, Austria, 20 – 22 May 2003

Discussion paper from ETSI TC LI about the introduction of the CS domain clause into 3GPP TS 33.108

ETSI TC LI meeting #02, Benalmadena, 4-6 March, TD061

| Source: | ALCATEL S.A. |
| --- | --- |
| Title: | S3LI03_005r2 checking |
| Date: | March, 4th 2003 |
| Notice: | This document is not to be made publicly available |
| Document for: | Decision: |  |
|  | Discussion: |  |
|  | Meeting Report: |  |
|  | Liaison: | X |
|  | Information: | X |
| Contact details: | Eric.meilleray@alcatel.fr |  |  |

# Introduction

Liaison’s report on 3GPP S3 LI meetings (see 02litd036r2) concludes S3LI03_005r2 has to be checked by TC LI for backward compatibility to ETSI ES 201671.

The intent of this TD is to present that checking outcome.

# Checking outcome

It must previously be noted S3LI03_004r2 hasn’t been sent with the LS. That TD would have been interesting as it contains a table that maps differences between 33.108 and TS 101671.

The present TD is therefore the result of the checking between TS 101671 v2.5.0 on the one hand and S3LI03_005r2 plus S3LI03_004’s table on the other hand.

Main differences :

TS101671 Annex D.3  ---> not reported in 33.108 :

This section describes the HI Management operations.

It should be reported for backward compatibility.

It is necessary to comply with the normative annex related to ROSE (see section A.1.2.3 in 33.108 (C.1.2.3 in 101671))

Let's note this section is also necessary for PS HI2 when using ROSE.

TS101671 section A.3.3/A.3.4/A.3.5 ---> not reported into 33.108 :

The Table A.3.3 lists some “parameters which may be contained in the IRI” and these parameters are included into S3LI03_005r2’s ASN.1 description.

It should then be reported.

The other part of those sections could be reported if necessary.

TS101671 Annex D.6  ---> not reported in 33.108 :

In S3LI005r2’s Table 5.7 it is stated that for  User-to-user signalling 1,2,3 : “Optionally, ETSI’s HI3 interface for UUS may be maintained for backwards compatibility reasons”

For that reason the TS101671 Annex D.6 should be reported into 33.108 as it contains related ROSE operations.

TS101671 section A.4.4 ---> not reported in 33.108 :

This section deals with failure of CC link and with HI3 CS fault reporting.

Those sections may be reported.

TS101671 Annex D.4  ---> not reported in 33.108 :

This annex deal with HI1 operation notifications and with alarms notification.

Sending-of-HI1-Notification operation should be reported for backward compatibility.

Decision could be different for alarms.

Minor differences :

TS101671 section 10&11&12 ---> Already in 33.108 according to S3LI03_004 :

(Performance / Quality / Security requirements)

Checking shows they are reported in Chapter 6 (Packet data domain) only.

Those sections should remain common to both CS and PS.

TS101671 section A.4.1 ---> section 5.3.1 in 33.108 :

In S3LI005r2’s section 5.3.1 it is stated : "CC will be delivered as described in Annex H". It is probably a typo as annex H only deals with the transportation of CC related info.

TS101671 Annex A ---> not reported in 33.108 according to S3LI03_004 :

Probably it is a mistake in Table as this normative annex is still reported into 33.108 in tne current Annex C.

TS101671 Annex D, D.1  ---> not reported in 33.108 according to S3LI03_004 :

Probably it is a mistake  in Table as this normative annex is still reported into 33.108 in tne current Annex B.

# Comments

Document numbers are allocated by the Working Group Secretary.