3GPP TSG SA WG3 #17 LI Meeting	Tdoc S3LI05_044

Sophia Antipolis, France, 05 – 07 April 2005

Title: 		Correlation of CC & IRI for IMS interception

Source:	Siemens

Document for: 	Discussion & Information

Contact:	mailto:Bernhard.spalt@siemens.com

# Introduction

Correlation of IRI and CC was for further study in TS 33.108 and not fixed.

We discussed this topic in the least meetings and this document should point to a soltion.

According the following Figure usually two PDP contexts are established for a ‘SIP communication’ one for signaling and one for content / bearer. With our current recommendation in the standards also two correlation numbers (CR) are generated. Two keep the current solution within SGSN and GGSN also two correlation numbers in the CSCF’s are necessary. For this the ASN.1 tree in TS 33.108 had to be adapted and additional explanations in TS 33.107 and TS 33.108 are necessary.

# Conclusion and proposal

Tdoc 045 is the relevant CR for TS 33.107

Tdoc 046 is the relevant CR for TS 33.108

Are also CR’s for Rel. 6 necessary???

# Text boxes

IRI

With CR1 & CR2

IRI 1

With CR1

CC2

With CR2

HI3

HI2

MF HI3

DF3

IRI

With CR1 & CR2

IRI 2

With CR2

CC 1

With CR1

LEMF

MF HI2

DF2

SGSN

GGSN

CSCF

-

P

CSCF

-

S

Visited /Home Network