3GPP TSG-SA3 LI Meeting #17	Tdoc S3LI05_051r2

Sophia Antipolis, France, 5 – 7 April 2005

Source:	Nokia

Title:	Comments on CR to 33.107 (S3LI05_041)

Agenda item:	I-WLAN, 33.107

Document for:	DISCUSSION / APPROVAL

Introduction:

This paper collects comments on ambiguous parts in S3LI05_041 and offers modifications.

- Table 2 contains many similar IEs, which do not have clear type definitions (Tunnel address of observed party, WLAN UE remote address and Remote address assigned to WLAN UE; Session termination reason and Tunnel disconnect cause). I added comments to all ambiguous IEs. Just point the cursor to read them

- Table 2: it is not clear PDG or AAA Server must generate the I-WLAN specific correlation number. It is not clear if we need to deliver it to another node and how. I added clarification that PDG must do that, which is highlighted.

- Table 2: failure reasons: as discussed in Barcelona, in order to make these informative the text should be more specific. I believe "authentication failure", or other similar reason, which is related to subscription could be informative. Given, that such reason is available at all at ICE. I added text, which is highlighted.

- Table 2: what is "WLAN Location Name"?

- In all tables under 9.4 ambiguous IEs were highlighted in gray color. Once we clarify them in Table 2, the either the highlight or the IE should be removed.

- Text in 9.4.1 and 9.4.2 and respective tables are ambiguous on the matter which node is responsible for IRI.

- Observed target IP address and WLAN ID are not defined in Table 2, but are used in 9.4.5.

Proposal:

*** FIRST CHANGE ********

## 9.3	Provision of Intercept Related Information

Figure 25 shows the transfer of intercept related information to the DF2. If an event for / from a mobile subscriber occurs, the PDG, or the AAA Server sends the relevant data to the DF2.

Figure 25: Provision of Intercept Related Information

### 9.3.1	X2-interface

The following information needs to be transferred from the PDG or the AAA server to the DF2 in order to allow a DF2 to perform its functionality:

-	target identity (IMSI, NAI, or MSISDN, if available);

-	events and associated parameters as defined in section 9.3.2 may be provided;

-	the target location (if available);

-	Correlation number (for PDG only);

-	Quality of Service (QoS) identifier (if available).

The IRI should be sent to DF2 using a reliable transport mechanism.

### 9.3.2	3GPP WLAN Interworking LI Events and Event Information

The following events are applicable to AAA Server:

-	I-WLAN Access Initiation;

-	I-WLAN Access Termination;

-	I-WLAN Tunnel Establishment;

-	I-WLAN Tunnel Disconnect;

-	Start of Intercept with I-WLAN Communication Active;

The following events are applicable to the PDG:

-	I-WLAN Tunnel Establishment;

-	I-WLAN Tunnel Disconnect;

-	Start of Intercept with I-WLAN Communication Active.

A set of possible fields as shown below is used to generate the events. Information associated with the events are transmitted from the PDG or AAA server to DF2.

Note – some of these parameters apply to the PDG and some apply to the AAA server.  Parameters sent from the PDG or AAA server is dependent on what is available at the network element.

Table 2: Information Elementsfor Packet Data Event Records

Observed MSISDN MSISDN of the target subscriber (monitored subscriber). PDG and AAA Server.

Observed NAI NAI of the target subscriber (monitored subscriber). AAA Server only. In most cases at PDG NAI will be encrypted, and therefore cannot be used.

Observed IMSI IMSI of the target subscriber (monitored subscriber). AAA Server only.

Event type Description which type of event is delivered: I-WLAN Access Initiation, I-WLAN Access Termination, I-WLAN Tunnel Establishment, I-WLAN Tunnel Disconnect, Start of Intercept with I-WLAN Communication Active. PDG and AAA Server.

Event date Date of the event generation in the PDG or the AAA server. PDG and AAA Server.

Event time Time of the event generation in the PDG or the AAA server. Timestamp shall be generated relative to the PDG or AAA server internal clock. PDG and AAA Server.

WLAN UE Local IP address of observed party (see TS 23.008) The WLAN UE Local IP Address field, specified in 3GPP TS 23.234 [62], represents the IPv4/IPv6 address of the WLAN UE in the WLAN AN. It is an address used to deliver the packet to a WLAN UE in a WLAN AN.Note that this address might be dynamic. PDG only.

WLAN UE MAC address The WLAN MAC address of the target subscriber. Note that this address might be dynamic. AAA Server only.

WLAN UE Remote IP Address(see TS 23.008) The WLAN UE Remote IP Address field, specified in 3GPP TS 23.234 [62], represents the IPv4/IPv6 address of the WLAN UE in the network which the WLAN UE is accessing. It is an address used in the data packet encapsulated by the WLAN UE-initiated tunnel and is the source address used by applications in the WLAN UE. PDG only

WLAN Access Point Name The W-APN of the access point. AAA Server. (see 8.2.1.3 in 24.234 for PDG).

WLAN Operator Name The name of the WLAN operator name serving the target subscriber. AAA Server only.

WLAN Location Name The name of the location of the WLAN serving the target subscriber (e.g. string like "coffee shop" or "airport", ect.). AAA Server only.

WLAN Location Information Location Information regarding the WLAN as provided in RADIUS or DIAMETER signalling exchanged with the AAA server. AAA Server only.

I-WLAN Correlation Number The correlation number genarted by PDG and used to correlate CC and IRI. PDG only. AAA Server?

Network Element Identifier Unique identifier for the element reporting the ICE. PDG and AAA Server.

Initiator The initiator of the request either the network or the UE. PDG and AAA Server.

NAS IPv4/IPv6 address The IPv4 or IPv6 address of the NAS in the WLAN. AAA Server only.

Visited PLMN Identity Identity of the visited PLMN to which the user is terminating their WLAN tunnels or through which the user is establishing their WLAN tunnels. AAA Server only.

Session Alive Time The amount of time in seconds during which the target subscriber can be registered for WLAN access. AAA Server only.

Failed access reason Provides the only reason for why a WLAN access attempt failed (“authentication failure”). AAA Server only.

Session termination reason Provides a reason for why a WLAN access session is terminated (UE or network). AAA Server only.

Failed tunnel establishment reason Provides one of the reasons for why a WLAN tunnel establishment failed (either “Authentication failed” or “Authorization failed”). PDG and AAA Server.

Tunnel disconnect cause Provides a reason for why the WLAN tunnel is disconnected. FFS.

*** NEXT CHANGE – ADD NEW CLAUSE 9.4********

## 9.4	Structure of I-WLAN Events

### 9.4.1	I-WLAN Access Initiation

For I-WLAN Access Initiation, a I-WLAN Access Initiation-event is generated. When a WLAN Access Accept is generated from the mobile to servicing PDG this event is generated. These fields will be delivered by AAA Server to the DF2 if available:Table 1. I-WLAN Access Initiation - AAA Server

Observed MSISDN

Observed IMSI

Observed NAI

Event Type

Event Time

Event Date

Network Element Identifier

WLAN Operator Name

WLAN Location Name

WLAN Location Information

NAS IP/IPv6 Address

Visited PLMN ID

Session Alive Time

Failed Access reason

### 9.4.2	I-WLAN Access Termination

For WLAN Access Termination or the immediate purging of a user from a WLAN access, a WLAN access termination-event is generated. These fields will be delivered by AAA Server to the DF2 if available:

Table 2. I-WLAN Access Termination - AAA Server

Observed MSISDN

Observed IMSI

Observed NAI

Event Type

Event Time

Event Date

Network Element Identifier

WLAN Operator Name

WLAN Location Name

WLAN Location Information

NAS IP/IPv6 Address

Session Termination reason

### 9.4.3	I-WLAN Tunnel Establishment

For I-WLAN Tunnel Establishment, a I-WLAN tunnel establishment-event is generated. When a WLAN tunnel establishment is generated from the mobile to PDG this event is generated. These fields will be delivered to the DF2 if available:

Table 3. I-WLAN Tunnel Establishment - PDG

Observed MSISDN

FFS

FFS

Event Type

Event Time

Event Date

Correlation number

WLAN UE Local IP address

WLAN UE Remote IP address

FFS

Network Element Identifier

Failed tunnel establishment reason

EDITOR’s NOTE:  The inclusion of Tunnel Type and Location Information parameters from the PDG require further study. QoS not currently supported for WLAN Interworking.

Table 4. I-WLAN Tunnel Establisment - AAA Server

Observed MSISDN

Observed IMSI

Observed NAI

Event Type

Event Time

Event Date

FFS

WLAN Access Point Name

Network Element Identifier

Visited PLMN ID

Failed tunnel establishment reason

EDITOR’s NOTE:  The inclusion of Tunnel Type and Location Information parameters from the AAA server require further study.  QoS not currently supported for WLAN Interworking.

### 9.4.4	I-WLAN Tunnel Disconnect

At I-WLAN Tunnel Disconnect, a I-WLAN tunnel disconnect event is generated. These fields will be delivered to the DF2 if available:

Table 5. I-WLAN Tunnel Disconnect - PDG

Observed MSISDN

FFS

FFS

Event Type

Event Time

Event Date

Correlation number

WLAN UE Local IP address

WLAN UE Remote IP address

FFS

Network Element Identifier

FFS

Initiator (optional)

EDITOR’s NOTE:  The inclusion of the Location Information parameter from the PDG requires further study.

Table 6. I-WLAN Tunnel Disconnect - AAA Server

Observed MSISDN

Observed IMSI

Observed NAI

Event Type

Event Time

Event Date

FFS

WLAN Access Point Name

Network Element Identifier

FFS

Initiator (optional)

EDITOR’s NOTE:  The inclusion of the Location Information parameter from the AAA server requires further study.

### 9.4.5	Start of Intercept with I-WLAN Communication Active (check stage 2 spec and find that PDG keeps necessary parameters associations in memory)

This event will be generated if interception for a target is started and if the target has one or more active I-WLAN Access sessions or one or more I-WLAN Tunnels established. These fields will be delivered to the DF2 if available:

Table 7. Start of Intercept with I-WLAN Communication Active - PDG

Observed MSISDN

FFS

FFS

Event Type

Event Time

Event Date

Correlation Number

WLAN UE Local IP address

WLAN UE Remote IP address

FFS

Network Element Identifier

EDITOR’s NOTE:  The inclusion of Tunnel Type and Location Information parameters from the PDG require further study. QoS not currently supported for WLAN Interworking.

Table 8. Start of Intercept with I-WLAN Communication Active - AAA Server

Observed MSISDN

Observed IMSI

Observed NAI

Event Type

Event Time

Event Date

FFS

WLAN Access Point Name

Network Element Identifier

WLAN Operator Name

WLAN Location Name

WLAN Location Information

NAS IP/IPv6 address

Visited PLMN ID

EDITOR’s NOTE:  The inclusion of Tunnel Type parameter from the PDG require further study.

# Comments

Document numbers are allocated by the Working Group Secretary.

I belive it should read ‘elements’, and nor ‘events’.

This depends on the outcome of IMSI-in-PDG discussion.

What kind of address is implied? IP? Other? Is this UE address? These must be specified.

How different is this from “Tunnel address of observed party” or from “Remote address assigned to WLAN UE”? MAC address is available only to a network element, which is in the same LAN as UE. Therefore, in most cases neitrher PDG, nor AAA server can have UE’s MAC address. This should be clarified.

What does location mean here?

As discussed in Barcelona, in oder to make this informative the text should be more specific.

As discussed in Barcelona, in oder to make this informative the text should be more specific. Looks like this is the same as ‘Initiator’.

As discussed in Barcelona, in oder to make this informative the text should be more specific.

How different is this from “session termination reason”?

How AAA Server would know PDG generated correlation number?

How different is this from “Tunnel disconnect cause”?

This is not defined in Table 2. How different is it from “Tunnel address of observed party”, “WLAN UE remote address”, “Remote address assigned to WLAN UE”?

This is not defined in Table 2. How different is it from “WLAN Access Point Name” and “WLAN Operator Name”?